## Slide 1: Addition of Subscription Information for Selecting a Specific Network
NTT DOCOMO
S2-133304
TSG SA WG2 #99
Xiamen, China, 23-27 September 2013

## Slide 2: Introduction
LAPI (Low Access Priority Indicator)
  SA2 agreed CRs (S2-132262 and S2-132263) to use LAPI for selecting a specific MME.
  Effective only for UEs compliant to Release 10 or later version of specifications, which supports LAPI.
UE
MME
Specific S/PGW
eNB
Specific
MME
S/PGW
Attach Request
An eNodeB/RNC may select a specific MME/SGSN on the basis of its pre-configured information if a UE sets LAPI in RRC.
LAPI

## Slide 3: Introduction (cont’d)
However, existing UEs which do not support LAPI have no way to select a specific network.
So many existing UEs have been already in widespread use, but will be required to support the same function.
This paper shows the proposal of addition of subscription information for network selection regardless of LAPI implementation of UEs.
 | Rel-9 or former | Rel-10 or later
LAPI supported | (No UEs) | LAPI
LAPI unsuppoted | NO WAY | (LAPI implementation)
Current Problem!

## Slide 4: Proposal: Addition of subscription information for network selection
UE
HSS
MME
Specific S/PGW
eNB
Specific
MME
S/PGW
0. Attach Request
1. ULR/ULA
The Subscription Data in ULA contains information to use a specific network.
2. Reroute command
(NAS, information to use a specific network)
3. Initial UE Message
-> Perform an Attach procedure again to a specific MME

## Slide 5: Proposal: Addition of subscription information for network selection (cont’d)
Alternatives of information to use a specific network are as follows;
Alt.1: Add new bit to show a subscription state
  0: Without subscription to use a specific network
  1: With subscription to use a specific network
Alt.2: Add LAPI as a subscription state
  0: Without LAPI (Normal User) -> Without subscription
  1: With LAPI (Low Priority User) -> With subscription
  # “LAPI” used in this case is different from that of UE’s.

## Slide 6: Conclusion
We have a strong requirement of using a specific network even for LAPI-unsupported UEs.
See relevant CRs we prepared.