## Slide 1: SID on NTN Store and Forward – Rel19
Stawros Orkopoulos, Nokia

## Slide 2: Motivation and Methodology
For NTN Release 19 the support of the Store & Forward (S&F) functionality is required and implicit the support of gNB on-board architecture for the Satellite.
This SID is based on the SA1 NTN Rel19 phase 3 SI [1].
As part of this analysis, the relevant NTN Rel19 architecture and protocol stacks will be taken into account [2].
In a first step, all documented use cases will be reviewed from security perspective with the aim to derive the corresponding key-issues. Thereafter, in a second step, solutions should be developed per key-issue.

## Slide 3: Architecture and Functional Mapping
Separation in transparent and regenerative satellite-based architecture.
For the transparent satellite architecture, there is no radio network mapped to (hosted by) the satellite. The radio network layer (RNL) is between the UE and the (ground) gNB. The assumption is, there is no S&F support.
For the regenerative satellite architecture, the following architecture deployment scenarios can be considered:
AS#1: satellite gNB on board UE <-Service-link (Uu-I/F)-> Satellite (gNB on board) <-Feeder-link-> NTN GW <-NG-I/F-> CoreNetwork
AS#2: satellite gNB-DU on board UE <-Service-link (Uu-I/F)-> Satellite (gNB on board) <-inter-SAT-I/F-> Satellite (gNB on board) <-Feeder-link-> NTN GW <-NG-I/F-> CoreNetwork

## Slide 4: Use Cases
UC#1: Use case on store and forward – MO
UC#2: Use case on store and forward - MT
UC#3: Use case on store and forward - Inter-satellite
UC#4: Use case on data transfer for IoT devices in remote areas
UC#5: Use case on Temporary LAN using Satellite Access
UC#6: Use case on Information Exchange between Ships at sea
UC#7: Use case on the support of UE-satellite-UE phone call
UC#8: Use case for enabling multiple communication services between UEs
UC#9: Use case on usage of satellite connectivity for collection of information to aid terrestrial network planning
UC#10: Use case on vehicle fleet management in the desert
UC#11: Use case on service differentiation for UEs via satellite access
UC#12: Use case on UAVs using satellite access
UC#13: Use case on Enhanced Positioning Service using Satellite Access
UC#14: Use case on service continuity for UE-to-UE communication between satellites
UC#15: Use case on service continuity for UE-to-UE communication in case of mobility between satellite and terrestrial network
UC#16: Use case on store and forward – emergency report
Basic use cases
Basic use case
From security point of view, all use cases can be merged into a few basic use cases.
Ergo, only the basic use cases are used for the analysis.

## Slide 5: Store and Forward
In the Store and Forward scenario, either the Feeder-link or the Service-link is missing.
In the Store and Forward scenario w/ inter-SAT communication, the Inter-Satellite communication is available.

## Slide 6: Protocol Stack (overview)
User Plane Protocol Stack (Regenerative Satellite)
User Plane Protocol Stack (Regenerative Inter-Satellite)
Control Plane Protocol Stack (Regenerative Inter-Satellite)
PDCPsec
NDS/IPsec
Clear-text
Control Plane Protocol Stack (Regenerative Satellite)

## Slide 7: The following working assumptions will be considered:
[WA#1]: There is no terrestrial network available, i.e., the UE will be authenticated and authorized via the NTN.
[WA#2]: In the “S&F satellite” mode of operation, the Feeder link is available while the service link is not (Step B), or the Service link is available while the Feeder link is not (Step A).
[WA#3]: The legacy UE (IoT) does not know anything about NTN S&F functionality or other new features. The introduction of the NTN S&F is not impacting the operation of a legacy UE.
[WA#4]: After successful UE registration, the NAS security context is remaining valid.
[WA#5]: After successful RRC idle state the AS security context will retain.
[WA#6]: In the “normal/default” mode of operation, both, the Feeder link, and the Service link are available.
Mode | AS context… | NAS context…
“normal/default” | Setup | Setup
“S&F satellite” | Setup @ UE mobility | Setup @ SAT mobility

## Slide 8: Proposal
It is proposed to run a Study on the Security for NTN Store and Forward function as part of 3GPP Release 19. For more details please refer to [3] and [4].

## Slide 9: References
[1] 3GPP TR 22.865, Study on Satellite Access – Phase 3, Release 19
[2] 3GPP TR 38.821, Solutions for NR to support non-terrestrial networks (NTN), Release 16
[3] S3-233551, Discussion on NTN Store and Forward
[4] S3ah-230002, SID on Study for Security of NTN Store and Forward

## Slide 10: Abbreviations
NTN Non-terrestrial Network
S&F Store and Forward

## Slide 11
Thank You!