## Slide 1: S3ah-230036 Security management service
Minpeng Qi
CMCC

## Slide 2: Security management aspects
For an operator, typically, security management includes key management, certificate management, security hardening
Usual implementation follows: configuration of NF management account credentials, issuing certificates for device authentication, applying port filtering rules for firewalls, etc.
These aspects are still applicable for SBA

## Slide 3: Enhanced Intrusion detection analysis
Service-Based Architecture (SBA) introduces some new security management requirements
  SBA introduces more threat-vectors from other compromised NFs (VNFs or CNFs)
  SBA raises security policy management requirement for authorization
Enhancements required in the mechanisms for intrusion detection analysis
  Compromised NFs can increase the attack surface towards other NFs
  Increased virtualization of 5GC add to potential attack vectors due to possible vulnerabilities in the virtualization environment
  Therefore, security protection and detection capabilities of NF need to be strengthened

## Slide 4: Enhanced Intrusion detection analysis …
SA3 has defined SCAS which helps guarantee NF security by means of testing and verification of NF security
  However, this is done during development phase and does not assist in detecting compromised NFs in the live operator’s network
Security devices like gateways and firewalls deployed at the perimeter/borders of the network focus on traffic detection
  Such devices don’t provide inputs for detection of attacks on NFs like brute-force attacks, abnormal signaling, etc.
Due to such limitations in existing mechanisms, built-in attack detection feature should be developed in 5G network
  Requires enhancements in security related information collected by NFs

## Slide 5: Example for enhanced intrusion detection
NRF
OAM
IDS
Security Device
NF4
NF5
NF6
NF1
NF2
NF3
Warning: A lot of signaling from NF1 to NF6
2.Illegal access attempt from NF1!
NRF
OAM
IDS
Security Device
NF4
NF5
NF6
NF1
NF2
NF3
Warning: A lot of signaling from NF1 to NF6
2.Illegal access attempt from NF1!
3. Send to OAM

## Slide 6: Security analysis and access control of internal traffic
Compromised NFs from the same host can illegally access other NFs
VMs may also be subject to illegal access from other VMs deployed other part of NFs
  If public and private clouds are used, a compromised NF in public cloud can also be used to attack NFs on the private cloud
VLAN separation within the resource pool cannot mitigate such abnormal access
Based on security policy, NFs can collect more information about received traffic and report it to security management analysis service

## Slide 7: Security configuration enrolment/update
NRF needs to get security visit policy configuration about NF service provider when or after its registration
Such policy configuration should be updated if related NF consumer or provider is compromised.
Such policy configuration should be updated if compromised NF consumer or provider are fixed.

## Slide 8: Example for security configuration update
NRF
OAM
IDS
Security Device
NF4
NF5
NF6
NF1
NF2
NF3
NRF
OAM
IDS
Security Device
NF4
NF5
NF6
NF1
NF2
NF3
0.NF1 is detected as compromised
1.Send security configuration update command
Authorization profile:
{
Permit:
NF1->NF6, NF2->NF4/5/6,…
Forbidden:
}
Authorization profile:
{
Permit:
NF2->NF4/5/6,…
Forbidden:
NF1->All
}
Authorization profile:
{
Permit:
NF1->NF6, NF2->NF4/5/6,…
Forbidden:
}
Authorization profile:
{
Permit:
NF2->NF4/5/6,…
Forbidden:
NF1->All
}
1.Send security configuration update command
2.NF1 is restored from attacking

## Slide 9: Security configuration baseline check
After NF is installed, security hardening should be made according to the security configuration baseline
Also, such hardening should be checked periodically
Security management system should regularly and automatically verify the security baseline of NF, trying to discover and repair the exposed surface of NF in a timely manner
There are gaps between security management requirements and current security management mechanisms
In order to improve 5G network security management capabilities, it is necessary to study the concepts, uses cases, requirements and possible ways of security management under service based management architecture with deep analysis on the 5G network architecture and business requirements

## Slide 10: Study proposal
Proposal to study the concepts, use cases, requirements and possible solutions of security management under service based management architecture, including:
  Identify new security management service or capabilities for the SBMA architecture
  Potential requirements for the identified use cases
  Possible solutions to fulfil such requirements if needed