## Slide 1: Study to enable URSP rules to securely identify applications
Lenovo
3GPP TSG-SA3 Meeting #107-e S3-221070
e-meeting, 16 - 20 May 2022

## Slide 2: Problem
Operators can use the URSP rules to configure UEs to steer the traffic of specific applications based on the policy of operators.
For example, consider the following scenario:
    An operator has created an application which enables access to operator-hosted streaming services via a certain network slice X.
    The identity of this application is “com.operator.streaming-app”
    The operator configures UEs (with URSP rules) to send the traffic of application with identity “com.operator.streaming-app” over the network slice X.
However, the application identity is not a secure identifier and can be misused:
  The user may download another application (not the application created by the operator), which presents the same application identity “com.operator.streaming-app”.
  This is possible because the application identity is defined during the application development and can be any string chosen by the developer.

## Slide 3: Problem
Official app-stores typically check the identity of applications and make sure that the same identity cannot be present in more than one application.
   However, applications in a UE can be sideloaded (e.g., transferred directly via USB or Bluetooth), or can be downloaded from several app-stores.
Therefore, it is possible for a UE to have an application with identity “com.operator.streaming-app”, which is different from the application created by the operator.
   In this case, the UE would send the traffic of this application over the network slice X (based on the URSP rules), although this is not intention of the operator. So, the URSP rules are misused.
To address the above issue, a solution is needed which would enable a URSP rule to securely identify the application for which the URSP rule should be applied.

## Slide 4: Objective
Updated SID proposal now with single objective:
Identify enhancements that enable a URSP rule to securely identify the application for which the URSP rule should be applied.