## Slide 1: Discussion summary of CVD paper: A TELCO ODYSSEY 5G SUCI-CRACKER AND SCTP-HIJACKER
SA3 Vice-Chair (Rajavelsamy R)

## Slide 2: Outline
Contents
  CVD Paper details
  Meeting details
  Discussion summary

## Slide 3: CVD Details
Paper details:
  From: Pedro Cabrera, organization Ethon Shield
  Topic: 5G SUCI-CRACKER
  Details: The response to the authentication request allows to know if there is a relationship between the IMSI privacy identity in the 4G network (used to obtain the authentication vectors) and the SUCI identifier of a subscriber in the 5G network.
  Related Specs: TS 33.501
  Date detected: 2022-02-01
  Threat: Loss of subscriber anonymity, which may allow a potential attacker to identify and locate subscribers in 5G networks where Subscriber Concealed Identifier is enabled.

## Slide 4: Meeting details
Meeting happened on: 07 February 2023
Participants:
  3GPP CVD panel:
    Suresh Nair, Minpeng Qi, Rajavelsamy R, Alf Zugenmaier, Mirko Cano Soveri
  Authors:
    Pedro Cabrera Camara, Miguel Gallego
Scope of the meeting
  Requested the authors to the present their paper, to understand the details on the assumptions and test environment to assess the criticality and feasibility of the attack.

## Slide 5: Discussion summary
Discussion on: SUCI-Cracker and SCTP-Hijacker attacks
SUCI-Cracking
  Belongs to "IMSI probing" attack category, not a new threat
  Feasibility of the threat to be tested in real deployments
    Vulnerability has been tested only in the test environment with programmable SIM cards
    SQN and lifetime of the AV: Need to check how this could affect the success of the attack
  Takeaway: Threat detailed may not be effective and SUCI (SUPI encryption) is not cracked, that’s a wrong tile. Knowing an IMSI, the attacker checks the UE being authenticated is really the UE under consideration.
SCTP-Hijacker
  Tested in a real deployment that does not support interface protection between gNB and AMF (i.e. NDS/IP not deployed).
  If interface security (NDS/IP) is activated then threat detailed in the paper can be mitigated
  Takeaway: Network needs to adopt the 3GPP recommendations on interface security