## Slide 1
China Telecom
Discussion on application login
via IMS

## Slide 2
  Background: SMS based login solutions
Numerous Apps use PIN based solutions to facilitate login experience enhancements compared with password based login. It is generally composed of following steps:
Click on the SMS login button;
Enter the mobile phone number；
Click the PIN get button；
Wait for the SMS；
Extract the PIN from the SMS；
Enter the PIN；
Click the login button;
The main idea is that the application server can verify whether the application client can use this phone number as an identity.

## Slide 3
  Typical procedures and drawbacks
Two main drawbacks:
1. Non-efficient and error-prone: multiple manual interventions are needed, e.g., get the SMS, read the code, fill in the code, click the login button.
2. Insecure: The SMS is easy to be hijacked which will cause spoof attack.

## Slide 4
  Example: One-click login solutions
To facilitate the user experience, there are several one-click login solutions as shown in the left.
The user only needs to click the button “use current phone number”, then the user can login directly without any manual intervention needed. It can achieve the same result that the application server can verify whether the application client can use this phone number as an identity.

## Slide 5
Typical procedures and drawbacks in current one-click login
Two main drawbacks:
In case the user has two SIM cards, e.g., one for voice and SMS while the other for data usage, he/she can only use the number related to the second SIM cards since the step 1~3 can only be performed in data network.
Since there is no standard work, each operator has to implement customized SDK which will cause complexities to both Apps and operators.

## Slide 6
  Proposals
A general idea is:
The user open the app client;
User only needs to select the phone number used to access the service and click the login button (if the user has only one phone number, the selection is not necessary);
The client, the server and the core network will exchange messages without any manual intervention. The exchanges should be conveyed in some well protected messages instead of SMS, e.g., SIP messages in IMS.
The app server verifier whether the app client can use the phone number as the identity to sign in the service. If the verification succeeds, the server will accept the login request.
The reason why we consider IMS is to address the two SIM cards scenario since both cards will have IMS access and can be selected by users.
Therefore, it is proposed to study how to accomplish the above procedures, especially step 3, in 3GPP to enhance security and efficiency in existing mechanisms.
Note：the solution should consider the existing implementation on the APP server side to facilitate the deployment of such feature.

## Slide 7
THANKS