## Slide 1
Clarification of Test Cases in TS 33.117
Representing the opinion of GSMA NESAS Group | November 2023
NESAS
Network Equipment Security Assurance Scheme
3GPP TSG SA3 Meeting #113 Chicago, US, 6 -10 November 2023
S3-23xxxx
Discussion Paper
Source to WG:: Deutsche Telekom T-Mobile US Telecom Italia Mobile Telus China Mobile Ericsson Huawei Nokia ZTE BSI (Germany) MITRE Corporation
Non-3GPP: NCC Group member atsec contributors:

## Slide 2: Problem Statement
All NESAS Test Labs must comply with the requirements of ISO 27025, the first line of which states: “This document specifies the general requirements for the competence, impartiality and consistent operation of laboratories.”
As ISO 17025 may not be familiar to all SA3 members, some of the requirements have been reproduced on the next few slides.
As can be seen, there is a very strong and consistent theme of ensuring objectivity, impartiality, repeatability, reproducibility, consistency and validity.
To be able to demonstrate to the Accreditation Body that a Test Lab is meeting these requirements, there must be appropriate wording in all documentation such that any interpretation or subjectivity is removed, or at least minimised as far as possible.
Where there is text that could be interpreted differently by different Test Labs, it becomes extremely difficult to be certain that all tests are being conducted such that the results would be the same, regardless of which Test Lab did the work.
Some of the text within the generic SCAS TS 33.117 is not at a level where this objectivity and impartiality can be guaranteed. Some of these are identified in these slides and some suggestions are made as to how these might be improved to remove subjectivity.
It appears that TS 33.117 has been written by different authors, as the depth and language used varied throughout. Some sections, therefore, are more closely aligned to ISO 17025 than others.

## Slide 3: ISO 17025 Definitions
impartiality
presence of objectivity
Note 1 to entry: Objectivity means that conflicts of interest do not exist, or are resolved so as not to adversely influence subsequent activities of the laboratory.
Note 2 to entry: Other terms that are useful in conveying the element of impartiality include “freedom from conflict of interests”, “freedom from bias”, “lack of prejudice”, “neutrality”, “fairness”, “open-mindedness”, “even-handedness”, “detachment”, “balance”.
verification
provision of objective evidence that a given item fulfils specified requirements
validation
verification where the specified requirements are adequate for an intended use

## Slide 4: ISO 17025 Requirements
General requirements
4.1 Impartiality
4.1.1 Laboratory activities shall be undertaken impartially and structured and managed so as to safeguard impartiality.
The laboratory shall document its procedures to the extent necessary to ensure the consistent application of its laboratory activities and the validity of the results.
5.6 The laboratory shall have personnel who… identify deviations… from the procedures for performing laboratory activities;
7.2.1.5 The laboratory shall verify that it can properly perform methods before introducing them by ensuring that it can achieve the required performance.
7.2.2.3 The performance characteristics of validated methods, as assessed for the intended use, shall be relevant to the customers' needs and consistent with specified requirements.
NOTE Performance characteristics can include, but are not limited to measurement uncertainty of the results, selectivity of the method, linearity, repeatability or reproducibility and bias.

## Slide 5: ISO 17025 Requirements
General requirements
7.2.2.4 The laboratory shall retain the following records of validation:
a) the validation procedure used;
b) specification of the requirements;
c) determination of the performance characteristics of the method;
d) results obtained;
e) a statement on the validity of the method, detailing its fitness for the intended use.
In short, testing must be carried out in a way that is objective and repeatable, such that anyone doing the test given the same environment, should obtain the same results.
To achieve this, the testing procedure must be written to allow different testers to follow the same steps and see the same evidence.
There can be no room for interpretation or doubt.

## Slide 6: 33.117 Issues
4.2.2.2.2 - Protection at the transport layer
Comment
The test case applies to SBI only, but is not explicitly stated.
Suggested change:
Explicitly state that the test is applicable to the SBI only..

## Slide 7: 33.117 Issues
4.2.3.2.4 - Protecting data and information in transfer
Pre-conditions
For protocols, for which 3GPP did not define a security profile, e.g. SSH, the tester shall base the tests on a widely recognised and publicly available security profile
“Widely recognised” is a subjective term.
Suggested change:
Providing better-defined terms or explicit sources to be used or not to be used, would be preferable.

## Slide 8: 33.117 Issues
4.2.3.3.2 - Boot from intended memory devices only
Execution Steps
The tester verifies that there is no possibility to access and modify the firmware of the network product without successful authentication
This expects the tester to prove a negative, which is extremely difficult. Changing the text to be more achievable is recommended.
Suggested change:
“The tester verifies that attempts to access and modify the firmware of the network product are permitted following successful authentication but prevented without prior successful authentication”

## Slide 9: 33.117 Issues
4.2.3.4.1.1 - System functions shall not be used without successful authentication and authorization
Execution Steps
The accredited evaluator's test lab is required to execute the following steps:
1. The tester verifies, based on his/her own experience, that the list is adequate.
This is subjective, what constitutes an "adequate list”?
Suggested change:
Define what is an "adequate list" or rewrite the clause..

## Slide 10: 33.117 Issues
4.2.3.4.3.1 - Password Structure
Comment
States "Absolute minimum length of 8 characters" (for a password), but then goes on to state "The network product shall use a default minimum length of 10 characters", which appears contradictory.
Suggested change:
Clarify whether the network product is required to support a password with a minimum length of 8 or 10 characters..

## Slide 11: 33.117 Issues
4.2.3.4.6.2 - Role-based access control
Pre-conditions
Documentation describing the role based access control system including details on which user roles are defined.
Just ‘describing’ the RBAC is weak.
Suggested change:
Documentation defining the role based access control system including details on which user roles are defined.

## Slide 12: 33.117 Issues
4.2.3.6.2 - Log transfer to centralized storage
Pre-conditions:
The manufacturer shall list the standard protocols which transfer security event logging data.
Execution steps
2. The tester checks whether the used transport protocol is secure protocol
The tester checks whether the used transport protocol for log file upload is a secure standard protocol.
The words in red are subjective terms.
Suggested change:
The text should be changed to remove subjectivity. If there are protocols that are/are not permitted to be used, these should be listed.

## Slide 13: 33.117 Issues
4.2.4.1.1.1 - Growing (dynamic) content shall not influence system functions.
Expected results:
“It is verified that the taken measures are sufficient so that system operation is not influenced by growing or dynamic content at any case.”
“sufficient” is not defined
Suggested change:
The text should be changed to remove subjectivity. Either define “sufficient” or reword the expected results to be objective.

## Slide 14: 33.117 Issues
4.2.4.1.1.2 - Processing of ICMPv4 and ICMPv6 packets #1
Pre-conditions:
“The tester knows whether the network product supports IPv4 and/or IPv6:
The tester needs to be told this information by the vendor.
Execution steps
“The tester sends samples of the applicable ICMP messages from the tester machine to the network product and verifies by appropriate means…”
This is subjective.
Suggested change:
“Vendor to provide documentation that details the use of ICMP for both IPv4 and IPv6”
Remove “…by appropriate means…” from that step

## Slide 15: 33.117 Issues
4.2.4.1.1.3 - Handling of IP options and extensions
Comment
This clause refers to IP packets with "unnecessary options", but do not define what is meant by "unnecessary options".
Suggested change:
Define what is meant by "unnecessary options".
Options for the IPv4 header were originally defined in RFC 791 “Internet Protocol”. It turned out since then that IPv4 Options are rarely usedin practice and that they can – if not filtered properly – impose a security risk. It is therefore recommended to treat IPv4 Options as defined in RFC 7126 “Recommendations on Filtering of IPv4 Packets Containing IPv4 Options”. It is suggested to reference RFC 7126, instead of using “unnecessary options”.

## Slide 16: 33.117 Issues
4.2.4.1.1.2 - Processing of ICMPv4 and ICMPv6 packets #2
The test itself seems weak.
Tests should be done to check that the messages are actually getting to the device from the tester, to eliminate the possibility that the network is dropping them, rather than the product.
Capturing the traffic to prove the message arrived and that the device did not respond would be stronger.

## Slide 17: 33.117 Issues
4.2.4.1.2.1 - There shall not be a privilege escalation method in interactive sessions (CLI or GUI) which allows a user to gain administrator/root privileges from another user account without re-authentication.
Execution steps
The tester logs into the network product and verifies that list "A" is accurate, based on his expert knowledge of the operating system(s) used in the network product, and operating system documentation.
This is subjective and there is no need to define the required gender of the tester.
Suggested change:
Either the required knowledge of the tester needs to be defined or these words should be removed such that the tester uses the documentation provided by the vendor.
Testers may be any gender and these documents must reflect that.

## Slide 18: 33.117 Issues
4.2.4.2.2 - System account identification
Pre-conditions
Unix is used on the MME.
The meaning of MME is undefined here. If It refers to a 4G Management Mobility Element specifically, then this test is probably in the wrong SCAS and should not be included in the General Catalogue SCAS.
Suggested change:
Clarify whether MME is applicable in this clause, if so define MME, or modify the clause to be applicable to generic Network Functions. Or move the test case to the specific SCAS for MME.
If the test case is moved, a comparable test case in the SCAS for AMF and/or SMF may be necessary.

## Slide 19: 33.117 Issues
4.2.5.3 - HTTP User sessions
Execution steps
The tester logs in repeatedly with different user IDs and a number of times with the same user ID in a row
This is subjective.
Suggested change:
The minimum number of times that this should be done must be specified.

## Slide 20: 33.117 Issues
4.2.6.2.1 - Packet filtering
Expected format of evidence
NA
This seems strange, as it would be expected that some form of evidence should be presented in the test report.
Suggested change:
Check and verify what format of evidence should be provided in the test report to the results of this test and add accordingly.

## Slide 21: 33.117 Issues
4.3.2.1- No unnecessary or insecure services / protocols
Execution steps
1b - Validation that all entries in the list are meaningful and reasonably necessary for the operation of the Network Product class.
2 - Identification of the network services and protocol handlers by means of capable tools or any other suitable testing means.
Both of these are subjective.
Suggested change:
Remove the subjectivity from the execution steps.

## Slide 22: 33.117 Issues
4.3.2.1- No unnecessary or insecure services / protocols
Expected format of evidence
The test results i.e. services existing or not existing in the MME.
Both of these are subjective.
Suggested change:
Clarify whether MME is applicable in this clause, if so define MME, or modify the clause to be applicable to generic Network Functions. Or move the test case to the specific SCAS for MME.
If the test case is moved, a comparable test case in the SCAS for AMF and/or SMF may be necessary.

## Slide 23: 33.117 Issues
4.3.2.3 - Unused software shall not be installed or shall be uninstalled
Execution steps
1b - Validation that all entries in the list of software / libraries and components are meaningful and reasonably necessary for the operation of the Network Product class.
2 - Identification of the software / libraries or components which are installed in the system using any suitable command line tools or any other suitable means of determination.
4 - Based on his/her experience, the tester will check for known default example files for software installed on the system.
All of these are subjective.
Suggested change:
Remove the subjectivity from the execution steps.
Remove reference to the gender of the tester.
Define which default example files the tester must look for and how this checking must be done.

## Slide 24: 33.117 Issues
4.3.2.4 - Unused functions of the network products' software and hardware shall be deactivated.
Purpose
To ensure that there is no unused hardware or software functions that are not deactivated in the network product which are not required for its operation or functionality.
Execution steps
Identification of the hardware and software functions which are installed in the system or might have been disabled using any suitable command line tools or any other suitable means of determination.
All of these are subjective.
Suggested change:
For clarity, replace the stated purpose with: “To ensure that all active hardware or software functions are explicitly required for operation or functionality of the network product”.
Remove subjectivity from the execution steps by providing explicit information.

## Slide 25: 33.117 Issues
4.3.2.5 - The network product shall not contain software and hardware components that are no longer supported by their vendor, producer or developer.
Purpose
To ensure that there is no unsupported software that is running in the network product which is not supported anymore and has reached its end-of-life or end-of-support.
Execution steps
The accredited evaluator's test lab is required to execute the following steps:
Identification of the hardware and software components, version information and the kind of support available for the software provided by the vendor, the producer, the developer or other contractual partner of the operator using any tool or any other suitable means of determination.
The tester should not be responsible for all of these actions.
Suggested change:
For clarity, replace the stated purpose with: “To ensure that all active software running in the network product has not reached either its end-of-life or end-of-support, and is still supported”
Rewrite the execution steps such that the tester is validating the vendor claims and how this ought to be done
Remove subjectivity from the execution steps by providing explicit information.

## Slide 26: 33.117 Issues
4.3.2.7 - Filesystem Authorization privileges
Purpose
Verify that only users that are authorized to modify files, data, directories or file systems have the necessary privileges to do so.
This seems a strange way to express what should be a negative requirement. It would be better expressed as suggested below.
Suggested change:
Change the Purpose clause text to: "Verify that users that are not authorised to modify files, data, directories or file systems do not have the privileges to do so".

## Slide 27: 33.117 Issues
4.3.3.1.2 - Minimized kernel network functions (TC_ IP_MULTICAST_HANDLING)
Purpose
In particular this test case verifies that packets with IP source or destination address belonging to the multicast IP ranges (224.0.0.0 through 239.255.255.255) are not handled by the network product.
The execution steps do not align to the stated purpose.
Pre-conditions
Network traffic analyser on the network product or an external traffic analyser directly connected to the network product is available
This is a pre-condition but the test execution steps do not make use of it
Execution steps
Verify that none of the network product's interfaces is running Multicast (e.g. typing command ip maddr or ifconfig on any Unix® based platform)
Examples are subjective and this requires a tester to have knowledge of all network products OS.
Suggested change:
Rewrite the test case so it is objective and meets the stated purpose

## Slide 28: 33.117 Issues
4.3.3.1.2 - Minimized kernel network functions
Execution steps
This clause covers 4 different test cases, each with a different "Test Name", "Purpose", "Procedure and Execution steps", "Expected results" and "Expected format of evidence".
This seems quite confusing for the reader. Could, each of these test be sub-divided into separate sections?
Suggested change:
Consider sub-dividing the 4 test cases presented in clause 4.3.3.1.2 into separate clauses..

## Slide 29: 33.117 Issues
4.3.3.1.3 - Syn Flood Prevention
Comment
The title of Section 4.3.3.1.3 is "No automatic launch of removable media" and the text for the requirement name states: "Requirement name: No automatic launch of removerable media".
This is grammatically incorrect and conveys a different meaning. And, confuses the object and subject of the clause. In this particular case, what is being automatically launched: the removable media or the Network Product?
What is presumably meant here is "No automatic launch from removable media"
The two statements have very different meanings.
Suggested change:
Check the meaning here and correct, if necessary..

## Slide 30: 33.117 Issues
4.3.3.1.4 - Syn Flood Prevention
Execution steps
The tester configures the tool to send a huge amount of TCP Syn packets against the Network Product (e.g. hping3 -i <waiting time between each packet> -S -p <TCP port> -c <Number of packets> <MME IP>)
The Network Product is still up and running normally, its services are still available and reachable, the memory is not exhausted, there is no crash
“A huge amount” is subjective.
How would a tester identify what is normal, which services should still be available and if the memory is exhausted (which is a subjective term)?
Suggested change:
Quantify these terms or reword the test case.

## Slide 31: 33.117 Issues
4.3.3.1.6 - External file system mount restrictions
Execution steps
The tester tries to gain privileged access to system by using a suitable privilege escalation method using the contents of the mounted file system and then confirms that privilege escalation doesn't happen.
Suggested change:
Define what is or is not a “suitable” method.

## Slide 32: 33.117 Issues
4.3.4.2 - No system privileges for web server.
Pre-condition
Recommended: an automatic assessment tool has been configured /script adapted in line with the Requirement Description.
Execution steps
Check that relevant system settings and configurations are correct to ensure fulfilment of the requirement.
Expected results
System settings have been found correctly set to ensure that no processes will run with system privileges.
Suggested change:
Define what is or is not to be used as an automatic assessment tool, what is “correct”, which system settings should be checked, and what does “correctly” means.

## Slide 33: 33.117 Issues
4.3.4.3 - Unused HTTP methods shall be deactivated.
Pre-condition
Recommended: an automatic assessment tool has been configured /script adapted in line with the Requirement Description.
Execution steps
Check that relevant system settings and configurations are correct to ensure fulfilment of the requirement.
Expected results
System settings and configurations have been found adequately set, in all Web components of the system, to ensure that unneeded HTTP methods are deactivated.
Suggested change:
Define what is or is not to be used as an automatic assessment tool, what is “correct”, which system settings/configurations should be checked, and what does “adequately” means.

## Slide 34: 33.117 Issues
4.3.4.4 - Any add-ons and components that are not required shall be deactivated.
Pre-condition
Recommended: an automatic assessment tool has been configured /script adapted in line with the Requirement Description.
Execution steps
Check that relevant system settings and configurations are correct to ensure fulfilment of the requirement.
Expected results
System settings and configurations have been found adequately set, in all Web components of the system, to ensure that unneeded HTTP methods are deactivated.
Suggested change:
Define what is or is not to be used as an automatic assessment tool, what is “correct”, which system settings/configurations should be checked, and what does “adequately” means.

## Slide 35: 33.117 Issues
4.3.4.5 - No compiler, interpreter, or shell via CGI or other server-side scripting.
Pre-condition
Recommended: an automatic assessment tool has been configured /script adapted in line with the Requirement Description.
Execution steps
Check that relevant system settings and configurations are correct to ensure fulfilment of the requirement.
Expected results
System settings and configurations have been found adequately set, in all Web components of the system, to ensure that unneeded HTTP methods are deactivated.
Suggested change:
Define what is or is not to be used as an automatic assessment tool, what is “correct”, which system settings/configurations should be checked, and what does “adequately” means.
As for other similar tests, these are repeating the requirement, rather than specifying the steps of the testing that is required for the test.

## Slide 36: 33.117 Issues
4.3.4.8 - Access rights for web server configuration Pre-condition
Recommended: an automatic assessment tool has been configured /script adapted in line with the Requirement Description.
Execution steps
Check the access rights settings for Web server system configuration files.
Check that relevant system settings and configurations are correct to ensure fulfilment of the requirement.
Expected results
Access rights for system configuration files are adequately set.
Suggested change:
Define what is or is not to be used as an automatic assessment tool, what is “relevant” and “correct”, which system configuration files should be checked, and what does “adequately” means.
As for other similar tests, these are repeating the requirement, rather than specifying the steps of the testing that is required for the test.

## Slide 37: 33.117 Issues
4.3.4.9 - Default content shall be removed.
Purpose
To verify that there is no default content on the web server, that is not needed for web server operation, since such default content can be useful for an attacker.
Pre-condition
Recommended: an automatic assessment tool has been configured /script adapted in line with the Requirement Description.
Execution steps
Check that all default content (examples, help files, documentation, aliases) that is provided with the standard installation of the web server has been removed.
Expected results
No default content (examples, help files, documentation, aliases, un-needed directories or manuals) has been found to remain on any Web server component.
Suggested change:
Change the Purpose text to: “To verify that any default content on the web server is explicitly needed for web server operation” for clarification.
Define what is or is not to be used as an automatic assessment tool. Define “default content”. The test doesn’t align to the purpose (i.e. default content is permitted for operation of the web server).
As for other similar tests, these are repeating the requirement, rather than specifying the steps of the testing that is required for the test.

## Slide 38: 33.117 Issues
4.3.4.10 - No directory listings / Directory Browsing.
Pre-condition
Recommended: an automatic assessment tool has been configured /script adapted in line with the Requirement Description.
Execution steps
Check that Directory listings (indexing) / "Directory browsing" has been deactivated in all Web server components.
Expected results
Evidence that Directory listing / Directory browsing has been deactivated in all Web server components.
Suggested change:
Define what is or is not to be used as an automatic assessment tool.
Define what needs to be checked and what are the expected settings.
As for other similar tests, these are repeating the requirement, rather than specifying the steps of the testing that is required for the test.

## Slide 39: 33.117 Issues
4.3.4.11 - Information about the web server in HTTP headers shall be minimized.
Pre-condition
Recommended: an automatic assessment tool has been configured /script adapted in line with the Requirement Description.
Execution steps
Check that HTTP headers do not include information on the version of the web server and the modules/add-ons used.
Expected results
Evidence that HTTP headers do not include information on the version of the web server and the modules/add-ons used
Suggested change:
Define what is or is not to be used as an automatic assessment tool.
As for other similar tests, these are repeating the requirement, rather than specifying the steps of the testing that is required for the test.

## Slide 40: 33.117 Issues
4.3.4.12 - Web server information in error pages shall be deleted.
Pre-condition
Recommended: an automatic assessment tool has been configured /script adapted in line with the Requirement Description.
Execution steps
Check that generated error pages and error messages do not include information about the web server.
Expected results
Evidence that generated error pages and error messages do not include information about the web server.
Suggested change:
Define what is or is not to be used as an automatic assessment tool. Which error message/pages are to be checked?
As for other similar tests, these are repeating the requirement, rather than specifying the steps of the testing that is required for the test.

## Slide 41: 33.117 Issues
4.3.4.13 - File type- or script-mappings that are not required shall be deleted.
Pre-condition
Recommended: an automatic assessment tool has been configured /script adapted in line with the Requirement Description.
Execution steps
Check that all file type- or script-mappings that are not required have been deleted.
Expected results
Evidence that all file type- or script-mappings, that are not required, have been deleted.
Suggested change:
Define what is or is not to be used as an automatic assessment tool. How would the tester know what “all” means, or which are required, or which have been deleted (as they will not be visible)?
As for other similar tests, these are repeating the requirement, rather than specifying the steps of the testing that is required for the test.

## Slide 42: 33.117 Issues
4.3.5.1 - Traffic Separation.
Pre-condition
NOTE: This test applies if the network product is meant to handle traffic from different network domains, e.g. both O&M and control plane traffic.
Execution steps
1. The tester checks whether the network product refuses traffic intended for one network domain on all interfaces meant for the other network domain, and vice versa.
Step 1 is to be performed for all pairs of different network domains.
Expected results
The two tests should be successful.
Suggested change:
The pre-condition should be amended to state that the vendor must provide this information for the tester.
Execution steps would benefit from more detail and defining what traffic should be used for testing (i.e. would ANY traffic be acceptable for this test?) Consider adding clarity by changing the wording to “The tester checks whether the network product passes traffic only to interfaces in the same domain and that it is dropped from all interfaces in other domains.”
Expected results should be reworded to state that traffic should not be passed to a domain from which it did not originate.

## Slide 43: 33.117 Issues
4.3.6.2 - No code execution or inclusion of external resources by JSON parsers.
Pre-condition
The tester should have access to an effective Web Application Security (WAS) test tool that allows to generate HTTP messages exploiting JSON parsers that do not prevent the above-mentioned scenarios of code execution and loading external resources.
Execution steps
Execution of available WAS test tools against the network product’s API endpoints via its Service Based Interfaces.
Suggested change:
“Effective” should be defined. Is there a particular way for the tools to be executed? How should they be configured?

## Slide 44: 33.117 Issues
4.3.6.3 - Validation of the unique key values in IEs.
Pre-condition
Test environment with network product under test. Rest of the network and network products may be simulated.
Execution steps
1) The test equipment sends requests with duplicate keys in message IE payload to the network product under test.
The test equipment sends valid requests to network product under test
Suggested change:
“IE” is not defined in the document.
The pre-conditions are vague. What does the “test environment” need to have or not have?
What is the “test equipment”? What “requests” should be sent?

## Slide 45: 33.117 Issues
4.3.6.4 - Validation of the IEs limits.
Pre-condition
Test environment with network product under test. Rest of the network and network products may be simulated.
Execution steps
1) The test equipment sends requests with out of bounds IEs towards the network product under test.
Suggested change:
“IE” is not defined in the document.
The pre-conditions are vague. What does the “test environment” need to have or not have?
What is the “test equipment”? What “requests” should be sent?

## Slide 46: 33.117 Issues
4.4.2 - Port scanning
Pre-condition
The port scanning tool that is used shall be capable to detect open ports on the relevant transport layer protocols.
Execution steps
Validation that all entries in the list of services are meaningful and reasonably necessary for the operation of the Network Product class.
Suggested change:
The tools to be used or not used are not defined. How should they be configured?
Define “meaningful”.
How necessary is “reasonably”?

## Slide 47: 33.117 Issues
4.4.3 - Vulnerability scanning
Pre-condition
The used vulnerability scanning tool shall be capable to detect known vulnerabilities on common services. The used vulnerability information shall be reasonably recent at the time of testing.
Execution steps
1. Execution of the suitable vulnerability scanning tool against all interfaces providing IP-based protocols of the Network Product.
Suggested change:
The tools to be used or not used are not defined. How should they be configured?
How recent is “reasonably”?

## Slide 48: 33.117 Issues
4.4.4 - Robustness and fuzz testing
Pre-condition
The robustness and fuzzing tools that are selected for this test shall utilize state-of-the-art technology …
Test labs shall acquire fuzz testing tools for those protocols where commercially feasible.
The accredited test lab is expected to have sufficient expertise to recognize the level of effectiveness of the available tools.
Execution steps
Execution of available effective fuzzing tools against the protocols available via interfaces providing IP-based protocols of the Network Product for an amount of time sufficient to be effective.
Execution of available effective robustness test tools against the protocols available via interfaces providing IP-based protocols of the Network Product for an amount of time sufficient to be effective.
The execution of tests shall run sufficient times.
Suggested change:
Remove the subjectivity (or as much as possible).