## Slide 1: CAPIF RNAA authorization methods and related interfaces
Nokia, Nokia Shanghai Bell

## Slide 2: Background
High level functional architecture for CAPIF supporting RNAA
Figure is ffs as per SA6; SA3 has not made decision on this
SA3 is utilizing the mechanisms specified in IETF RFC 6749.
  Authorization Code Flow
  Authorization Code Flow with PKCE (IETF RFC 7636)
  Enhanced version of Client Credentials Flow
Status
  Procedures for obtaining authorization from resource owner by API invoker from Authorization Function (CCF)
    For OAuth 2.0’s Authorization Code Flow procedure as specified in IETF RFC 6749 can be supported over CAPIF-1/1e. (see next slide)
    For client credentials flow the RFC states: The client can request an access token using only its client credentials (or other supported means of authentication) when the client is requesting access to the protected resources under its control, or those of another resource owner that have been previously arranged with the authorization server
Details are missing on CAPIF-8
  As per TS 33.122 (SA3), technical details of CAPIF-8 is out of scope in Rel-18.
  As per TS 23.222 (SA6), role of CAPIF-8 for RNAA is FFS and is out of scope of Rel-18.
  Figure as shown in 33.122 is misleading without explaining role of CAPIF.

## Slide 3: CAPIF RNAA and OAuth Auth Code Flow
CCF
API invoker
CAPIF-1/1e
CAPIF-1/1e
Authorization endpoint
Token endpoint
Information Flows | OAuth (RFC 6749) | CAPIF (TS 23.222, TS 33.122)
(A) – API invoker requesting Authorization Code for resource access via service API | Authorization Request from Client to Authorization Server. (Uses Authorization endpoint) | Supported by CCF (Authorization Function) over CAPIF-1/1e Use Authorization Request of OAuth
(B) – Resource Owner granting resource access | By implementation methods. Out of scope of RFC 6749. | Aligned with OAuth and a standardized method is out of scope of Rel.18
(C) – Authorization Code provided to API invoker by Authorization Function | Authorization Response from Authorization Server to Client (Uses Authorization endpoint) | Supported by CCF (Authorization Function) over CAPIF-1/1e Use Authorization Response of OAuth
(D) – API invoker request for Access Token with Auth Code | Access Token Request from Client to Authorization Server (Uses Token endpoint) | Supported by CCF (Authorization Function) over CAPIF-1/1e Use Access Token Request of OAuth
(E) – Authorization Function provides the Access Token to API invoker | Access Token Response from Authorization Server to Client (Uses Token endpoint) | Supported by CCF (Authorization Function) over CAPIF-1/1e Use Access Token Response of OAuth
OAuth’s Authorization Code Flow can be implemented over CAPIF-1/1e.

## Slide 4: CAPIF RNAA mapping to CAPIF-1/-8
CCF
API invoker
CAPIF-1/1e
CAPIF-1/1e
Authorization endpoint
Token endpoint
OAuth’s Authorization Code Flow can be implemented over CAPIF-1/1e.
CAPIF-8 can be considered purely for step B (user authentication) which supports interactions between Authorization Server and Resource Owner for User Authentication and obtaining permission from Resource Owner (ie end user granting access).
Steps A, B and C are so used for Authorization Code Flow over the Authorization Endpoint. They are not used for Client Credentials Flow.
Allowing the latter, potentially means further study.
CAPIF-8
ROC
End user interaction
UE

## Slide 5: Update proposal related to CAPIF-8
For this release, it is sufficient to provide a short clarification in 3GPP spec regarding RNAA/CAPIF-8
ROC represents the PLMN user or PLMN subscriber of the UE whose resources are exposed via AEF. ROC is deployed on the UE.
Different functional security models can be envisioned with ROC connecting to CCF
  API invoker can be part of the UE and located on the device
  API invoker can be independent from the UE, e.g. deployed by a third party, but still located on the device
  API invoker can be independent of the UE and located outside of the device (e.g. at the game server)
From security perspective, the API invoker is always the OAuth client. The authorization function is part of the CCF
CAPIF-8 is needed for authentication the ROC (user or subscriber of a UE) to the authorization function (CCF) before authorizing.
API invoker can only access the northbound API via CAPIF-2 after gaining access token subjected to authorization grant from ROC (CAPIF-1).
The detailed architecture for CAPIF-8 is out of scope of this release
The authentication step between API invoker and CCF is depending on the functional security model.
ROC
CAPIF-8

## Slide 6: Summary
Following proposals are submitted to SA3#113
  Relevant updates to TS 33.122 about CAPIF-8 (see CR)
  Inform SA6 about the update related to CAPIF-8 (can be part of a LS-reply)

## Slide 7: Thank You!