## Slide 1: Virtual Resource Isolation for Applications in 5G network
Jing Ping
Nokia

## Slide 2: Background and motivation
5G will be able to support extreme and diverse requirements for throughput, latency, availability, capacity. Security is another fundamental network requirement that needs to be optimized for each specific use case, especially for those uses cases where security becomes critical (e.g., V2X platooning, enterprise VPN or Electric grids).
Operator allocates 5G network resources to vertical/enterprise customers to support various use cases and applications, the resource can be isolated from networks or network resources used by other cellular customers.
Network slicing is a key feature and business driver for 5G, which enables enterprises and operators to address specific requirements of different market segments (e.g., industrial, smart cities, healthcare, automotive). The overall security architecture of 5G network is enhanced with new security features, available as well in network slices as logical networks created within the 5G network.
However, without proper isolation, a compromised or malicious low security profiled slice may impact a highly sensitive slice breaching isolation and/or access control, or Denial of Service (DoS) attacks on slices may be launched successfully if resources are shared by multiple slices, or services/resources and data of mission critical slices may be stolen by other vulnerable or malicious slices.
That may cause incompliance of security requirements of customer and regulation of vertical industry, hence loose confidence of the vertical customers and hinder the commercial deployment of network slice for new business chances.

## Slide 3: Expected resource allocation with proper isolation
Operator allocates 5G network resources to vertical/enterprise customers to support various use cases and applications, the resource can be isolated from networks or network resources used by other cellular customers.
The network resources can be isolated from logic network layer (e.g. network slice), a set of NFs/resource layer (e.g. network slice subnet, or network slice instance), virtualization layer (e.g. VNF, CNF), physical layer (e.g. physical server, RF).
Based on security requirement of the customers, security policies of operators, and regulations, etc., the resources may be fully or partial isolated or shared.

## Slide 4: Expected network resource selection and traffic routing with proper isolation
DU
PLMN - 1
UPF-1
SMF-1
UPF-21
SMF-2
AMF-1
S-NSSAI#21
UE#2
S-NSSAI#22
CU-CP RRC/PDCP-1
CU-UP-21
CU-UP-1
S-NSSAI#1
UE#1
AMF-2
CU-CP
RRC/PDCP-2
CU-UP-22
UPF-22
uRLLC
eMBB
mIoT
N2
N2
N3
N3
N3
NSSF
Resource isolation
uRLLC
mIoT
eMBB
Enterprise A
Enterprise B
UE camps on cell supporting specific slice(s).
gNB communicates to AMF supporting specific slices.
CP NFs in 5GC communicate with other NFs within specific slice(s).
Dedicated SMF may be selected for PDU session of specific slice(s)
Dedicated UPF may be selected for transmission of UP traffic of specific slice(s).
No communication/interaction between NFs which should be isolated from each other.

## Slide 5: Example of expected network slice isolation in deployment
A slice is fully isolated from other slices, from RAN to transport to CN, and from control plane (CP) to user plane (UP), dedicated resources are allocated to the slice, e.g. S-NSSAI#1
A slice is partially isolated from other slices, e.g. share DU and other CP NFs, but use dedicated UP related NFs, e.g. S-NSSAI#3
A slice shares all NFs with other slices, e.g. share DU, CU, CP and UP NFs, e.g. S-NSSAI#4 and 5
Another example as shown in right bottom is that slices may share some CP NFs while use other dedicated CP/UP NFs, but it’s possible to communicate between some CP NFs of different slices.

## Slide 6: Business Requirements (3GPP)
Traffic and services in one network slice shall have no impact on traffic and services in other network slices in the same network – see 6.1.2.2, TS 22.261
Based on operator policy, a 5G network shall provide suitable means to allow a trusted and authorized third-party to create and modify network slices used for the third-party with appropriate security policies (e.g. user data privacy handling, slices isolation, enhanced logging) – see 8.2, TS 22.261
Isolation between different AMFs was assumed in AMF reallocation study – see 4.3, TR 33.864
Slice isolation in virtualization layer was studied and requirement was proposed as “The system should manage slice isolation, security domains and trust domains” – see 5.10, TR 33.848

## Slide 7: Business Requirements (GSMA)
Isolation requirement from GSMA E2E Network Slicing Requirements (GSMA NG.135)
  Isolation in network slicing is a multi-faceted problem, articulated into three separate dimensions:
  (i) performance, ensuring that Service Level Specification (SLS) is always met on each NS (Network Slice) instance, regardless of workloads or faults from other running instances;
  (ii) security, ensuring that any type of intentional attack occurring in one NS instance have no impact on any other running instance;
  (iii) management, ensuring that each slice instance can be operated as a separate network partition, with an independent lifecycle management.
Isolation requirement from GSMA E2E Network Slicing Architecture (GSMA NG.127)
  Slice security isolation is a security feature, as it separates slice related data and activities of different customers. With the corresponding slice specific enforcements slice security isolation can prevent unauthorized access and modification to data, processes, services or functions. If the SLA includes slice security isolation.

## Slide 8: Threat and Risk Analysis
UE1
UE2
RAN1
RAN2
AMF1
SMF11
NEF1
UPF11
NSSF1
NRF1
PCF1
NWDAF1
SMF12
UPF12
UDM1
AMF2
SMF21
NEF2
UPF21
NSSF2
NRF2
PCF2
NWDAF2
UDM2
5GC
DN
App11
App12
App3
Public Safety
Vulnerable slice acquired/exploited by malicious consumer
Finance
A public facing NF in the vulnerable slice may be exploited and compromised
Without proper isolation, it may impact other more security sensitive slice
Without proper isolation, it may also launch attack towards mission critical slice

## Slide 9: Status quo – Network slice deployment scenario
Network and Network Slice Management Function (MnF) provides the management services (MnS) for network or network slice which includes RAN part, CN part and TN part to the Consumer. Network and NetworkSlice MnF consumes MnSs for RAN/CN SubNetwork or network slice subnet (NSS) produced by RAN/CN Domain MnFs and interface produced by TN Domain Manager.
RAN/CN Domain MnFs provides the MnSs for a RAN/CN SubNetwork or NSS and/or MnSs for RAN/CN NF(s). RAN/CN domain MnF may consume MnSs for RAN SubNetwork or NSS and MnSs for RAN NF.
Network and Network Slice MnF, RAN Domain MnF, CN Domain MnF, even RAN MnFs, CN MnFs, may be provided by different vendors.
Annex 8 of 3GPP TS 28.533: deployment scenario for management of a mobile network including network slicing

## Slide 10: Status quo – Slice requirement mapping
The GST parameters are used as input to ServiceProfile. The ServiceProfile is translated into the SliceProfile. In particular, the attributes captured in the ServiceProfile are mapped to TopSliceSubnetProfile attributes. Based on the TopSliceSubnetProfile attributes, the corresponding requirements for the dedicated domain specific network slice subnets are defined. For example, the CNSliceSubnetProfile attributes are used to carry 5GC domain requirements, the RANSliceSubnetProfile attributes are used to carry NG-RAN domain requirements, and the TN requirements are derived and provide input to the TN domain.
Some of the attributes in CNSliceSubnetProfile and RANSliceSubnetProfile parameters can be translated to configurable parameters related to network function behaviour to satisfy SLS of the service in the control plane. While other information (e.g., delay tolerance, deterministic communication support) in CNSliceSubnetProfile and RANSliceSubnetProfile are kept at OAM domain and is used to determine the overall behaviour of the network slice.
Annex L of 3GPP TS 28.541
GSMA GST

## Slide 11: Status quo – information model to support slice
Network Resource Model defined in 3GPP TS 28.541, including IM for:
network slice and service profile (6)
network slice subnet and slice profile (6)
network function (4, 5)
endpoint (for slice and NF) (4, 5, 6)

## Slide 12: Status quo – Solution #8 in TR 33.848: Slice isolation in both service and resource layer
6.9.2 Solution Details
It is proposed to first define a set of isolation principles for network design. The general 3 levels of isolation principles are listed as follows:
1) Isolation between slices: Network slices for critical sectors (e.g. energy sector, emergency services sector, critical manufacturing sector, etc.) should be isolated from general commercial network slices. This implies that all NFs in critical should be isolated from NFs in other ordinary slice or a particular set of NFs in critical slice should be isolated from other NFs.
…………………………………………………………
2) Isolation between network functions in the same slice: In a particular network slice, several NFs are more sensitive than others, e.g. UDM/AUSF/ARPF, etc. It may be needed to isolate these NFs from others even in the same network slice.
3)Isolation between network services in the same NF: It's general recommended to isolate sensitive services (e.g. LI service) in a NF from other services.
6.9.3 Evaluation
Parts of this solution require other groups to complete the standardization. ETSI NFV ISG is expected to involved and enhance the MANO functionality in order to support the new parameters in NSD, i.e. the umbrella group identifier and group isolation attributes.
The isolation of network functions is in the scope of 3GPP

## Slide 13: Gaps and problems
As described in previous slides, resource isolation is fundamental requirements on network slice for its commercial deployment.
Some specifications and solutions were developed in 3GPP to support network slice deployment and configuration. E.g. management services (including network resource model) and procedures defined in SA5 enables mapping slice SLA to attributes of network slice and network slice subnet, then further translating those attributes to slice related configuration parameters of NR and 5GC NFs. The MnSs and procedures also support to deploy and scale the NFs, either in physical device or cloudified infrastructure, to satisfy the slice requirements. Virtualized resource isolation for network slice was also discussed in 3GPP in previous release, ETSI NFV based solution was proposed in the study, which is available for “intra-slice” isolation.
However, the resource isolation between different slices cannot be enforced based on existing 3GPP specification. Concretely , operator may deploy several slices to support different business cases of vertical customers, and make plan to assign different business applications to corresponding slices, and isolate the slices based on security requirements from the customers, security policies of operators, regulations, and other non-security related criteria, etc. As isolation related information model is not supported in existing specification, the isolation plan cannot be mapped to attributes of network slice, network slice subnet, network function, or infrastructure requirements. Therefore, the domain management functions (e.g. RAN/CN NSSMF, RAN/CN NFMFs, from different vendors) cannot translate the isolation requirement to corresponding network and network function configuration. The resource may be still shared between slices expected to be isolated with each other, and the NFs of different slices may be able to communicated with each other even they’re expected to be separated. That can be exploited for attack on security sensitive slices, and cause losses on both network slice operator and their vertical customers.

## Slide 14: Objectives
Study how to enable verticals, operators and cloud service providers to address diverse requirements of different market segments for security and isolation, and to investigate the gaps in existing specification and collect potential solutions to enforce resource isolation for applications in 5G network.
Clarify resource isolation concept especially in security point of view.
Investigate the gaps of existing specification on network and virtualization resource isolation and protection for vertical applications.
Collect potential solutions to enforce resource isolation and correct resource selection for applications in 5G network, hence satisfy the security requirements of various business cases from different industries and improve compliance with industry regulatory and business requirements.