## Slide 1: 5G Security and topics of interest for SA3
Abstract: 5G, being not just a “better and faster” 4G, presents SA3 with the opportunity to improve 3GPP Security.
This contribution proposes topics of interest for upcoming SA3 Work on 5G Security. It is TCG TMS input to SA3#82.
3GPP TSG SA WG3 (Security) Meeting #82 S3-160039
1-5 February 2016, Dubrovnik, HR
Source: Interdigital
Document for: Discussion
Agenda Item: 8.6 - Other Study Areas

## Slide 2: 5G Capabilities to Drive 5G Security
5G networks will provide communication capabilities for new use cases and new industries, and for a multitude of devices and applications. Supporting not only voice and data communication as we know it today.
  orders of magnitude more entities
  different traffic models (UL comparable or exceeding DL)
    60 PB yearly Netflix traffic in the US. A single B887 engine generates 0.5 TB of data during an average flight
5G will drive new security requirements due to
  new business and trust models
  new service delivery models
  much more complicated and dynamic threat landscape
  greater than ever before concern for privacy
5G Security will be affected almost everywhere in the network
  evolution involves all parts of the network,
    core network and management systems
    protocol layers ranging from radio to applications

## Slide 3: Current 3GPP security constraints
Existing trust model does not capture the evolved business and technological capabilities of 5G. The trust model will have to be redrawn.
  this does not mean completely redesigning security
  it is crucial to identify any significant challenges while defining a new trust model.
Only minimum protection of subscription/UE identities, no authentication of ME (only subscription authentication)
HSS/HLR being a repository of identities and attributes
  will not scale to expected number of identities in 5G
Architectural limitations dictated by trust concentrated in the network.
  edge and terminals are considered to be untrusted
Security is binary
  either on or off without selective security per flow/service

## Slide 4: Opportunity Areas
  Identity management (SA3, ETSI NFV SEC, ITU-T)
  Changing trust models to ones with trust located at the edge and in terminals as well as in the core (SA3, TCG, ETSI MEC, ETSI NFV SEC)
  Privacy of data and identities (SA3, ETSI NFV SEC, TCG)
  Flexible and scalable security architecture (SA3, ETSI MEC, ETSI NFV SEC)
  Energy-efficient security (SA3, ETSI MEC, ETSI NFV SEC)
  Virtualization security (SA3, ETSI NFV SEC, ETSI MEC, TCG)
  Security assurance (SA3, ETSI NFV SEC, TCG)
  5G radio network security - on-demand security, low latency security (SA3)

## Slide 5: 5G Security - Core areas
Flexible and scalable security architecture
virtualization and dynamic configuration for 5G, promotes new dynamic and flexible security architecture
Security for RAN signaling could be located close to the access (e.g., virtualization) with a higher degree of independence to the user plane security, allowing more robust security (key distribution, key isolation, etc.)
5G radio network security
attack resistance of radio networks to threats such as Denial of Service from potentially misbehaving devices
adding mitigation measures to radio protocol design
utilize available trusted computing technologies
Virtualization security (ETSI NFV SEC)
network virtualization with high assurance of VNF isolation to simplify the handling of diverse security requirements in common infrastructure
Use existing trusted computing tools (TCG) and concepts for Virtualized Platform Integrity
  root of trust
  remote attestation
  device integrity monitoring
  secure storage
cloud-friendly data encryption (homomorphic encryption, allowing operations on encrypted data).
Identity management
5G open identity management architecture
billions of heterogeneous end-devices, sensors, network nodes with variable security capabilities, device attributes, and policies
allow enterprises with an existing IDM solution to reuse it for 5G access.
new ways to handle device/subscriber identities with network slicing, enabling different IDM solutions per slice
Energy-efficient security
most constrained, and battery-dependent devices with a long life time might be separated in specialized energy-efficient lightweight network slice
need to compare energy cost of encrypting one bit vs. transmitting one bit
Security assurance
deployment of heterogeneous hardware and software components creates greater need for security certification
security certification (either static or dynamic) needs to be communicated between entities to provide assurance in platform integrity
multi-layer security certification scheme is needed to efficiently create and traverse certification records