## Slide 1: Integrity protection for SBA over N32 (IPX)
NTT DOCOMO

## Slide 2: Problem with interim solutions
Network effects:
  Participant with lowest capabilities defines what everyone implements
  Update to more secure protocol very difficult to argue commercially
  no iterim solution, as that will become permanent

## Slide 3: Changing integrity protected values
There is a requirement for "e2e" integrity protection in conjunction with requirement for intermediaries to be able to verifiably modify the message.
Proposed solution
  The whole request receives one integrity check value
  Intermediaries simply attach a "diff" to requests and responses each with its own integrity check value
Advantage
  The SEPP doesn't need to understand the complete semantics of integrity protected fields

## Slide 4: Example: Transformation of SBA request in SEPP V
POST APIroot/nausf_auth/v1/ue_authentications HTTP/2 Accept: application/json Content-Type: application/json Host: HPLMN.com Content-Length: 100 { "UE-id": "maguro_suci", "Serving network name": "some_VPLMN", "access_type": "5G" }
SEPP V directs request to IPX provider 1.
SEPP V puts HTTP header and body into JSON elements
POST APIroot/IPX1/v1/nf_to_nf HTTP/2 Accept: application/json Content-Type: application/json Host: HPLMN.com Content-Length: 560 { "requesthistory": [ { "request": {"originator": "some_VPLMN_SEPPid", "request_line": { "method": "POST", "URI":"APIroot/nausf_auth/v1/ue_authentications", "protocol": "HTTP/2"}, "HTTP-headers": { "Accept": "application/json", "Content-Type": "application/json", "Host": "HPLMN.com", "Content-Length": "100"},
"HTTP-body": { "UE-id": "maguro_suci", "Serving network name": "some_VPLMN", "access_type": "5G" } }}]}

## Slide 5: Example: Integrity protection of request body in SEPP
{"originator": "some_VPLMN_SEPPid", "request_line": { "method": "POST", "URI":"APIroot/nausf_auth/v1/ue_authentications", "protocol": "HTTP/2"}, "HTTP-headers": { "Accept": "application/json", "Content-Type": "application/json", "Host": "HPLMN.com", "Content-Length": "100"},
"HTTP-body": { "UE-id": "maguro_suci", "Serving network name": "some_VPLMN", "access_type": "5G" } }
{ "requesthistory": [ { "request":
{ protectedHeader.protectedPayload.signature }
]}
Whereby the protectedHeader contains the algorithm and key Id,
The protectedPayload contains the JSON object depicted on the left,
The signature is e.g. a ECDSA signature or an HMAC.
Because JWS uses compact base64 serialization, the protected content is not shown here.
The protected payload can be deserialized and interpreted in the IPX.
SEPP integrity protects complete request element using JOSE/JWS (RFC 7515)

## Slide 6: Modification in IPX provider 1 – HTTP Header
IPX provider 1 terminates HTTP – can direct TCP connection to new host, in this case IPX2.
IPX provider 1 inserts an element into the requesthistory array that describes how to patch the original request
{ "UE-id": "maguro_suci", "Serving network name": "some_VPLMN", "access_type": "5G" }
Mediation: e.g. direct to IPX2, and terminate in HPLMN2
And become
{ "UE-id": "maguro_suci", "Serving network name": "some_VPLMN", "access_type": "5G", "new_element": "value1" }

## Slide 7: Example: IPX1 patching SBA request
Attaching the patch to the message:
{ "requesthistory": [ { "request": { protectedHeader.protectedPayload.signature }]}
Is changed by the IPX operator to
{ "requesthistory": [ { "request":
{ protectedHeader.protectedPayload.signature },
{ "json_patch":
{ protectedHeaderIPX1.protectedPayloadIPX1.signatureIPX1 }
]
}

## Slide 8: Protected Payload IPX1 – the first patch in the array
Using RFC 6902 to describe the modifications the IPX provider wants to perform. The patch assumes as the root for the patch the request element.
In the example:
{ "previous": <signature of previous request entry in requesthistory array>,
"next": <expected next originator>,
"originator": "IPX1",
"operations":
[ {"op": "replace", "path": "/HTTP-headers/Host", "value": "HPLMN2.com"},
{"op": "replace", "path": "/HTTP-headers/Content-Length", "value": "131"},
{"op": "add", "path": "/HTTP-body/new_element", "value": "value1"}]}
Further IPX providers will append to the "request history" array.
Previous is always filled in a json_patch element.
If next is known, it contains the id of originator, otherwise left empty. If next is filled, but no patch is required, that next originator needs to create a json_patch with empty operations.
Content length changes due to new element
This produces a linked list of patches rooted in the request element

## Slide 9: Example: IPX2 patching SBA request
IPX2 takes the integrity protected request
Applies first json_patch
If mediation is required, appends second JSON patch
{ "requesthistory": [ { "request": { protectedHeader.protectedPayload.signature }, { "json_patch": { protectedHeaderIPX1.protectedPayloadIPX1.signatureIPX1 } ] }
Is changed by the IPX operator to
{ "requesthistory": [ { "request": { protectedHeader.protectedPayload.signature }, { "json_patch": { protectedHeaderIPX1.protectedPayloadIPX1.signatureIPX1 }, { "json_patch": { protectedHeaderIPX2.protectedPayloadIPX2.signatureIPX2 } ] }

## Slide 10: Processing by SEPP H
Receives POST request
Checks all signatures
Takes request from requesthistory
Applies all patches in order
Recreates SBA request to forward NF in home network
SBA response is handled in the same way

## Slide 11: Proposed agreements
IPX providers use JSON-Patch mechanism to update SBA requests and responses on interconnect
SEPP encapsulates complete SBA requests and responses including request line and HTTP headers in JSON elements
SEPP integrity protects complete SBA request and responses
IPX providers integrity protect the JSON_Patch including originator and the linked list elements ("next", "previous") in the array
  Linked list is required to ensure correct order of application of patches even if an adversary tries to replace, delete or reorder patches.
A pCR will be produced if the idea is deemed acceptable