3GPP TSG-SA WG3 LI Meeting	Tdoc S3LI02_086

Orlando, Florida. 09 – 11 April 2002

| CR-Form-v4 |
| --- |
| CHANGE REQUEST |
| ( | 33.108 | CR | CRNum | ( rev | - | ( Current version: | 5.0.0 | ( |
| For HELP on using this form, see bottom of this page or look at the pop-up text over the ( symbols. |
| Proposed change affects: ( | (U)SIM |  | ME/UE |  | Radio Access Network |  | Core Network | x |
| Title: ( | Changes to 33.108 to add support for Serving System Reporting |
| Source: ( | Telcordia Technologies |
| Work item code: ( |  |  | Date: ( | 9 April 2002 |
| Category: ( | C |  | Release: ( | Rel-5 |
|  | Use one of the following categories: F (correction) A (corresponds to a correction in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: 2 (GSM Phase 2) R96 (Release 1996) R97 (Release 1997) R98 (Release 1998) R99 (Release 1999) REL-4 (Release 4) REL-5 (Release 5) |
| Reason for change: ( | Include enhancements and clarification to provide support for the reporting of a Serving System event from the HLR. |
| Summary of change: ( | Add changes to ASN.1 and an Annex to describe the mechanism to report the Serving System event from the HLR. |
| Consequences if ( not approved: | Does not meet US requirements. |
| Clauses affected: ( | B.4 and new Annex H |
| Other specs ( | x | Other core specifications ( | 33.107 |
| affected: |  | Test specifications |  |
|  |  | O&M Specifications |  |
| Other comments: ( | This CR has been agreed to by T1P1.SAH |

How to create CRs using this form:

Comprehensive information and tips about how to create CRs can be found at: http://www.3gpp.org/3G_Specs/CRs.htm.  Below is a brief summary:

1)	Fill out the above form. The symbols above marked ( contain pop-up help information about the field that they are closest to.

2)	Obtain the latest version for the release of the specification to which the change is proposed. Use the MS Word "revision marks"  feature (also known as "track changes") when making the changes. All 3GPP specifications can be downloaded from the 3GPP server under ftp://ftp.3gpp.org/specs/ For the latest version, look for the directory name with the latest date e.g. 2001-03 contains the specifications resulting from the March 2001 TSG meetings.

3)	With "track changes" disabled, paste the entire CR form (use CTRL-A to select it) into the specification just in front of the clause containing the first piece of changed text.  Delete those parts of the specification which are not relevant to the change request.

B.4

Instructions to Editor:  The ASN.1 encoding in Clause B.4 of TS 33.108 must be modified to define the new parameters required to be reported with the Serving System event.

servingSGSN-Number		[31?] OCTET STRING (  SIZE (1 .. 20 ) ) (  SIZE (1 .. 9 ) ), OPTIONAL

servingSGSN-Address			[32?] OCTET STRING (  SIZE (5 .. 17 ) ), OPTIONAL

-- procedures for the use of the servingSGSN-Number and servingSGSN-Address are

-- provided in Annex H

Instructions to Editor:  The ASN.1 encoding of the GPRSEvent parameter in TS 33.108 needs to be modified to add a codepoint for this event (See Clause B.2.6). Within the ASN.1, the following value should be added

GPRSEvent ::= ENUMERATED

{

pDPContextActivation 					(1),

startOfInterceptionWithPDPContextActive	(2),

pDPContextDeactivation					(4),

gPRSAttach 								(5),

gPRSDetach 								(6),

locationInfoUpdate 						(10),

sMS 									(11),

servingSystem							(13?),

-- procedures for the use of the servingSystem event are provided in Annex H

...

}

-- see ref [10]

Instructions to Editor: Add new Annex for the Serving System capability

Annex H (Normative):

U.S. Serving System Reporting

This annex provides the details for the reporting of the Serving System event.

The Serving System event reports the NOW/AP/SvP providing service to an intercept subject with terminal mobility, when the terminal is authorized for service.

A Serving System event is reported from the GPRS HLR when a mobile terminal is authorized for service with another NOW/AP/SvP or in another service area.

The event to HI2 record mapping is as shown in Table H.1

Table H.1: Mapping between Serving System Event and HI2 records type

| Event | IRI Record Type |
| --- | --- |
| ServingSystem | REPORT |

The ServingSystem event is reported via the REPORT record type.

Table H.2: Mapping between Events information and IRI information

| parameter | description | HI2 ASN.1 parameter |
| --- | --- | --- |
| ServingSGSN-Number | An E.164 number of the serving SGSN | ServingSGSN-Number |
| ServingSGSN-Address | An IP address of the serving SGSN | ServingSGSN-Address |

The REPORT record is sent to report information about the NWO/AP/SvP providing service to the interception subject with terminal mobility, when the terminal is authorized for service with another NWO/AP/SvP or in another service area.

The REPORT record shall include the information as described in Table H.3.

Table H.3: Serving System REPORT Record

| Parameter | MOC | Description/Conditions |
| --- | --- | --- |
| observed MSISDN | C | Provide at least one and others when available. |
| observed IMSI |  |  |
| observed IMEI |  |  |
| event type | C | Provide Serving System event type. |
| event date | M | Provide the date and time the event is detected. |
| event time |  |  |
| network identifier | M | Network identifier of the HLR reporting the event. |
| lawful intercept identifier | M | Shall be provided. |
| ServingSGSN-Number | C | Provide to identify the E.164 number of the serving SGSN |
| ServingSGSN-Address | C | Provide to identify the IP address of the serving SGSN |

# Comments

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to http://www.3gpp.org/3G_Specs/3G_Specs.htm

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark one or more of the boxes with an X.

Enter a concise description of the subject matter of the CR. It should be no longer than one line.

Enter the source of the CR. This is either (a) one or several companies or, (b) if a (sub)working group has already reviewed and agreed the CR, then list the group as the source.

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, B & C CRs for release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See http://www.3gpp.org/ftp/information/work_plan/

Enter the date on which the CR was last revised.

Enter a single letter corresponding to the most appropriate category listed below. For more detailed help on interpreting these categories, see the Technical Report 21.900 "3GPP working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR was to be rejected. It is necessary to complete this section only if the CR is of category "F" (i.e. essential correction).

Enter each the number of each clause which contains changes.

Enter an X in the box if any other specifications are affected by this change.

List here the specifications which are affected or the CRs which are linked.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.

This is an example of pop-up text.