## Slide 1
Import Aid
Nagaraja (Nag) Rao

## Slide 2
Overview
Purpose of this is to help in the strategy/decision making on the porting aspects:
  TS 33.107 to TS 33.127
  TS 33.108 to TS 33.128
  TS 33.107 to TS 33.9xx
  TS 33.108 to TS 33.9xx
Discussion points:
  Should the architecture and functions be changed?
  Or, just cut and paste?
  ASN.1 module be merged with the new module in TS 33.128
  Or, just cut and paste?
Upon consensus, CR can be generated to do the porting.
Decision to make on the items that need not be ported.

## Slide 3
Overview
TS 33.107 Vs TS 33.127

## Slide 4
Comparing the 5G LI architecture to pre-5G LI architecture
TS 33.127
TS 33.107
New terms:
  POI
  MDF
  POI Output
  Interception Product
New LI functions:
  Triggering Function
  SIRF
ADMF split into two:
  LICF & LIPF.

## Slide 5
Comparing LI specific interfaces 5G LI Vs pre-5G LI
TS 33.127
TS 33.107
Prefixing all interfaces with LI_
Common LI_X1
  Replacing X1_1, X1_2, X1_3
New interfaces:
  LI_T2, LI_T3
  LI_MDF
  LI_ADMF
  LI_SI
  LI_X0
  LI_HI4
LI_HI1 from LEA

## Slide 6
Point of Interception (POI) & Triggering Function
Point of Interception (POI):
  Two Categories:
    Directly Provisioned POI: Target list is provisioned at the POI
    Triggered POI: Target list is provisioned at the Triggering Function.
  Two types in each category:
    IRI-POI: output is xIRI
    CC-POI: output is xCC.
Triggering Function (TF)
  Two types:
    IRI-TF triggers Triggered IRI-POI
    CC-TF triggers Triggered CC-POI
TF to POI Interface (LI_T)
  Two variants:
    LI_T2: IRI-TF to IRI-POI
    LI_T3: CC_TF to CC-POI
TS 33.127
TS 33.107

## Slide 7
Interception at SMF/UPF Vs CUPS LI
TS 33.127
TS 33.107

## Slide 8
Overview
TS 33.108 Vs TS 33.128

## Slide 9
Overview
TS 33.128 |  | TS 33.108 | 
Interface | Protocol | Interface | Protocol
LI_X1 | ETSI TS 103 221-1 | X1 | Not standardized
LI_X1 (management) | ETSI TS 103 221-1 | n/a | n/a
LI_X2 | ETSI TS 103 221-2 | X2 | Not standardized
LI_X3 | ETSI TS 103 221-2 | X3 | Not standardized
LI_T2 | ETSI TS 103 221-1 | X3c, Sxa’/SXb’ | X3c not standardized, Sxa’, SXb’ in TS 29.244
LI_T3 | ETSI TS 103 221-1 | X3c, Sxa’, SXb’, Iq, Mc, Rx, Gx, Ix, Mn | X3c not standardized, Sxa’, SXb’ in TS 29.244 Iq, Mc, Rx, Gx, Ix, Mn are not standardized
LI_SI | Not standardized | n/a | n./a
LI_ADMF | Not standardized | n/a | n/a
LI_MDF | Not standardized | n/a | n/a

## Slide 10
Overview
TS 33.128
  Internal interfaces are standardized
  One Module for all functions
  Trigger descriptions are at stage 3 level (more detail).
TS 33.108:
  Internal interfaces are not standardized
  Separate ASN.1 module for each function.
  Trigger descriptions are at stage 2 level.

## Slide 11
Porting Decision
TS 33.107  s TS 33.127

## Slide 12
Porting Decision
Functional Architecture (clause 4 in TS 33.107)
Provisioning (clause 5 in TS 33.107)
CS (clause 6 in TS 33.107)
UMTS (clause 7 in TS 33.107)
Packet data w/ multimedia (clause 7A in TS 33.107)
WLAN (clause 9 in TS 33.107)
MBMS (clause 10 in TS 33.107)
IMS Conferences (clause 11 in TS 33.107
EPS (clause 12 in TS 33.107)
H(e)NB (clause 13 in TS 33.107)
GBA (clause 14 in TS 33.107)
  IMS Voice (clause 15 in TS 33.107)
  GCSE (clause 16 in TS 33.107)
  ProSE (clause 17 in TS 33.107)
  Messaging (clause 18 in TS 33.107)
  LALS (clause 19 in TS 33.107)
  S8HR (clause 20 in TS 33.107)
  PTC (clause 21 in TS 33.107)
  CSR (clause 22 in TS 33.107)
  NIDD (clause 23 in TS 33.107)
Main differences:
  Target Identifiers
  Change in LI specific functional names
  Change in LI specific interfaces

## Slide 13
Porting Decision
TS 33.108  s TS 33.128

## Slide 14
Porting Decision
Basic HO definitions (clause 4 in TS 33.108)
CS (clause 5in TS 33.108)
Packet Data (clause 6 in TS 33.108)
Multi-media domain – IMS IRI (clause 7 in TS 33.108)
WLAN (clause 8 in TS 33.108)
MBMS (clause 9 in TS 33.108)
EPS (clause 10 in TS 33.108)
IMS conference (clause 11 in TS 33.108)
IMS voice (clause 12 in TS 33.108)
Prose (clause 13 in TS 33.108)
GCSE (clause 14 in TS 33.108)
Messaging (clause 15 in TS 33.108)
CSR (clause 16 in TS 33.108)
PTC (clause 17 in TS 33.108)
PTC Encryption (clause 18 in TS 33.108).
Differences:
  Internal interfaces standardized
  Separate ASN.1 module for each function
  Stage 3 trigger descriptions

## Slide 15
Porting Decision
TR 33.9xx

## Slide 16
Porting decision
TS 33.107 Informative
  Annex A (CS voice flows)
  Annex B (GSN flows)
  Annex C (packet data with multi-media)
  Annex D (MGW with H.248)
  Annex E (IMS voice scenarios)
  Annex F (IMS call flows)
  Annex G (transcoded media)
  Annex H (Location only warrant)
  Annex I (Non-Local ID)
  Annex J (S8HR)
  Annex L (IP based HO interface for CS intercepts)
  Annex M (virtualization)
TS 33.108 Informative
  Annex D (LEMF handling of unrecognized fields)
  Annex F (Correlation Indications of IMS IRI with Annex G (US LI)
  Annex C (UMTS and EPS HI3)
  Annex M (HI notification using HI2)
  Annex N (IMS voice correlation - guidelines)
  Annex O (selection of ASN.1 sub-domain for LALS)