## Slide 1: [FS_AMD] Multi-CDN Thoughts
Source: Qualcomm Germany GmbH
Agenda Item: 2.5
Online, 16-18 October 2024
3GPP SA4 MBS SWG Post SA4#129-e
S4aI240175

## Slide 2: Multi-CDN is either ...
... A feature of the 5GMS AS or it is a feature of the Application Provider
Multi-CDN
Multi-CDN
Multi-CDN Client
Multi-CDN Client

## Slide 3: Examples
Option 1: 5GMSd AS does active multi-CDN operation
  DASH content is provided to the 5GMSd AS
  5GMSd AS initiates multi-CDN AS
  Note that 5GMSd AS can be in trusted or non-trusted network
  Examples for multi-CDN
    Multi-CDN hosting and client decision  add multiple service locations to MPD
    Content Steering  Add multiple service locations and content steering server
    Multi-CDN as defined in TS 26.247  Add multiple service locations to MPD and use SAND for switching
    CMMF  create new content from the DASH content and host it on different CDNs
Option 2: 5GMSd AS is an edge cache
  In this case the multi-CDN operation is done by the App
  The App may instruct to select the 5GMS AS as the serving CDN or maybe an external CDN.
  There may be two or multiple "5GMSd ASes", for example the 5GMS AS for each operator may be different.
  In this case the 5GMSd AS may only host a subset of the content

## Slide 4: What would multi-CDN mean in context of 5GMSd AS?
A service location defines a collection of network resources that share commonalities and can be referred to by a common label.
Several elements in the MPD of type xs:anyURI may have associated a @serviceLocation attribute which provides the label for a Service Location. If two resources share the same value for this attribute , (i.e., they are assigned to the same Service Location), then these URLs are likely to have their URLs resolve to services at a common network location, for example a common Content Delivery Network.
If the element does not include a @serviceLocation attribute, no relationship to any resource in the MPD is known.
The string value of @serviceLocation should only contain characters from the set [a..z], [A..Z], [0..9], '.', '-', and '_'.
A client may for example use such information in order to correlate network statistics from the collected statistics when resolving to a URL at the same service location to predict the behaviour when resolving for another resource at the same service location.
Service locations may for example be used to annotate redundant content offerings. In this case, for example a content steering operation as defined in Annex K.3.6 may use the values of service locations to steer the client towards a specific version of the redundant content offering.
MPEG-DASH defines service locations in clause 5.6.6

## Slide 5: Option 1: Implementation of AS with multi-CDN
5GMSd AS
Multi-CDN Controller
CDN/Service Location 1
CDN/Service Location 2
Multi-CDN Processor
Media Player+
Multi-CDN Client
DASH/HLS /CMAF
Media Player
M4
Multi-CDN Client
For 5GMS multi-CDN, either
an extension to the player and player manifest is needed or
a new module in player is added that is initiated with use plane information and interfaces with the media player through well defined APIs.

## Slide 6: Option 1: Implementation of AS with multi-CDN
5GMSd AS
Multi-CDN Controller
CDN/Service Location 1
CDN/Service Location 2
Multi-CDN Processor
Media Player+
Multi-CDN Client
DASH/HLS /CMAF M2
Media Player
M4
Multi-CDN Client
5GMSd AF
Provisioning M1
M3
MSH
M5
M10

## Slide 7: Implementation of AS with as one of multiple CDNs
5GMS application provider
5GMS-aware application
5GMSd AS
Multi-CDN Controller
CDN/Service Location 1
CDN/Service Location 2
Multi-CDN Processor
Media Player+
Multi-CDN Client
DASH/HLS /CMAF
Media Player
M4d
Multi-CDN Client
M8
M2
M7d
For 5GMS being one service location, most of the control exchange happens via M8d, but the player is instructed by M10d to change the behaviour, for example switch to the new service location

## Slide 8: Call flow for Option 1a: No Content Modification
Content is ingested into the AS
The 5GMSd prepares the content for multi-CDN delivery
  Updates the MPD to provide multiple service locations, possibly priorities
  Publishes the content at multiple service locations
  Potentially establishes a processor the manages the multi-CDN content (e.g. Steering server, MPD rewriter, SANDer)
The MPD is published and the media player uses the multi-CDN information
The Media Player may contact the Content Steering or SAND server for information and acts accordingly.
The Media Player downloads the content typically from one of the service locations
This information may be updated based on dynamic information from MPD updates, SAND information or from the Content Steering Server

## Slide 9: Call flow for Option 1b: Content Modification
Content is ingested into the AS
The 5GMSd prepares the content for multi-CDN delivery
  Creates a configuration information to provide information to Multi-CDN client
  Includes the Player entry point to the Manifest
  Creates multiple copies of each segments (e.g. CMMF encoding)
  Maps the redundant copies to a label taht can be associated to MPD URLs (something like an FDT in MBMS/MBS)
  Uploads the redundant copies to the service location
The AS Provides the configuration information to the CMMF module in the client
The CMMF client requests the redundant objects (for example on demand or proactively)
The CMMF client reconstructs the original segments and makes them available to the Media Player
This is very similar to DASH-over-MBMS and DASH-over-MBS

## Slide 10: Option 2: to be completed

## Slide 11: Proposal
It is proposed to
  revisit the entry point for multi-CDN CR
  Separate two cases, one with AS creates multiple service locations and second one were AS is a CDN.
  Develop generic call flows
  Map different solutions to the multi-CDN