## Slide 1: Alignment between generic and FS_eiRTCW’s architectures
S4aR220027
NTT

## Slide 2: Summary
This document proposes abbreviations for GA4RTAR’s functional blocks. Based on the abbreviations, this document shows the relationship between the generic architecture in GA4RTAR and the current FS_eiRTCW architecture.
The current FS_eiRTCW studies an architecture which assumes collocation of some generic functional blocks, which are being defined in GA4RTAR.
This document shows how the generic FBs are grouped and collocated in FS_eiRTCW.
It also shows how the relevant interfaces look like by the collocation.
Discussion points are:
The recognition and confirmation of the grouping and collocation of FS_eiRTCW
Naming for FS_eiRTCW’s FBs. How similar or different against generic and iRTCW? New names are proposed.
It seems convenient to define some variants of some generic interfaces. How?
According to the resolutions for the above issues, S4-221195 and FS_eiRTCW’s PD should be updated.
S4-221195 should include new abbreviations of GA4RTAR and one new functional block
FS_eiRTCW’s PD should rename all functional blocks

## Slide 3: Proposed Abbreviations for GA4RTAR’s FBs
FBs in GA4RTAR | Proposed Abbreviation
Media Session Handler | 5GRTC-MSH
Network Supporting Function | 5GRTC-NSF
Configuration Function | 5GRTC-CNF
Provisioning Function | 5GRTC-PVF
Ice Function | 5GRTC-ICEF
Media Function | 5GRTC-MF
WebRTC Signalling Function | 5GRTC-WSF
WebRTC IOP Function | 5GRTC-WIWF
Application Supporting Web Function | 5GRTC-WEBF
Based on the functional blocks in S4-221195.
The prefix (5GRTC-) can be omitted when it is obvious.

## Slide 4: Mapping of Functional Entities
ID | GA4RTAR | GA4RTAR Abbreviation | FS_eiRTCW (Block Category) | FS_eiRTCW (the current Function Block Name)
1 | Network Supporting Function | 5GRTC-NSF | S | Collocated with WSF
2 | Configuration Function | 5GRTC-CNF | S | Collocated with WSF
3 | Provisioning Function | 5GRTC-PVF | S | Collocated with WSF
4 | Ice Function | 5GRTC-ICEF | M | Collocated with WMCF
5 | Media Function | 5GRTC-MF | M | WMCF (WebRTC Media Centre Function)
6 | WebRTC Signalling Function | 5GRTC-WSF | S | WSF (WebRTC Signalling Function)
7 | WebRTC IOP Function | 5GRTC-WIWF | I | WNSGF (WebRTC NNI Signalling Gateway Function)
7a |  |  | Im | WNMGF (WebRTC NNI Media Gateway Function)
8 | Application Supporting Web Function | 5GRTC-WEBF | W | CSF (Conference Supporting Function)
Eight functional blocks in GA4RTAR are converged into four blocks (S, M, W, and I) in FS_eiRTCW due to collocation (with one exception)
Functional block collocations are based on the NOTEs in Clauses 2.5.2, 2.5.3, and 2.5.5 of S4-221195.

## Slide 5: Proposed new names for FS_eiRTCW FBs
ID | GA4RTAR | GA4RTAR Abbreviation | FS_eiRTCW (the current Function Block Name) | FS_eiRTCW (proposed new name)
1 | Network Supporting Function | 5GRTC-NSF | Collocated with WSF | 
2 | Configuration Function | 5GRTC-CNF | Collocated with WSF | 
3 | Provisioning Function | 5GRTC-PVF | Collocated with WSF | 
4 | Ice Function | 5GRTC-ICEF | Collocated with WMCF | 
5 | Media Function | 5GRTC-MF | WMCF | eMF
6 | WebRTC Signalling Function | 5GRTC-WSF | WSF (WebRTC Signalling Function) | eWSF
7 | WebRTC IOP Function | 5GRTC-WIWF | WNSGF (WebRTC NNI Signalling Gateway Function) | eWIWF
7a | TBD (WebRTC IOP Media Function) | TBD (WIMF) | WNMGF (WebRTC NNI Media Gateway Function) | eWIMF
8 | Application Supporting Web Function | 5GRTC-WEBF | CSF (Conference Supporting Function) | eWEBF
A new generic functional block may be needed, i.e., WebRTC IOP Media Function

## Slide 6: Architecture including interfaces
Generic architecture
5GRTC components are renamed.
(with missing 5GRTC-WEBF is added.)
FS_eiRTCW architecture
When 5GRTC-eWSF is collocated with 5GRTC-NSF/CNF/PVF, it works as a 5GRTC-AS.
The IFs related to 5GRTC-eWSF/eMF/eWEBF are variants of RTC-4 or RTC-3. They should be identified such as RTC-4XY (between X and Y) or RTC-3z.
Operator NW (HPLMN)
WebRTC Domain (Trusted DN)
UE
WebRTC
Endpoint
UDM
PCF
AMF
N5
SMF
N10
N8
N7
N11
N6
N3
N1
UPF
(R)AN
eWSF
(“S”)
RTC-4SU
RTC-4MU
RTC-4WU
eWEBF
(“W”)
RTC-3W
eMF
(“M”)
RTC-4SN
RTC-4MN
RTC-3M
RTC-4SI
RTC-4MI
eWIWF
(“I”)
eWIMF
(“Im”)
RTC-3I