3GPP TSG-SA Meeting #88	Tdoc SP-19XXXX

e-Meeting, 17th-19th June 2020

Title:	Presentation of Specification to TSG SA:
TS 26.511, Version 1.4.1

Source:	SA4

Document for:	Approval

Abstract of document:

This specification defines the profiles, codecs and formats for 5G Media Streaming (5GMS) services based on the 5G Media Streaming Architecture (5GMSA) including both unicast downlink and unicast uplink. The codec and format capabilities are defined for media components such as video, speech and audio codecs, subtitles, presentation format, media encapsulation as well as content encryption. Based on those capabilities, a collection of 5GMS profiles addresses specific service scenarios by defining requirements on the media capabilities. So far, Television (TV) and Virtual Reality (VR) profiles are specified. A default downlink profile and a default uplink profile are also defined in the case no other profile is claimed to be supported, providing indication on the minimum device capabilities supported by a 5GMS client.

Changes since last presentation to SA Meeting:

Media profiles have been defined following CMAF playback requirements. CMAF is identified as the preferred distribution format for compatibility with DASH and HLS. 5GMS has been added a default profile for uplink services with associated media capabilities and sending requirements. The support for subtitles has been included for downlink and TV profiles.

A video media presentation capability, namely HD-HDR, has been defined so as to identify the minimum capability under which HEVC decoding support is mandatory on top of AVC.

Outstanding Issues:

None.

Contentious Issues:

None identified.

Change history of this document:

1999-11-17: original issue

2007-09-06: removal of references to Working Groups; bring names of TSGs up to date; correction of typo

2015-01-06: adds tdoc header & removes redundant information below