## Slide 1: Structuring work on iRTCW and FS_eiRTCW
April-13 2022
NTT
S4-220517

## Slide 2: Proposal (Immersive Real Time Communication for WebRTC)
Between MNO and Application provider (i.e., OTT), four collaboration scenarios should be investigated. Refer to 511.
Two realizations are currently proposed.
  Type 1: Based on 5GMS-AF, extension of streaming architecture.
  Type 2: Based on WebRTC-AF, representing WebRTC Signaling server. Refer to 420.
Architecture, call flows, and protocol stacks should be further investigated.
The following work structure is proposed.
  iRTCW (normative work) covers Type 1 realization.
  FS_eiRTCW (study) covers Type 2 realization.
  Outputs will be maintained by two Permanent Documents (PDs).
  This allows flexible consideration and progress for each realization. Later, the two should be checked.
NOTE:
  Proponents should watch the architecture discussion in 5G_AREA.
  A scenario for NPN (Non Public Networks) was also suggested. Specific requirements are invited.

## Slide 3: Time plan – Option #1 taken with two PDs
 | 4-6 (2022) | 7-9 | 10-12 | 1-3 (2023) | 4-6 | 7-9 | 10-12
R-18 |  |  |  | S2 freeze |  |  | S3 freeze
iRTCW |  |  |  |  |  |  | Complete
Study |  |  |  |  | Comp |  | 
Option 2) 5GMS-AF
CS1
CS2
CS3
WebRTC-AF
CS3
CS4
Follow-up activity
In Rel-18/19?
Normative TSs
Option 1) 5GMS-AF
CS1
CS2
CS3
Informative TR

## Slide 4: Informative attachment

## Slide 5: Two scenarios for iRTCW (Immersive Real Time Communication for WebRTC)
Type 1) OTT is a primary service provider.
  WebRTC is one of the OTT’s services.
  MNO supports and assists OTT’s services indirectly.
    MNO doesn’t touch on WebRTC.
    MNO gets basic information (e.g., 5 tuples and QoS parameters) from UE and provides QoS enhancements.
  By providing an enabler, MNO is an actor behind an OTT.
  Simple scenario.
Type 2) MNO is a primary service provider.
  WebRTC is an MNO’s service.
  OTT and MNO can jointly provide the service.
  MNO plays the leading role.
  Advanced scenario.

## Slide 6: General view of WebRTC
Control-plane is up to a provider.
An intermediary is usually used.
Media
APP
Control
Media
APP
Control
Media
APP/SigServ/ICE/MCU/SFU
Control
UE-A
UE-B
Intermediary

## Slide 7: Two realizations around WebRTC
X is embedded as an NW control entry point.
Features by X are primitive (not full SDP level).
Media
APP
Control
Media
APP
Control
Media
APP/SigServ/ICE/MCU/SFU
Control
UE-A
UE-B
Intermediary
Type 1) MNO provides access to basic NW control via 5GMS-AF.
X
X
AF
PCF/NEF
Media
APP
Control
Media
APP
Control
Media
APP/SigServ/ICE/MCU/SFU
Control
UE-A
UE-B
Intermediary
Type 2) MNO provides entire session control by WebRTC signaling server (WebRTC-AF).
PCF
Traditional C-plane, but WebRTC-based
MNO

## Slide 8: Discussion points on the second week
Two realizations; 5GMS-AF by QLC and native WebRTC by NTT
Clarification on call flow image
  CS#3 by 5GMS-AF, what does signaling mean?
Modeling; AF or AS? Confusing?
  AF(Application function)
    5GMS-AF
    P-CSCF/IMS type (WebRTC Signaling Server)
  AS(Application server)?
Time plan (one PD or two PDs?)

## Slide 9: Collaboration scenarios (CS) and realizations
Realizations Collaboration Scenarios | Type 1: 5GMS-AF | Type 2: Native WebRTC-AF
CS1 (OTT) | Applicable | 
CS2 (ICE only) | Applicable | 
CS3 (One Signaling Server with one MNO) | Applicable (Not conferencing. Not call. Websocket + sub protocol) | Applicable (Typical conferencing)
CS4 (multiple Signaling Servers with MNOs) |  | Applicable

## Slide 10: Q & A
Q. For 5GMS-AF, what is the relationship with WebRTC?? What does “signaling” mean?
A. QoS Control. WebRTC Signaling Server looks like an AS.
Q. 5GMS is MPEG-DASH only, not RTP?
Q. 5G_AREA (stage 2) generalizes 5GMS to support RTC. Control should be similar for both streaming and RTC. Media are different.
In 5GMS-AF, AF is an access entry to MNO’s infra control.
Modeling for WebRTC Signaling servers has two views: AS (with 5GMS-AF) or AF (as WebRTC -AF).
The modeling of the two AFs needs further refinement along with the progress.

## Slide 11: Planning – Rel-18
Release 18 planning (no changes)
  SA Rel-18 Workshop September 2021 - completed
  Rel-18 Stage 1 100% complete by December 2021 (TSG#94) (with 80% completion at TSG#93)
  Rel-18 Stage 2 freeze March 2023 (TSG#99)
  Rel-18 Stage 3 freeze December 2023 (TSG#102)
  Rel-18 Protocol coding Freeze (ASN.1, OpenAPI), March 2024 (TSG#103)

## Slide 12: Planning – Rel-19
Release 19 planning – SA1’s assumptions
  Rel-19 Stage 1 completion by September 2023 (TSG#101) (with 80% completion at TSG#100)
  Rel-19 Stage 2 freeze TBD
  Rel-19 Stage 3 freeze TBD
  Rel-19 Protocol coding Freeze (ASN.1, OpenAPI) TBD

## Slide 13: backup

## Slide 14: TS 26.114

## Slide 15: TS 26.114

## Slide 16: Proposal in 377

## Slide 17: NTT’s idea

## Slide 18: 26.501

## Slide 20: Different Models between RTC Work Items
iRTCW
(WebRTC-based OTT model)
FS_eiRTCW
(WebRTC-based Carrier Assistance model)
WebRTC
Signalling
Server
NEF
(R)AN / UPF
MCU/SFU
with ICE
U-Plane
OTT-Data NW
QoS
Control
(NBI?)
QoS
Tunnel
Operator NW
(R)AN / UPF
new WebRTC
C-Plane
U-Plane
PCF
OTT
C-Plane
MCU/SFU
with ICE
QoS
Control
Npcf
N7,N4
OTT proprietary
Client
OTT proprietary
Client
Various
Client
Various
Client
With specified C-plane, Operator-Assistance will provide interoperability
as IMS-based model while involving OTT-related elements.
IBACS Expectation
(IMS model)
To be checked..
IMS Client
P-CSCF
(R)AN
C-Plane
Operator NW
S-CSCF
MRFP
MRFC
U-Plane
Mw
ISC
AS
Mp
IMS Client
PCF
Mr’
QoS
Control
N7,
N4
PCF
N7,
N4
WebRTC
Signalling
Server
Operator
NW
OTT-related elements
OTT App
OTT App
To be updated