## Slide 1: PDU and NAL units
Support for offline discussion related to S4-220424

## Slide 2
NAL unit
NAL unit
NAL unit
NAL unit
PDU
PDU
PDU
PDU
NAL unit
NAL unit
NAL unit
NAL unit
PDU
PDU
PDU
PDU
NAL unit
NAL unit
NAL unit
NAL unit
PDU
PDU
PDU
PDU
NAL unit
NAL unit
NAL unit
NAL unit
PDU
PDU
PDU
PDU
PDU Set
PDU Set
PDU Set
…
…
…
…
…
…
Possible ?
Mapping modes

## Slide 3
Parameter sets dependencies
Inter-frame prediction dependencies
Use cases
SPS
PPS
Slice
any type
PDU
PDU
PDU
PDU
…
…
PDU Set
I slice
P slice
B slice
P slice
PDU
PDU
PDU
PDU
PDU Set
…
…
slice
slice
slice
any type
PDU
PDU
PDU
PDU
PDU Set
…
…
Coded picture
Multiple slices per coded picture
slice
any type
any type
any type
PDU
PDU
PDU
PDU
PDU Set
…
…
Fragmentation unit

## Slide 4: Summary
Dependency use cases | Dependency level | Dependency type
Multiple slices per coded picture | Inside PDU set | Coding dependency
Parameter sets | Inside PDU set if PS and referring slices in same PDU set, otherwise inter PDU set | Coding and parsing dependencies
Other non-VCL NAL unit type dependencies (e.g. SEI, VUI) | More likely inter PDU set but also inside PDU set for frame-specific SEI. | Post decoding dependencies (non decoder)
Inter-frame prediction | Intra PDU set if reference frame in same PDU set, otherwise Inter PDU set | Coding dependency
Fragmentation unit | Inside PDU set | Parsing dependencies
Other? |  |