## Slide 1
3GPP TSG SA WG4#121 Tdoc S4-221470
Toulouse, France, 14th – 18th November 2022
Agenda item: 6.1
Source: Qualcomm Incorporated
Title: XR Architectures Summary
Document for Discussion and Agreement

## Slide 2: XR Architectures Summary
Thomas Stockhammer, Imed Bouazizi, Nikolai Leung, Liangping Ma

## Slide 3: Background
As proposed during the 3GPP SA4 Emmy Award Workshop, there was a rapporteur’s call on XR Client architecture. The goal is to define a way forward such that we can agree an XR client architecture that is common to all relative Rel-18 Study and Work Items.
Based on this rapporteur’s call, it was proposed:
  Prioritize definition of a baseline XR client architecture inputs at SA4#121 for use as baseline for all SIs/WIs related to XR: all interested members to bring proposals on such baseline XR architecture:
    Assume AR Client Device architecture will be set mostly by MeCAR. MR/VR client architecture is assumed to be a subset of AR Architecture despite different capabilities.
    Assume [iRTCW and] IBACS client architecture will inherit from MeCAR XR baseline architecture
  Interested members to bring descriptions of key XR use cases for such XR client architecture to ensure required capabilities are appropriate
    No fancy/too futuristic use cases. Best if expressed in terms of How do I plan to use OpenXR?
    Expectations:
      VR Chat/Gaming and AR call
      6DoF experience (6 degrees of freedom within a given reference system)
      AR experience (allow the user to relate to the real world)
      Define the need for enabling interactions? Controllers, trackers etc.
  Discussion to happen Monday 14th November afternoon in a plenary session

## Slide 4: Qualcomm Input Contributions related to this discussion
We have provided input to several Agenda Items and this slide deck summarizes this for the Architecture discussion
TDoc | Title | Source | Agenda Item
 | Split Rendering MSE |  | 
S4-221455 | Split Rendering Architecture and Call Flow | Qualcomm Korea | 8.6
 | SmarTAR – Tethering Glasses |  | 
S4-221317 | [FS_SmarTAR] Updates to Architectures | Qualcomm incorporated | 8.9
 | MeCAR |  | 
S4-221327 | [MeCAR] Updated AR Framework | Qualcomm incorporated | 9.5
S4-221328 | [MeCAR] Minimum Device Architecture | Qualcomm incorporated | 9.5
S4-221329 | [MeCAR] Interoperability Points for Visual and Audio | Qualcomm incorporated | 9.5

## Slide 5: Architecture from Permanent Document from MeCAR

## Slide 6: Comments and Considered Refinements
The Scene Manager is extended with a Presentation Engine block as typically a scene is setup and managed, but a presentation engine and the underlying hardware like a GPU is used to render the data accordingly.
Data to be consumed by the device is selected by the scene manager. The scene manager communicates with the MAF through the MAF API in order to setup of the delivery and decoding pipelines to provide the primitive buffers to the scene
The initial architecture focussed exclusively on visual processing. However, audio processing is as important and hence both media types have been added based on the discussions in the Video AHG meetings.
Data from the XR Runtime can be accessed within the device, for example the application. Only a selected subset, also possibly a converted one may be sent to the MAF and to the network. An XR Source Management is added to address the management or sources provided through the XR runtime such as microphones, cameras, trackers, etc.

## Slide 7: AR Framework for UE (1327)

## Slide 8: Implementable AR Device (1328)
Based on the framework in the previous slide, a simplified version of an XR device is presented that follows the principles for a 5G_STAR EDGAR-type device architecture with a standalone 5G System integrated.
In this case it is taken into account that the device not capable to render complex 3D scenes, but basically only makes use of the composition capabilities of the XR runtime.
The media is pre-rendered to for a specific time and pose and the Scene manager only converts the data to be compatible with the XR Runtime formats in the swap chain.
In the uplink a coded pose information needs to be made available that can be used remotely for prerendering to the latest pose. Additional media data may be sent.
Such a UE may be used in a split rendering application.
A detailed description of reference implementation APIs for such a device are provided in S4-221328.

## Slide 9: Edge-Dependent AR UE for Split Rendering (1328, 1455)

## Slide 10: Split Rendering Architecture (1317 + 1455)
Split rendering addresses the case that data is pre-rendered in the cloud/edge.
The EDGAR UE from the previous slide is used

## Slide 11: Operation Points (TS 26.118)

## Slide 12: Interop for Audio-Visual AR UE (1329)

## Slide 13: Interfaces
IF | Name | Functionalities | Specification
1 | XR Runtime API | The functionalities of the API include what is documented in clause 4.2.2 predominantly, namely Creation of a XR Session Providing controller and pose information to support immersive and 6DoF based rendering Visual composition through swap chains including associated timing and predicted pose information and adapted to the latest pose and the output peripheries Audio composition to through buffers including associated timing and predicted pose information and adapted to the pose and the output peripheries Synchronization of audio-visual output Collection of audio and video sources provided to the XR source management Query of optional processing and rendering capabilities, for example projection formats | Specification of reference system with the capabilities. As reference system API, Open XR APIs are provided with possibly a subset of specifications. For Video rendering, it is based on OpenGL ES. For Audio rendering, it is based on OpenSL ES and TS 26.118 Any XR System that fulfils the functionalities, is ok. This API is similar and an extension to the VR-API in TS 26.118.
2 | Source media and metadata formats | The functionalities of this interface include to collect information from the XR Runtime that then may then be sent and encode | The semantics and syntax of the viewer pose need to be specified as a reference to OpenXR. Other capturing and sensor if not directly related to AR is out of scope.
3 | Scene Information and Buffers | The functionality of this interface is to define a set of primitive buffers for different media types that can be rendered by the Visual and Audio renderer. In combination with the Scene description, the information can be used render 3D and immersive scenes by the Scene manager and the presentation engine The combination of the scene description information, possibly generated from the application or in a delivery document, as well as the primitive buffers provide sufficient information to the presentation engine in order create an immersive audio-visual experience | A reference scene description format based on glTF2.0 as a reference. The scene description is specified as one way to support it, but equivalent application functions may be defined. A proper subset of glTF2.0 with possible extensions need to be defined. This information is similar to what was defined as VR Scheme in the context of TS 26.118
4 | MAF-API | A functionality to configure and control the media access and delivery by the scene manager, the XR source manager and/or the application in order to set up media delivery pipelines. The API is rich enough to support configuration of downlink access for media, downlink access of scene description, uplink delivery for media, Uplink delivery for metadata The information may include for example dynamic information such as updated pose information, etc. | A reference API should be specified for the MAF in order to configure the pipelines. While this API may not be mandatory, it is a reference to support the functionalities This part is included in the VR-API as defined in TS 26.118.
5 | 5G Media API | This is the core network interfaces to support media delivery in the downlink and uplink including QoS support and media session handling. The functionality includes: Scene Description delivery and updates, Audio and video decoding for multiple buffers, Audio and video encoding for multiple buffers, Coding and delivery of pose information, Media Session Handling and QoS, Metadata delivery, 5GMS based Content Delivery protocol based on DASH/CMAF, RTP-based delivery, Encryption and security, Rate control | Core of the specification for TR 26.119 This API is equivalent to the 3GPP VR OP as defined in TS 26.118. The DASH API is not defined as the entry point is the Scene Description.
6 | Internal Application API | The application may have access to control the runtime and the sources in order to configure the work flow. | This is outside of the scope of the specification
7 | Application network API | The application may connect to the network to identify entry points or deal with XR Runtime specific data. | Basic functions may be supported, but do not have to be specified in TS26.119.

## Slide 14: Tethered Display AR glasses-based device architecture (1317)

## Slide 15: Important Principles
The Media Access Function at this stage is not including control plane
  Media Compression and Delivery functions are included
Control plane is specific to the architecture that the device is used in. Examples
  5GMS Media Session Handler and AF
  GA4RTAR Media Session Handler and AF
  IMS control channel
  We may add a generic control session block to the architecture (see next slide)
XR Runtime API wraps device hardware and many proprietary optimization happen below the API.
  Hence, the XR Runtime API is the furthest southbound API
  no interop specs south of this API
All media types are controlled by a single Presentation engine

## Slide 16: Control Session Client included

## Slide 17: Important Principles
The Media Access Function at this stage is not including control plane
  Media Compression and Delivery functions are included
Control plane is specific to the architecture that the device is used in. Examples
  5GMS Media Session Handler and AF
  GA4RTAR Media Session Handler and AF
  IMS control channel
  We may add a generic control session block to the architecture (see next slide)
XR Runtime API wraps device hardware and many proprietary optimization happen below the API.
  Hence, the XR Runtime API is the furthest southbound API
  no interop specs south of this API
All media types are controlled by a single Presentation engine

## Slide 18: Proposals
Ádopt the architure framework
Adopt the EDGAR architecture
Move forward with network architectures
Agree on the important principles

## Slide 20: Media Access Function