## Slide 1: Qualcomm's View on Rel-19 Planning
Thomas Stockhammer, Imed Bouazizi, Nikolai Leung, Liangping Ma
Qualcomm Technologies
tsto@qti.qualcomm.com
3GPP TSG SA WG4 Meeting #124 S4-230809
Berlin, Germany 22 – 26 May 2023

## Slide 2
Background: 5G-MAG Rel-19 Workshop
RAN Considerations
SA2 Considerations
SA4 in Rel-18
SA4 Considerations
Proposal

## Slide 3: 3GPP work-planning and schedule
SA2 Rel-19 timeline
2020 |  | 2021 |  |  |  | 2022 |  |  |  | 2023 |  |  |  | 2024 |  |  |  | 2025 | 
Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2
R18 package
Rel-19 External discussions begin in May 2023
Release 18
Release 19
R18 package
1st batch
(Sep. 23)
2nd batch
(Dec. 23)
Ext
SA4?

## Slide 4: RAN Considerations
Broadcast and Media-Related Considerations

## Slide 5: Broadcast and Media-Related Considerations
High Priority: XR & Metaverse enh Phase 2, WI (R2)
  XR awareness: delivery deadline, awareness of APP level FEC in RAN; PowS enh: DRX enh for reduced PDCCH monitoring & HARQ re-tx; Cap enh: dynamic msmrt. gaps
Neutral: MBS Phase 3, WI (R2)
  Other feature combination with MBS
Important: 5GB/ATSC 3.0 Coex WI (R1)
  5GMAG proposal expected
  Small project - it could be done by TEI
Not in priority: Enhancements of LTE-based 5G Broadcast (Time and Frequency Diversity)
  If this would be needed/of interest, Broadcasters would have to lead
Not of interest:
  MBS and NR for HPHT systems  if at all very long-term project starting with gap analysis

## Slide 6: SA2 Considerations
Broadcast and Media-Related Considerations

## Slide 7: XR: further enhancements for RAN scheduling and PDU Set based QoS handling
  Awareness of Application Layer Forward Error Correction (AL-FEC) at RAN can assist detection of PDU-set errors and allow scheduler optimization in delivery of PDU-sets
    For example: Indication of Content Ratio to RAN to know how many PDUs (in %) are needed to consider a PDU Set successfully delivered
  For certain types of XR flows, PSDB/PDB does not fully represent the actual latency requirements because applications care about the absolute delivery time of display.
    Introduce PDU-Set delivery deadline (PSDD) as an alternative to PDB
  Better adaptability of 5GS QoS level for XR traffic
    Extend Alternative QoS Profile concept to PDU Sets
UPF
RAN
UE
SMF
PCF
FEC content ratio = 75%
4
3
2
1
4
2
1
PDU set w/ 4 PDUs

## Slide 8: Dual Steer: PDU sessions with dual 3GPP access paths
Currently ATSSS requires one 3GPP access and (at least) one integrated non-3GPP access
In certain use cases, non-3GPP access(es) are not ideal to improve capacity, coverage, reliability and QoE, e.g.:
  stadium with SNPN or local PLMN deployment
  aggregation of 2x 5G links for AVPROD
  3GPP terrestrial access + 3GPP non-terrestrial access
Goals:
  Enable additional 5GS tools, under MNO control/policy, to improve access/NW resources utilization, capacity, coverage, reliability and QoE, using dual 3GPP access
  Provide flexible user plane traffic aggregation, steering & switching at 3GPP layer

## Slide 9: Recap: Some MM/XR Work in Rel-18 SA4
  Architectures
  Features

## Slide 10: 5G Media Streaming
Ongoing Enhancements in Rel-18

## Slide 11: Stage-3 Work for Rel-18 in Preparation
Stage 3 support for uplink streaming as defined in TS 26.501 and based on the conclusions in clause 6.5 of TR 26.804.
Stage 3 support for end-to-end low latency live streaming as defined in TS 26.501 and based on the conclusions in clause 6.11 of TR 26.804.
Stage 3 support for 5GMS over MBS and 5GMS hybrid services as defined in TS 26.501 and based on the conclusions in TR 26.804 and TR 26.802
Stage 3 support for multiple media service entry points as defined in TS 26.501 and based on the conclusions in TR 26.804.
Extensions to 5GMS protocols to support traffic identification based on the conclusions in TR 26.804, clause 6.3.
Addition of HTTP/3 to the 5GMS protocols as an optional alternative based on the conclusions in clause 6.4 of TR 26.804.
Addition of necessary parameter extensions to the M1, M5, and M6 reference points to provide access to Background Data Transfer based on the conclusions in clause 6.6 of TR 26.804.
Specification of the usage of Oauth 2.0 (according to the SA3 guidelines) for 5GMS protocols based on the conclusions in clause 6.9 of TR 26.804.
Specifications for the 3GPP Service Handler and URL including the necessary functions on UE and device to support automatic launch of 5G System services in the context of 5G Media Streaming based on the conclusions in clause 6.13 of TR 26.804.
Additional minor enhancements based on feedback from 5G-MAG Reference tool developments.
Specification of a RESTful API at reference point M3 for the configuration of 5GMS AS instances by 5GMS AF based on the conclusions in TR 26.804.
Specification of data types for data reporting of ANBR-based Network Assistance invocations and (in liaison with CT3) specification of data types for exposure of events relating to invocation of AF-based and ANBR-based Network Assistance.
Completion of the Work item March 2024
Can everything be completed?

## Slide 12: G4ARTAR
Rel-18 Stage 2 work to create 5GMS equivalent for Real-time and WebRTC based delivery
Stage-3 Work unclear

## Slide 13: Rel-18 Media Capabilities for XR/AR
Defining baseline requirements for an AR lightweight and XR device
Hinge
SoC Media
Connectivity
Eye Tracking + Camera/Sensor Aggregator
Requirements include
OpenXR Core APIs
rendering capabilities
capturing capabilities
audio and video codecs
scene description
Wire formats for metadata
Profiles for split rendering and stand-alone rendering
Basic functionalities expected

## Slide 14: Media Service Enablers
4 General
4.1 Overview: Motivation, Overview
4.2 Typical Use Cases and applications
5 Reference architecture and procedures
5.1 Reference Architecture
5.2 Core functions and extensions
5.3 Procedures and call flows
6 Prerequisites
6.1 5G System functionalities
6.2 Device APIs and functionalities
7 MSE Application Function specification
7.1 Overview of the MSE API calls
7.2 Functionality
7.3 MSE AF API methods and parameters
8 MSE user plane specification
8.1 Overview
8.2 User plane configuration protocols
8.4 Content delivery protocols
8.3 Formats and Codecs
8.4 QoS considerations
8.5 Security considerations
9 MSE Client specification
9.1 Overview of the MSE API Calls
9.2 Functional description
9.3 MSE Client API methods and parameters
Annex A (informative): Implementation guidelines
A.1 Guidelines for application developers
A.2 Guidelines for MSE implementers
Annex B (informative): Considerations on conformance testing
Annex C (normative): API Reference Pages
Annex D (informative): Considerations on API Instantiations
Annex E (informative): Attachments and online repositories
Framework proposed and completed in Rel-18, TR 26.857

## Slide 15: A distributed compute architecture enables rich XR user experience
M2R2P = Edge processing + 5G round-trip time + Device processing
Game engine
Encoder
Application
Post processing (ATW, error concealment, …)
Decoder
Perception algorithms
Compressed rendered frames
6DoF HMD pose, controller, eye/hand tracking
Motion-to-render-to-photon latency
M2R2P
How to standardize split rendering?

## Slide 16: Split Rendering Workflow Architecture
Network API
Qualcomm is planning to bring this to 5G-MAG Reference Tools

## Slide 17: Split Rendering MSE and Interfaces
Basic functionalities expected

## Slide 18: Variants - Smartly Tethering AR Glasses (SmarTAR)
Issues:
  Non-provisioned additional tethering link (e.g. WiFi)  QoS and latency measurement and control
  End-to-end formats to avoid transcoding and security issues
  Combination of UE/Phone and network rendering
  Distribution of compute resources across glasses, UE and edge/cloud
Study item in 3GPP SA4
Expect input for Rel-19 Work Items

## Slide 19: FS_AI4Media: Reference Architecture – Split Inference
Evaluation
Inference
Inference
Inference
Test Dataset
Anchor Model
Split Model Part #1
Split Model Part #2
Compression
Decompression
NW
Bit rate (or bit stream)
Consider complexity in evaluation? – reflects impact on power consumption and delay.
Send compressed video
Privacy (a motivation of split inference) is left to next-level decision
Need details of anchor model
Process
Codec, encoder config
Study expected to take on full Rel-18 as evaluation framework will be created

## Slide 20: SA4 Considerations for Rel-19
Broadcast and Media-Related Considerations

## Slide 21: 3GPP work-planning and schedule
SA2 Rel-19 timeline
2020 |  | 2021 |  |  |  | 2022 |  |  |  | 2023 |  |  |  | 2024 |  |  |  | 2025 | 
Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2
R19 package
Rel-19 External discussions begin in May 2023
Release 18
Release 19
R19 package
1st batch
(Sep. 23)
2nd batch
(Dec. 23)
Ext
SA4 & Media?
5G-MAG

## Slide 22: SA4 Timeline and Process Considerations
SA4 is still doing bug fixes to MBS Rel-17
Based on Rel-18 progress, it is expected that SA4 will be busy until Mar 2024
Study and work items in RAN and SA2 expected to impact SA4 work
Proposal:
  Start SA4 Rel-19 planning only in December 2023
  Build on leftovers from Rel-18, studies from Rel-18, as well as work topics related to RAN and SA2 work
  Identify substantial new work topics for Rel-19
  Build Media Service Enablers
  Work with requirements and inputs from the industry: 5G-MAG, Metaverse Standards Forum, etc.

## Slide 23: Potential Larger Topics based on Rel-17/18 study and work items
Details are tbd
New Video Codecs
AI/ML for Media
VVC
Avatars
Animation and Uplink
XR Extensions
Advanced Split Rendering, Immersive and Split Audio
5G Media Streaming and MBS Extensions
HEVC for XR, if anything needs to be done
Representation, Formats, Communication
Leftovers from Rel-18 (e.g. DRM, Content Steering)
Requirements from 5G-MAG
Distributed Inference and Learning
AI/ML-based Computer Vision
Requirements from MSF, e.g. QoE and Metrics

## Slide 24: Conclusions

## Slide 25: Proposal for SA4‘s Message to SA Workshop
SA/SA2/RAN2
  Let SA4 do stage-3 on media related topics
  indicate early potential impact on SA4
Provide input related to SA4:
  Start SA4 Rel-19 planning only in December 2023
  Build on leftovers from Rel-18, studies from Rel-18, as well as work topics related to RAN and SA2 work
  Identify substantial new work topics for Rel-19
  Work with requirements and inputs from the industry: 5G-MAG, Metaverse Standards Forum, etc.
Potential larger work topics for SA4
  New Video Codecs
  Avatars
  XR Extensions
  5G Media Streaming and MBS Extensions
  AI/ML for Media