## Slide 1
Study on Glasses-free 3D Real-Time Communication (FS_G3D) for Release 19
  China Mobile，Huawei，ZTE，Lenovo
  3GPP SA WG4 Meeting #126
  Chicago, US, 13–17 Nov, 2023
  S4-231712

## Slide 2: Motivation-1
With the increasing prevalence of 3D capture technologies and glasses-free 3D displays in consumer products (e.g., phones equipped with depth sensors, glasses-free autostereoscopic displays, and multiscopic displays [1]), substantial advancements have been achieved in glasses-free 3D telecommunications. This progress has resulted in the development of prototypes [2,3] and even commercial products [4].
Glasses-free 3D communication may require the processing, transmission, and storage of massive data through the 3GPP network, thereby demanding more network capabilities and computing resources. For example, in the case of single-viewpoint G3D, data consumption is expected to double, while light field technology needs to accommodate up to multiple viewpoints to ensure an optimal user experience.
3D Real-time Communication Network Requirements (Point Cloud/ 60 fps) |  | 
Usage Scenario | Peak Data Rate | User Experienced Data Rate
Human/Objects (Dense point cloud) | 0.5Gbps | 100Mbps
Large-scale Scenes (Sparse point cloud) | 2Gbps | 400Mbps
Tecent 3D Meeting
G3D Live Broadcasting
Google Project Starline

## Slide 3: Motivation-2
In 2012, the ISO/IEC MPEG and ITU-T Video Coding Experts Group (VCEG) formed the Joint Collaborative Team on 3D Video Coding Extension Development (JCT-3V) [5]. These 3D coding standards encompass extensions based on both AVC and HEVC (e.g., H.264/MVC, H.264/SVC, MV-HEVC and 3D-HEVC).
In Release 11, the Mobile 3D stereoscopic video has been investigated in FS_M3DVC, TR 26.905 [6]. It targets the support of stereoscopic 3D video coding solutions, enhance the integration of selected video coding technologies into existing service components and functionalities, and address the potential network capacity and QoS requirements for stereoscopic 3D video services.
In Release 18, 3GPP SA4 is working on the Evaluation of new HEVC coding tools (FS_HEVC, TR 26.966), with the anticipation of offering HEVC-based solutions for the delivery of 3D video content. Additionally, SA4’s ongoing study on the 5G Real-time Media Transport Protocol Configurations (5G_RTP, TS 26.522) is expected to provide the RTP-based solution for the transport of real-time immersive media and assoicated metadata. For example, use of multiple simultaneous RTP streams in a single RTP session.

## Slide 4: Open Issues
    TR 26.905 leftovers worth to be further investigated in Rel-19:
3GPP services extension to support 3D, involves the 2D-to-3D conversion, conversational services and specific mobile 3D video adaptations to the bitrate variation.
Potential requirements and optimization for switching between 2D and 3D modes (e.g., re-configuration of the codec, UE display capability).
Communication and networking solutions need to be investigated for satisifying the delay and data rate requirements of FS_G3D.
In the TR 26.905, it addressed the DASH-based streaming solution, which falls short of meeting the demands of FS_G3D. Real-time transport protocols like RTP and RTCP, or new protocols based on UDP, such as QUIC over HTTP/3, could potentially offer viable solutions.
A more comprehensive QoE can be studied as a measure that indicates the end-to-end performance of FS_G3D, assessing how effectively the network satisfies user requirements.
3GPP TR 26.905: "Mobile stereoscopic 3D video"

## Slide 5: Potential 3D Content Formats
Name | Example | Definition | Pros | Cons | Codecs
Stereoscopic 3D frames | - side-by-side - top and bottom - checker-board - interleaved | The frame-compatible packing for 3D contents. | Compatible with a 2D frame infrastructure. | Conumes twice the bandwidth when compared to a standard video; | H.264/AVC ...
RGB+Depth |  | A combination of a RGB image and its corresponding depth image. | Small data volume; High mobility and low cost; | Hard to represent 3D geometric details with 2D images; | H.264 ...
Multi-view |  | Representing 3D geometry through multiple 2D images from different perspectives. | Small data volume; | Hard to represent 3D geometric details with 2D images; | MV-HEVC ...
Voxel Grid |  | A voxel grid geometry is a 3D grid of values organized into layers of rows and columns. | Topology flexibility; Adapt to 3D CNN; | High memory usage; Limited resolution; Difficult to reconstruct details; | -
Point Clouds |  | A point cloud is a collection of points of data plotted in 3D space. | Simple data structure; Easy to edit; Topology flexibility; | Difficult to reconstruct details; Large data volume; | V-PCC ...
Meshes |  | A mesh is a collection of vertices, edges and faces that defines the shape of a 3D object. | Industry Standard; Explicit connectivity information; Easy to render; | Complex structure, not suitable for tiling and culling; Topology changes difficult; | 3DMC ...
Implicit Neural Representation |  | An implicit function represents a geometry as a function that operates on a 3D point that satisfies | Infinite resolution； Easy to reconstruct details; | Complex function representation; High computational resource requirements; | /

## Slide 6: Reference Use Case: G3D Conversational Services
Use Case Description:
3D conversational services have also been supported by the newest 3D-enabled products and these applications have been gaining significant popularity among the consumers recently. For instance, the latest 3D-enabled laptops have 3D web cameras that capture and record 3D video, and transfer it to others over the internet, enabling services such as 3D video chat, 3D video conferencing, 3D gaming and 3D video phone using web applications.
Potential Requirements:
3D-enabled UE devices that capture and record 3D video via the availiability of 3D web cameras.
Transmission of 3D video content through the 3GPP network, e.g., through the use of MTSI services.
UE capability for decoding and rendering the 3D video.
UE capability for exchanging signalling of supported 3D video codecs and formats.
3D video hardware and high-performance software drivers for watching high-quality 3D videos and playing 3D video games.
3GPP TR 26.905: "Mobile stereoscopic 3D video"

## Slide 7: Reference Use Case: Multiple-party G3D Conference
Use Case Description:
This use case describes a multiple-party 3D video conference service, a meeting host can setup the 3D video conference call, and other 3D phone users can join the call. The 3D video information is exchanged among the multiple 3D-Enabled phones users over MTSI system, the users can join or drop off the 3D video group call at different locations.
Potential Requirements:
3D-enabled mobile terminals to capture, record, store 3D video.
Transmission of 3D video sequence and audio via the MTSI system over the 3GPP operators' mobile network.
UE capability for decoding and rendering the 3D video.
UE capability for exchanging signalling of supported 3D video codecs and formats.
3GPP TR 26.905: "Mobile stereoscopic 3D video"

## Slide 8: Reference Use Case: G3D Live Broadcasting
Use Case Description:
3D live broadcasting can serve a large number of audiences over the Internet. The host side uses multiple 3D cameras to capture scenes from different viewpoints simultaneously and automatically merge them. The audiences side can display the content on a wide variety of 3D capable devices to watch the 6DoF 3D live broadcast. The system can be used for entertainment or sporting events to achieve a more realistic and immersive experience.
Potential Requirements:
3D capture devices (e.g., Kinects, phone with depth sensors) for multi-view acquisition.
Transmission of 3D video content through the 3GPP network, e.g., through the use of WebRTC/DASH server.
UE capability for decoding and rendering the 3D content.
3D Camera
3D Camera
Broadcast Server
3D Video
Content
HLS
DASH
FLV-HTTP
Audiences
Host

## Slide 9: Possible Solutions for Compression and Transmission
Investigation of solutions for deliverying 3D contents, such as Multi-view, Point Cloud, Volumetric Video, and 3D Mesh over IMS/WebRTC may also fall within the scope of the Rel-19 study.
H.265(HEVC)
MVC(Multiview Video Coding)
MVC was standardized by MPEG as an extension of the H.264/AVC. MVC provides a compact representation of multiple views that are simultaneously created by several cameras. In TR 26.905, MVC is used as one of the video codecs for stereoscopic 3D. A RTP playload format for MVC video can be applied in RTP based 3D video transmissions [8,9].
Current state-of-the-art S3D communication systems, such as Google Project Starline [7], have compressed color and depth
(RGB-D) data using 2D video compression schemes (e.g., H.264, H.265), and transmitted with WebRTC to a remote peer. At the remote side, the RGB-D data is then used to construct a 3D mesh and visualized with 3D displays.
Jason Lawrence, Danb Goldman, Supreeth Achar, Gregory Major Blascovich, Joseph G. Desloge, Tommy Fortes, Eric M. Gomez, Sascha Häberling, Hugues Hoppe, Andy Huibers, Claude Knaus, Brian Kuschak, Ricardo Martin-Brualla, Harris Nover, Andrew Ian Russell, Steven M. Seitz, and Kevin Tong. 2021. Project starline: a high-fidelity telepresence system. ACM Trans. Graph. 40, 6, Article 242 (December 2021), 16 pages. https://doi.org/10.1145/3478513.3480490
Schierl, Thomas & Narasimhan, Sam. (2011). Transport and Storage Systems for 3-D Video Using MPEG-2 Systems, RTP, and ISO File Format. Proceedings of the IEEE. 99. 671 - 683. 10.1109/JPROC.2010.2091370.

## Slide 10: Summary - Proposed Objectives
Identify and document the G3D RTC related use cases and requirements.
Study potential enhancement to current 3GPP conversational services (e.g., MTSI, IMS-based telepresence, etc.) to more effectively meet the G3D RTC requirements, such as reducing latency and optimizing bandwidth efficiency.
Document potential 3D content format, codecs, protocols and transmission solutions (e.g., RTP, RTCP, QUIC...):
  Evaluate their feasibility to be used in the G3D RTC based on factors such as network resource consumption, bandwidth usage, terminal-side decoding speed and etc.
  Note: The evaluation should prioritize network and service apsects when assessing existing video profiles from 3GPP or other standards for their feasibility to support G3D RTC over 5G/5G-A.
  Explore potential optimization solutions to further reduce the uplink bandwidth consumption of G3D RTC.
Explore the incorporation of glasses-free 3D into IMS and WebRTC services, covering aspects like 3D signaling (codecs, 3D video formats, and device capabilities), the processing of multi-view (multi-camera) data.
Whether and how the network can be utilized to support G3D-related technologies (e.g. ,multi-viewpoint generation and rendering, real-time 2D-to-3D conversion...) and thereby reduce the requirements and energy consumption of UE.
Define QoE model for measuring G3D RTC performance:
  User-centric parameters: video resolution, framerate, the quality of 3D anaglyph effect, the depth of analyph effect and etc.
  Network-centric parameters: network delivery speed, latency, end-to-end packet loss, network usage and etc.
Provide guidelines on what features should be recommended for support by UE and the network.
Identify any requirements for normative work of glass-free 3D real-time communications.

## Slide 11: References
All the Stereoscopic 3D devices presented at CES 2023
Google, Project Starline, 2023
C. Zhang, M. Su, Q. Liu and M. Yang, "3D Communication System Integrating 3D Reconstruction and Rendering Display," 2022 5th International Conference on Advanced Electronic Materials, Computers and Software Engineering (AEMCSE), Wuhan, China, 2022, pp. 167-170, doi: 10.1109/AEMCSE55572.2022.00041.
LUMA PAD 2
JCT-3V
3GPP TR 26.905: "Mobile stereoscopic 3D video"
Jason Lawrence, Danb Goldman, Supreeth Achar, Gregory Major Blascovich, Joseph G. Desloge, Tommy Fortes, Eric M. Gomez, Sascha Häberling, Hugues Hoppe, Andy Huibers, Claude Knaus, Brian Kuschak, Ricardo Martin-Brualla, Harris Nover, Andrew Ian Russell, Steven M. Seitz, and Kevin Tong. 2021. Project starline: a high-fidelity telepresence system. ACM Trans. Graph. 40, 6, Article 242 (December 2021), 16 pages. https://doi.org/10.1145/3478513.3480490
Schierl, Thomas & Narasimhan, Sam. (2011). Transport and Storage Systems for 3-D Video Using MPEG-2 Systems, RTP, and ISO File Format. Proceedings of the IEEE. 99. 671 - 683. 10.1109/JPROC.2010.2091370.
S. Vishwa Kiran, S. Raghuram, J. Thriveni, and K.R. Venugopal. 2023. Reduction of jitter in 3D video by transmitting over multiple network paths. Int. J. Adv. Intell. Paradigms 24, 1–2 (2023), 110–125. https://doi.org/10.1504/ijaip.2023.128077

## Slide 12
Thank you!