## Slide 1: Introducing 3GPP
Frédéric Gabin (Dolby Laboratories Inc.)
Chair of 3GPP SA WG4 (Multimedia Codecs, Systems and Services)

## Slide 2: Content
The role of 3GPP
3GPP – How the project works
The 3GPP eco-system
Technical Specification Groups
Quarterly meeting cycle
3GPP releases & Stages of a release
Bringing the work in
5G Releases
Rel-19 Workshops & planning
Focus on 3GPP TSG SA WG4 (SA4)
Conclusions

## Slide 3: The role of 3GPP
Part of the invention, proof of concept, standardization, trials, commercialization …cycle
Specifications and Studies providing a complete system description for mobile telecommunications
The system description is characterized by a number of standardized interfaces. It is not a description of a standardized deployment
This standardization effort enables an interoperable, multi-vendor approach to deployment and generates mass market economies of scale, without stifling innovation

## Slide 4: 3GPP – How the project Works
3GPP works based on
  Participation in face-to-face meetings
  Pro-activity & Contributions – you need written proposals to get attention
  Consensus – nobody says “no” in order to progress
Work organization
  Study Items, Work Items
  Releases with fixed time-lines, which are partially overlapping
  Work Plan (good overview)
3 stages, often overlapping
  Stage 1: Requirements
  Stage 2: Architecture
  Stage 3: Protocols
Companies not individuals participate
  From all over the world
  All major telecommunication companies – operators, vendors, service providers
  Ministries, Regulators and government agencies actively engaged
  More and more vertical industry representatives bring their work directly to 3GPP
Amazing Track Record
  3GPP started 1998, since then all major standards projects were deployed
  Seamless migration from “old” to “new” mobile generations
A new Release every 15 to 24 months
  Allows for resonably fast standardization & deployment of new technologies
  Strong commitment to time-lines guarantees reliable planning

## Slide 5: 3GPP Membership
The 3GPP Organizational Partners – from Asia, Europe and North America – determine the general policy and strategy of 3GPP.
838 organizations have joined 3GPP via one of these seven OPs.
https://www.3gpp.org/about-us/partners

## Slide 6: 3GPP standards eco-system
Next Generation Projects
5G Projects
Official Liaisons on specification work:
Certification Bodies
3GPP Organizational Partners (OPs)
The 3GPP Organizational Partners (OP) - 7 Standards Organizations - from China, Europe, India, Japan, Korea and the United States.
Participation in 3GPP by companies and organizations becoming Members of one of these 7 OPs.
Inputs on market requirements may come in to the Project via 3GPP Market Representation Partners (MRP).
There is a lot of additional external liaison activity…SDOs, Industry bodies, projects…
450 MHz Alliance, AISG, Bluetooth, Broadband Forum (BBF), CableLabs, International Special Committee on Radio Interference (CISPR), CTIA, Digital Video Broadcasting (DVB) Project, Ecma, International, Expert Group for Emergency Access (EGEA), Eurescom, COST 273, European Radiocommunications Committee (ERC), Fixed Mobile Convergence Alliance (FMCA), GCF, Global TD-LTE Initiative (GTD), GPS Industry Council, GSM Association, HomeRF Forum, IDB Forum, IEEE, Internet Engineering Task Force (IETF), IrDA, International Multimedia Telecomunications Consortium (IMTC), Internet Streaming Media Alliance, ISO-ITU expert group, ISO MPEG / JPEG, ITU-T SG2, JAIN tm (Javatm APIs for Integrated Networks), The Java Community Process (JCP), Liberty Alliance Project, Metro Ethernet Forum (MEF), NENA, NGMN (Next Generation Mobile Networks), oneM2M, OMA (Open Mobile Alliance ), Open Networking Foundation (ONF), Open IPTV Forum, Object Management Group (OMG), PCS Type Certification Review Board (PTCRB), Portable Computer and Communications Association (PCCA), Presence and Availability Management (PAM) Forum, RSA Laboratories, SDR Forum, Sun Micro Systems Inc., Steerco, SyncML Initiative, Trusted Computing Group (TCG), TeleManagement Forum (TMF), TCCA, TIA /TR45, TIA/TR47, ITU, TV-anytime Forum, Voice eXtensible Mark-up Language (VXML) Forum, Wi-Fi Alliance, Wireless Broadband Alliance (WBA), WLAN Smart Card Consortium, Wireless World Research Forum (WWRF), World Wide Web Consortium (W3C)
(Source: extract from https://www.3gpp.org/about-3gpp/15-bodies-with-which-3gpp-has)
838 companies
3GPP Market Representation Partners (MRPs)
…

## Slide 7: Market Statistics by 3GPP MRP:
The MRPs are a good source of data on the market.

## Slide 8: Technical Specification Groups
The TSGs prepare, approve and maintain the 3GPP Technical Specifications and Technical Reports.
They are responsible for the detailed time frame and management of the work’s progress;
  Management of work items;
  Technical Co-ordination;
  Proposal and approval of work items within the agreed scope and terms of reference of the TSG
The TSG Chair is responsible for the overall management of the technical work within the TSG and its Working Groups.
The WG Chair is responsible for the overall management of the technical work within the WG and its sub-groups.

## Slide 9: Work Schedule driven by technical meetings
New work is initiated by member companies as Work Items, via Tdocs at meetings
Work Items are prioritised and allocated time for discussion during meetings
3GPP member companies may contribute to any work item, on equal terms
3GPP seeks consensus on all technical matters (but has mechanisms if consensus cannot be reached)
The Release deadline is respected. Unfinished work is deferred to a later release

## Slide 10: 3GPP productivity
Chart: 
| R99 | Rel-4 | Rel-5 | Rel-6 | Rel-7 | Rel-8 | Rel-9 | Rel-10 | Rel-11 | Rel-12 | Rel-13 | Rel-14 | Rel-15 | Rel-16 | Rel-17
Nbr of specs | 446 | 516 | 582 | 760 | 875 | 1057 | 1099 | 1041 | 1147 | 1212 | 1266 | 1313 | 1523 | 1648 | 1749
Release-based work
  Releases are major packages of Features (There is a new 3GPP Release ~ every 15 – 24 months)
  A strong commitment to time-lines guarantees reliable planning and time-to-market
  The Work plan is built-up of Work Items that deliver the Features
  Work Items:
    WI may cover more than one specification
    WI may cover more than one TSG or WG
    WI Description document exists for each WI
  Multiple releases are maintained in parallel
See the 3GPP Work Plan for details of features:
    http://www.3gpp.org/Work-Plan
December 2022
Number of specifications (frozen Releases)

## Slide 11: Three stage approach to Features, through Releases
SA2
Architecture
SA6
Apps/MC
RAN
Radio Access
CT – Protocols & Coding
time
Stage 1 Requirements: Overall service description from the user’s standpoint.
Stage 2
Architecture: Overall description of the organization of the network functions to map service requirements into network capabilities.
Stage 3
Protocols: The definition of switching and signalling capabilities needed to support services defined in Stage 1.
SA1
Requirements
SA3
Security
SA4
Media
SA5
OAM

## Slide 12: Bringing the work in to the groups
3GPP Specifications and Reports: | 
Requirements | 21 series
Service aspects ("stage 1") | 22 series
Technical realization ("stage 2") | 23 series
Signalling protocols ("stage 3") - user equipment to network | 24 series
Radio aspects | 25 series
CODECs | 26 series
Data | 27 series
Signalling protocols ("stage 3") -(RSS-CN) and OAM&P and Charging (overflow from 32.- range) | 28 series
Signalling protocols ("stage 3") - intra-fixed-network | 29 series
Programme management | 30 series
Subscriber Identity Module (SIM / USIM), IC Cards. Test specs. | 31 series
OAM&P and Charging | 32 series
Security aspects | 33 series
UE and (U)SIM test specifications | 34 series
Security algorithms | 35 series
LTE (Evolved UTRA), LTE-Advanced, LTE-Advanced Pro radio technology | 36 series
Multiple radio access technology aspects | 37 series
Radio technology beyond LTE | 38 series
Use Case diversity
High or Low data rates
Higher user mobility
Improved coverage
Overall System Goals
Enable new business
Greater efficiency
More flexibility – not one-size-fits-all
3GPP Working Groups

## Slide 13
5G Releases
Release15: The work on new radio (nr) and the 5G system (5GS) jointly addressed the urgent subset of needs for early commercial deployments.
Release16: Met all identified 5G use cases, to allow a full 3GPP IMT-2020 submission to ITU-R.
Release 17: Enhances the earlier 5G work, meeting more 'vertical' industry needs, specifying NR operation in unlicensed bands, NR MIMO, V2-everything.
Release 18: The current focus of the groups, scheduled for completion during 2024. Rel-18 will see a balanced evolution in terms of:
  Mobile broadband evolution versus further vertical domain expansion;
  Immediate versus longer-term market needs;
  Device evolution versus network evolution.
  5G-Advanced is a mid-generational marker (covers Rel-18, 19, 20)
Release 19: From 2024
6G mobile systems come later. 6G time-to-market expected to be 2030.
Notes: 10/31/16

## Slide 14
Graphic adapted from original data in SP-230738 Work Plan report to TSG SA#100

## Slide 15: E-Meetings & Release Schedules
December 2019, TSG SA#90 (Sitges) agreed a firm Rel-17 schedule (see image right)
2020-05-15, 3GPP PCG activated annex I “Special procedures for exceptional situations restricting travel”.
E-meetings and COVID-19 have challenged the ability of the groups to complete all Rel-17 work in the time allowed. Groups completed down-scaling of some feature work for freeze dates to be met.
3GPP Rel-18 online workshops completed with package content (features) and timeline agreed.
  TSG RAN e-Workshop was held June 28 – July 2. See website article “Advanced plans for 5G”
  TSG SA (overall architecture and service capabilities) Workshop was held as an e-meeting Sept 9 – 10.
  TSG#93-e (September)Agreed Rel-18 timeline (right).
  Prioritization and content confirmed at TSG#94-e (December 2022)
Overview

## Slide 16: E-Meeting time planning (RAN example)
eMeetings are working Across all time zones
The number of meeting days have been extended to allow for email discussion
GoTO Webinar used for real-time discussions
Discussions are split into Initial, Intermediate, Final and Extended periods

## Slide 17: Emails during e-meeting era
Chart: Number of emails in LISTSERV / year
| 2017 | 2018 | 2019 | 2020 | 2021*
 | 137486 | 110304 | 175192 | 433431 | 363825
*up to 09/12/2021
Source: MCC Report to Plenary, December 2021

## Slide 18: Rel-19 Workshops I (June 2023)
TSG SA (SP-230765)
65 contributions.
SA identified 17 "core" and 15 "miscellaneous" potential topics for Rel-19.
The next step involves SA2 undergoing Moderated Email Discussion (MED) in August to define study/work items on “core” items to be submitted to SA#101 (Sep.) for approval.
The remaining core items and miscellaneous subjects will be further discussed in SA2 in Q4, 2023 for final Rel-19 content approval in SA#102 (Dec.).
TSG RAN (RWS-230488)
~480 submissions.
Presentations and Q&A focusing on RAN1/2/3-led items.
Focus on 5G-Advanced to further improve performance and address critical commercial deployment needs.
Release 19 to serve as a bridge to 6G - Strong interest to initiate some studies (e.g., channel modelling for new spectrum such as 7-24GHz, etc.)
The overall Rel-19 load is expected to be lower than Rel-18 load

## Slide 19: Rel-19 Workshops II (June 2023)
TSG SA (SP-230765, SP-230759)
Guidance to SA2 on Rel-19 work planning:
Headline “core” topics: Satellite Access, Ambient IoT, AI/ML enh., Multi-access (Dual 3GPP + ATSSS Enh), Energy Efficiency / Energy Saving as a Service, XRM and Metaverse, IMS and NG_RTC enh.
If SIDs approved in SA#101 (Sep.) then work can start Q4 2023.
Final decision on the complete set of SIDs for Rel-19 taken in SA#102 (Dec. 2023).
TSG RAN (RWS-230488)
Categorization of the topics for better management in RAN#101 (Sep. 2023).
All topics are subject to further discussion and justification.
Categorization of major topics under: AI/ML Air Interface, MIMO Evo., Duplex Evo., Ambient IoT, Network Energy Saving Enh., Mobility Enh., NTN Evo., XR Evo., AI/ML for NG-RAN, SON/MDT, Channel Modeling (& possibly additional aspects e.g. for ISAC) for further evol.
Plus, other RAN1, RAN2 & RAN3 led topics.
Plus, others listed in RWS-230488 slide 7.

## Slide 20: 3GPP TSG SA WG4 (SA4)
SA WG4 – Multimedia Codecs, Systems and Services
Within the 3GPP Technical Specification Group Service and System Aspects (SA), the main objectives of the 3GPP TSG SA WG4 (SA4) are the specifications of codecs for speech, audio, video, graphics and other media types related to emerging services such as extended realities (XR) and gaming, as well as the system and delivery aspects of such contents.
These objectives includes defining content formats and delivery protocols for unicast, multicast and broadcast streaming, cloud and edge computing architectures, media APIs, media handling in multimedia telephony, terminal acoustics requirements and performance testing, end-to-end service performance, objective and subjective quality testing, quality of experience (QoE) metrics, definition of traffic characteristics for media services, reporting for all services involving media aspects, and the use of artificial intelligence and machine learning models for multimedia.
SA WG4 is currently responsible for the XR-based services and traffic characteristics, Next Generation Video for 5G, Media Distribution over 5G unicast/multicast and broadcast, Media Cloud and Edge Processing in 5GS, Glass-based Augmented Reality, VR conferencing, Immersive Voice and Audio Services and Extension for headset interface tests of UE.

## Slide 21: SA4 participants (Nov. 2023)
Operators/Service providers: AT&T, Facebook/Meta, NTT, BBC, Verizon, Vodafone, Tencent, China Mobile, Orange, Telecom Italia, KPN, China Unicom, China Telecom, Rogers, USDoD, Deutsche Telekom, Douyin.
OEM/Chipset vendors: Qualcomm, Samsung, Xiaomi, MediaTek, Vivo, Apple, Panasonic, Futurewei, Lenovo, LG, Motorola, Oppo.
Network vendors: ATEME, Nokia, Ericsson, ZTE, Huawei, Intel, Convida, CableLabs.
Tech providers: Dolby, Interdigital, Fraunhofer IIS & HHI, ETRI, VoiceAge,
Labs/Test: Mesaqin, Head acoustics, DTS/Xperi, Philips, Pencheng labs.

## Slide 22: Ongoing Audio topics – Rel-18/19
New 3GPP codec for Immersive Voice and Audio Services (IVAS) – Rel-18 - see next slides: The overall objective of this work item is to develop a single general-purpose audio codec for immersive 4G and 5G services and applications including the XR use cases envisioned in 3GPP TRs 26.918 and 26.928.
Terminal Audio quality performance and Test methods for Immersive Audio Services (ATIAS) – Rel-18: The overall objective of this work item is to develop a set of test specifications for objective characterization of terminals for 3GPP immersive services. This covers both conversational services based on Multimedia Telephony / telepresence and non-conversational services (e.g. streaming, messaging).
Enhancements to UE Testing (eUET) – Rel-18: Define missing SWB frequency masks and review related UE acoustic test methods. Update "Jitter buffer management behavior" and "Test conditions" for jitter buffer management. Develop a new specification to verify correct implementations of the RTP payload format for 3GPP codecs. Review receiving performance of UEs at maximum volume control and define, if necessary, requirements and test methods to ensure an adequate user experience.
Immersive Audio for Split Rendering Scenarios (ISAR) – Rel-18: The overall objective of this work item is to develop solutions for immersive binaural audio on head-tracked devices that are compatible with the envisaged split architectures (TR 26.998). The solutions should consider low-complex and lightweight devices and demonstrate operational benefits over solutions with full decoding and rendering in the end device.
Study on Diverse audio Capturing system for End-user Devices (FS_DaCED) – Rel-19: This study item considers codec-independent immersive voice and audio capturing configurations for end-user devices. The outcome of the studies can be used as guidelines for the manufacturers to deploy immersive voice and audio services.

## Slide 23: IVAS Codec Work Item Details
IVAS Codec is an extension of the 3GPP EVS (Enhanced Voice Services) codec
  Targets completion by mid 2024 (Rel-18)
  IVAS floating-point code approved in September 2023
  IVAS main specifications for approval in March 2024
  IVAS fixed-point code approval expected in June 2024
  IVAS Codec characterization expected during Summer 2024
There are 12 IVAS_Codec work item supporters in 3GPP:
  The supporters are major telecom industrial players
    Operators
    Chipset & Tech vendors
    Terminal vendors
    Infra vendors
13 companies (11 contributors, 2 observers) have jointly developed the IVAS Codec under the framework of the IVAS Codec Public Collaboration that was open to any 3GPP member
IVAS
Public Collaboration

## Slide 24: IVAS: Features and Properties
  Complexity/RAM:
    Level 1: <= 3 * EVS
      Up to 80kbps (for most formats)
    Level 2: <= 6 * EVS
      Up to 256kbps
    Level 3: <= 10 * EVS
      Up to 512kbps
    Note: Supported bit rates for given levels are approximate and subject to IVAS Codec characterization
Input formats and supported bitrates
IVAS input formats | Supported bitrates (kbps)
Mono (100% EVS compatible/interoperable mode) | 5.9 - 128
Stereo/binaural | 13.2 – 256
SBA (Ambisonics, order 1 to 3) | 13.2 - 512
MASA (Metadata-assisted spatial audio) | 13.2 - 512
Multichannel (5.1 to 7.1.4, flexible layouts) | 13.2 - 512
ISM (Object Audio, 1-4 objects) | 13.2 – 256
End-to-end audio latency [ms]
32
32
33/38
37
32/37
32/37
Characteristics
  Supported input/output sampling rates: 16 kHz, 32 kHz, 48 kHz
    Supported audio bandwidths: NB (EVS only), WB, SWB, FB
  Head-tracked binaural split rendering
  Combined audio formats (SBA + Objects, MASA + Objects)
More information available in 3GPP Highlights Issue 7 (Nov 2023) and Issue 5 (Nov 2022)

## Slide 25: Ongoing MBS topics – Rel-18/19
Split Rendering Media Service Enabler (SR_MSE) – Rel-18: This work item will develop a Media Service Enabler that packages all the required enablers and defines the required formats and protocols to make split rendering accessible to media service and application providers. The package is aligned with the philosophy of Media Service Enablers and envisions deployments as an SDK that is offered to application developers.
5G-Advanced media PROfiles for MessagIng Services (PROMISE) – Rel-18: The purpose of this Work Item is to specify SMS/MMS/RCS/Messaging formats and codecs that GSMA and other organizations or application vendors can then reference and/or profile to improve messaging service quality and interoperability. See next slide.
5G Media Streaming Protocols Phase 2 (5GMS_Pro_Ph2) – Rel-18: The work item addresses stage-3 support for 5GMS protocol extensions for provisioning, ingest, user plane, control plane and device APIs for the following functionalities: uplink streaming, end-to-end low latency live streaming, 5GMS over MBS and 5GMS hybrid services , support for multiple media service entry points, traffic identification, Addition of HTTP/3 to the 5GMS protocols, Background Data Transfer, usage of Oauth 2.0, 3GPP Service Handler and URL, enhancements based on feedback from 5G-MAG Reference tool developments, Specification of data types for data reporting of ANBR-based Network Assistance invocations.

## Slide 26: 5G-Advanced media PROfiles for MessagIng Services (PROMISE)
MMS media formats were specified by 3GPP in TS 26.140 20+ years ago (Rel-5). SMS/MMS is still a very popular service with universal support, interoperability and roaming. SMS/MMS is used as fallback to GSMA RCS. It needs upgrading.
GSMA specified RCS (Rich Communication Services) which is now deployed by operators and Google. “5G Messaging” is being introduced in China based on MMS/RCS profiles.
OTT Messaging applications can benefit from interoperability and e2ee encryption – IETF is conducting “More Instant Messaging Interoperability (MIMI)” work to enable this.
Enable RCS and OTT messaging apps to reference new 3GPP TS 26.143 Messaging Media profiles.
Supporting companies: Dolby, Fraunhofer IIS, Ericsson, Nokia, Qualcomm, Interdigital, AT&T.
Upgrades:
  Add EVS codec support with SWB and FB support for speech messages
  Add xHE-AAC codec support for audio messages
  Add IVAS codec for spatial speech/audio messaging.
  Add 3d scenes and assets messages
  Upgrade 2D video support
Triggered by 3GPP SA4 liaison, MPEG (ISO/IEC SC 29/WG 3) will define a profile of ISOBMFF for the purpose of messaging (MeMAF), which will match SA4 requirements.
GSMA UPG/GSG regular liaison exchange

## Slide 27: Ongoing Video topics – Rel-18/19
Media Capabilities for Augmented Reality (MeCAR) – Rel-18: Define at least one AR device category that addresses the constraints of an EDGAR-type AR glass. Integrate IVAS once available. Define capability exchange mechanisms based on complexity of AR media and capability of device to support EAS KPIs for provisioning of edge/cloud resources. Identify QoE metrics and KPIs for AR media. Specify encapsulations into RTP, ISOBMFF and CMAF. Specify the relevant codec-level parameters for session setup. Enable AR media in 5G Media Streaming. Define typical traffic characteristics for AR media.
Feasibility Study on Artificial Intelligence (AI) and Machine Learning (ML) for Media (FS_AI4Media) – Rel-18: The objectives of the study item are primarily to identify relevant interoperability requirements and implementation constraints of AI/ML in 5G media services.
Feasibility Study on AR and MR QoE Metrics (FS_ARMRQoE) – Rel-18: Collect relevant external information on QoE Metrics for AR and XR services. Conduct subjective tests on XR QoE metrics, if considered relevant. Collect a set of relevant XR QoE Metrics and define their impact on the user experience. Based on a well-defined device architecture based on MeCAR, define the relevant observation points and define the measurement and derivation of relevant XR QoE metrics. Study the support of XR QoE metrics in 3GPP metrics collection frameworks such as NWDAF, RRC-based metrics configuration and collection, etc. Provide recommendation on normative work for new XR QoE metrics based on the findings in this study.
Feasibility Study on Film Grain synthesis (FS_FGS) – Rel-18: This study aims to evaluate use of Film Grain Synthesis (FGS) in 5G video services.
Feasibility Study on new HEVC profiles and operating points (FS_HEVC_Profiles) – Rel-18: This study aims to Identify and evaluate the opportunities for improving HEVC-based services.
Feasibility Study on Avatars for Real-Time Communication (FS_AVATAR) – Rel-18/19: Based on relevant TR 22.856 use cases, the study item aims, among other objectives, to collect and document Avatar animation and representation approaches, document the requirements for an interoperable base Avatar format.

## Slide 28: Ongoing RTC topics – Rel-18/19
Immersive Real-time Communication for WebRTC (iRTCW) – Rel-18: Define a non-vertical/modularized protocol stack, functional components, I/Os formats, for iRTC clients to support WebRTC-based real-time transport of media over 5G; Identify the required architecture for radio access network QoS realization over 5G systems. Identify the minimum information / elements in the C/U-Plane signal to establish media sessions with appropriate QoS for WebRTC-based applications. Document informative examples of iRTC operations to assist implementers.
IMS-based AR Conversational Services (IBACS) – Rel-18: The objective of this work item is to create a new specification for IMS-based AR conversational services. The features for RTP-based real-time communication, which can be used by IMS and non-IMS (AR) conversational services, will be specified in another new specification (as part of the 5G_RTP work). The relevant features and functional components specified for MTSI in TS 26.114 will be referenced and/or enhanced, if required.
5G Real-time Transport Protocols (5G_RTP) – Rel-18: The objective of this work item is to specify functionalities of RTP to improve support for traditional and immersive real-time services and enablers. To develop a commercially relevant set of functionalities that only include technologies that are either commercially relevant or deployed or demonstrate clear performance or relevant functionality that justifies introducing additional implementation or interoperability complexity.
Enhanced Multiparty RTT (MP_RTT) – Rel-18: This WI will specify suitable solutions for multiparty RTT media in IMS, for both RTP and IMS data channel transport, focusing on the transport format and procedures in IETF RFC 9071
Feasibility Study on the enhancements for immersive Real-time Communication for WebRTC (FS_eiRTCW) – Rel-18: In addition to the foreseen approach identified in TR 26.998 (Support of 5G glass-type AR/MR devices) and taken in WID on iRTCW (immersive Real-time Communication for WebRTC), which leaves C-plane signalling details open and simply makes use of the northbound APIs for end-to-end QoS), the possibility of another approach (i.e., defining a set of advanced details (including C-plane signalling) for the common and wider use among several WebRTC implementations) will be investigated under this SID.

## Slide 29: SA4 Typical F2F meeting schedule

## Slide 30: SA4 Typical e-meeting schedule

## Slide 31: SA4 leadership and subgroups
SA4 officials:
  Chair: Frédéric Gabin (Dolby Laboratories Inc. , ETSI)
  Vice Chairs:
    Gilles Teniou (Tencent, CCSA)
    Jaeyeon Song (Samsung Electronics Co., Ltd, TTA)
  Secretary: Antoine Burckard (ETSI/MCC Support)
Sub Working Groups and their Chairs – allows breakout sessions

## Slide 32: Working Group reminders

## Slide 33: SA4 Calendar 2024

## Slide 34: SA4 Calendar 2025

## Slide 35: Concluding thoughts
3GPP is industry driven - Standardization of interfaces enables an interoperable, multi-vendor approach to deployment.
The 3GPP processes are necessarily complex, but we will adapt to bring new sectors in to the work.
Release 19 content and priorities discussion ongoing. NOW is the time to influence this work.
Release 18 and Release 19 will have an important role in helping to lay early foundations for future work on 6G technologies.

## Slide 36: For more info on 3GPP…
www.3gpp.org/contact
www.3gpp.org/highlights
All documents available online; www.3gpp.org
Attend special newcomers sessions at F2F Plenary meetings
Subscribe to our regular newsletter ‘Highlights’
Keep in touch;
  Info, membership, marcom, liaisons;
Issue 6 - 3GPP Newsletter
May 2023
www.3gpp.org