## Slide 1: Response to New Draft SID on Evaluation of VVC and AV1 Codecs

## Slide 2: Context
On July 22, Vodafone shared a draft study proposal on the SA4 mailing list as follows
  As we had conversation on previous meeting, I’m going to introduce new study item for evaluation on new Codecs at August meeting.
  I wanted to introduce this Study Item offline So that I can gather comments and thoughts on it from you all. And if you’ll support this Study we can move forward.
  It’s open for all suggestions and if you want to add or delete some parts.
This document reviews the study item description and provides some responses.

## Slide 3: Comments on Justification (1)
In previous Study at 26.995 the only test and evaluation metric used was BD gain using PSNR.
  The study is documented in TR 26.955
  It is not correct that only the BD Rate gains using PSNR were used. The BD Rate gains for the following metrics were also provided
    For SDR sequences: y_psnr, psnr, ms_ssim, vmaf
    For HDR sequences: y_psnr, psnr, wpsnr, PSNRL100, DE100
Which for new Study it’ll be aside from BD gain, bitrate saving and complexity in terms of power consumption of encoder and decoder side.
  BD Rate gains provide a means to measure bitrate savings in a consistent and widely agreed manner
  We address the issue on complexity and power consumption in a different discussion later
Aside from standalone codec effectivity, impact of ABR (DASH) and AI4Media compression also to be tested to come out on which Codec these compressions would act more efficiently.
  ABR was considered as one of the scenarios.
  AI4Media is a new study in 3GPP SA4, but no conclusions are drawn yet

## Slide 4: Comments on Justifications (2)
As per Scenarios same as previous study below ones can be used but it’s open discussion to add any other Scenario recommended.
  The TR was always considered to add new scenarios if proposed properly – more details later
Metrics to be decided for tests (bitrate saving, BD gain (PSNR/SSIM), Complexity(Complexity (power consumption)),
  The TR already contains information on bitrate savings for different metrics
Quality to be decoded for Tests: is it feasible Using CRF instead of QP for Quality at tests? (Meta recommendation).
  The TR decided to use a specific set of reference software for each codec and there was a detailed discussion on using specific configuration for each reference software. If different settings are considered more appropriate, then new tests may be added. At this stage it is unclear why we would need different settings.
GOP size to be Decided for Tests.
  The TR decided to use GOP sizes for each scenario that were well justified. If there is new information on this not having been fully appropriate, concrete new proposals would be needed.

## Slide 5: Comments on Justifications (3)
Scenario 1: Full HD Streaming, as well as 360p, 540p, 720p, 1080p to see ABR efficiency on each Codec for each resolution.
  The addition of different resolutions was discussed during the study, but considered to be too complex to create value
  Issues addressed are: down- and upsampling filters, metrics for subsampled versions, defining ladders for each codecs, weighting of different resolutions, addressing codecs that allow resolution resampling and so on.
  A very concrete justification why this extended test is needed and how to conduct would be needed.
Scenario 2: 4K-TV
Scenario 3: Screen Content Scenario (Screen Sharing)
Scenario 4: Messaging and Social Sharing
Scenario 5: Online Gaming
  All the remaining scenarios seem to be identical to the ones in TR 26.955.
Scenarios

## Slide 6: Comments on Objectives (1)
The study aims to investigate and identify the best Codec (among VVC and AV1) to be used in telco Network for Media Services like Video streaming, Metaverse related Services (AR/XR services, Avatars), IMS based immersive Services (media sharing during interactive calls, Video resolution upscaling, AR/XR services, Avatars) …
  This objective reads as the proposed study is addressing a codec selection. Most of the work already completed
Identify Best Performance Codec in terms of Bitrate Saving
  Already addressed in TR 26.955  VVC
Identify Best Performance Codec in terms of Compression ratio.
  Already addressed in TR 26.955  VVC
Identify Best Performance Codec in Terms of BD gain.
  Already addressed in TR 26.955  VVC
For possible new scenarios, it would be encouraging to bring more details on the envisaged scenarios. This would include reference sequences, metrics, anchor configurations and so on

## Slide 7: Comments on Objectives (2)
Identify Best Performance Codec in terms of Complexity (Coding and Encoding sides) and effect of power consumption.
Encoding and Decoding impact and best performance Codec on Mobile Devices for user generated Media and sharing.
TR 26.955 already address encoding and decoding complexity by properly setting the configuration parameters including profiles/levels/search ranges/multi-path encoding and many other aspects. Hence, the experts considered the results fully comparable
Power consumption and complexity is very implementation-specific and a generic analysis by 3GPP is not suitable. Core implementors had been participating when defining new codecs and ensure that they are implementable on mobile platforms.
At this stage we do not see any missing aspects to be addressed.
Complexity analysis

## Slide 8: Comments on Objectives (3)
Identifying features and characteristics of the new Codecs (eg: leyerd scalability)
The TR States that HEVC has no functional deficiencies. It would be good to understand if there are any new indications for functional deficiencies that require a new codec.
New functionalities

## Slide 9: Timeline
The study item proposal does not include any timeline, or any details on the time plan
However, we would expect that the work needs to be carried out in the Video SWG, which is already overloaded for Rel-19 with 1 normative work, and 6 study items.
Hence, we do not see any reasonable way to allocate time and complete the study in Rel-19

## Slide 10: Summary
It seems that the proponent would like to extend the characterization done in TR 26.955 with some additional aspects, for example
  Definition of new scenarios
  Updates to reference software and new configuration parameters
  Possibly updated metrics
However, at this stage it is unclear what exactly is missing in TR 26.955. More concrete information would be needed to understand the amount of considered work. This would include:
  Concrete new scenarios, including reference sequences, metrics and so on
  Extensions to existing scenarios, what exactly needs to be done
  Concrete commitments by companies to support the work to be executed.
  Concrete time plans, as well as some indication what the expected outcome towards normative work would be
Based on the unclear justification and objectives, as well as the overload in SA4 and in particular in the video SWG, Qualcomm is not supportive to the proposal at this stage.