## Slide 1
Tdoc S4-140914
Basic SDP Parameters of EVS
3GPP SA4#80
August 4-8, 2014, San Francisco, California, U.S.
Agenda Item: 7
Source: Samsung Electronics Co., Ltd.
Document for: Discussion
Contact: Kyunghun Jung
E-mail: kyunghun.jung@samsung.com

## Slide 2
Changing Network Environments
Representing Bandwidths & Bit-Rates
Bandwidth Negotiation
Bit-Rate Negotiation
DTX Control
SDP Offer/Answer Example
Content

## Slide 3
Changing Network Environments
  Current procedures for session negotiation, like no mode-set in SDP offer, are defined in Rel-7, with only MTSI client in terminal and MGW in mind
  The lowest-end 3GPP access technology in TS 26.114 V12.6.0, EGPRS, can support the maximum bit-rates of AMR and AMR-WB in good channels
  As E-UTRAN and EPC were introduced to MTSI, SGSN and GGSN were replaced with a more generic term, PS Domain, from Rel-10
  In Rel-12, MTSI client in terminal using fixed access was introduced, which may require higher but fixed bit-rates and bandwidths, e.g., 64 kbps at WB
  In Rel-12, EVS was introduced, whose highest bit-rate is twice the transport capability of EDGE (maximum 61.85 kbps at MCS-9, no channel coding)
  EVS supports dual-mono (or stereo), whose parameters reflecting local situations need to be taken into account in session negotiation (SDP offer)
  Support of multi-channel necessitates asymmetric bit-rate/bandwidth negotiation, e.g., when only a UE is connected to a stereo headset

## Slide 4
Representing Bandwidths & Bit-Rates
Codec Type | Source Bandwidth (Hz) | Sampling Rate (samples/s) | Bit-rate (kbps)
Narrow Band (NB) | 20 ~ 4,000 | 8,000 (nb) | 5.9, 7.2, 8, 9.6, 13.2
Wide Band (WB) | 20 ~ 8,000 | 16,000 (wb) | 5.9, 7.2, 8, 9.6, 13.2, 16.4, 24.4, 32, 48, 64, 96, 128, AMR-WB Interoperable Mode (6.6~23.85)
Super Wide Band (SWB) | 20 ~ 16,000 (14,000*) | 32,000 (swb) | 9.6, 13.2, 16.4, 24.4, 32, 48, 64, 96, 128
Full Band (FB) | 20 ~ 20,000 | 48,000 (fb) | 16.4, 24.4, 32, 48, 64, 96, 128
  Each codec mode of EVS AMR-WB IO mode can be represented with 0, …, 8 as in the legacy AMR-WB
  To avoid confusion with EVS AMR-WB IO mode, and to save space in SDP, bit-rate in kbps can be used to represent the bit-rates of EVS Primary mode
  Representing bit-rate in kbps also increases readability, making (human) inspection of SDP easier
  In general, higher bit-rates match higher bandwidths, and vice versa
  With a large bandwidth range of nb-fb, the range may be partitioned into smaller ranges that match the bit-rates of each payload type
  Bandwidths can be compactly represented as bw1 when a bandwidth is used, and bw1-bw2 when equal to or more than two bandwidths are used
  When equal to or more than two bandwidths are used, the lowest bandwidth is nb
  When representing more than two bandwidths, bw1-bw2 will be more economical than bw1, …, bw2 or other expressions
  With a large bit-rate range of 5.9-128 kbps, service plan may partition the range into smaller ranges for each payload type
  Bit-rates can be compactly represented as br1 when a bit-rate is used, and br1-br2 when equal to or more than two consecutive bit-rates are used
  When representing equal to or more than three consecutive bit-rates, br1-br2 will be more economical than br1, …, br2 or other expressions
  Multiple ranges of bit-rates can be offered with multiple payload types, each of which can be defined for radio, fixed, multi-channel, …
  Bit-rates and bandwidths of EVS Primary mode need to be represented in a compact and consistent fashion, for send and receive directions separately

## Slide 5
Bandwidth Negotiation
Parameter | Location | Definition
bw-send | Definition | Specifies the bandwidth to be used in the session for the send direction. bw-send has a value from the set: nb, wb, swb, fb, nb-wb, nb-swb, and nb-fb. nb, wb, swb, and fb represent narrowband, wideband, super wideband, and fullband respectively, and nb-wb, nb-swb, and nb-fb represent all bandwidths from narrowband to wideband, super wideband, and fullband respectively. If not present, all bandwidths are supported.
 | Handling | When bw-send is not offered for a payload type, the answerer may include bw-recv for the payload type in the SDP answer. If bw-send is offered for a payload type which is accepted, the answerer shall include bw-recv in the SDP answer, and the bw-recv shall be a subset of bw-send for the payload type in the SDP offer.
bw-recv | Definition | Specifies the bandwidth to be used in the session for the receive direction. bw-recv has a value from the set: nb, wb, swb, fb, nb-wb, nb-swb, and nb-fb. nb, wb, swb, and fb represent narrowband, wideband, super wideband, and fullband respectively, and nb-wb, nb-swb, and nb-fb represent all bandwidths from narrowband to wideband, super wideband, and fullband respectively. If not present, all bandwidths are supported.
 | Handling | When bw-recv is not offered for a payload type, the answerer may include bw-send for the payload type in the SDP answer. If bw-recv is offered for a payload type which is accepted, the answerer shall include bw-send in the SDP answer, and the bw-send shall be a subset of bw-recv for the payload type in the SDP offer.
TS 26.114 Status | 
UE Support | Use
Mandatory | Optional

## Slide 6
Bit-Rate Negotiation
Parameter | Location | Description
br-send | Definition | Specifies the range of bit-rate, in kilobits per second (excluding RTP, UDP, and IP overhead), to be used in the session for the send direction. Possible value is a hyphen-separated pair of two bit-rates, br1-br2, where br1 is smaller than br2. br1 and br2 have a value from the set: 5.9, 7.2, 8, 9.6, 13.2, 16.4, 24.4, 32, 48, 64, 96, and 128. 5.9 represents the bit-rate of source controlled variable bit-rate (SC-VBR) coding, and 7.2, …, 128 represent the bit-rates of constant bit-rate source coding. If a single bit-rate is used in the session, br-send is set to the bit-rate. If not present, all bit-rates are supported.
 | Handling | When br-send is not offered for a payload type, the answerer may include br-recv for the payload type in the SDP answer. If br-send is offered for a payload type which is accepted, the answerer shall include br-recv in the SDP answer, and the br-recv shall be a subset of br-send for the payload type in the SDP offer.
br-recv | Definition | Specifies the range of bit-rate, in kilobits per second (excluding RTP, UDP, and IP overhead), to be used in the session for the receive direction. Possible value is a hyphen-separated pair of two bit-rates, br1-br2, where br1 is smaller than br2. br1 and br2 have a value from the set: 5.9, 7.2, 8, 9.6, 13.2, 16.4, 24.4, 32, 48, 64, 96, and 128. 5.9 represents the bit-rate of source controlled variable bit-rate (SC-VBR) coding, and 7.2, …, 128 represent the bit-rates of constant bit-rate source coding. If a single bit-rate is used in the session, br-recv is set to the bit-rate. If not present, all bit-rates are supported.
 | Handling | When br-recv is not offered for a payload type, the answerer may include br-send for the payload type in the SDP answer. If br-recv is offered for a payload type which is accepted, the answerer shall include br-send in the SDP answer, and the br-send shall be a subset of br-recv for the payload type in the SDP offer.
TS 26.114 Status | 
UE Support | Use
Mandatory | Optional

## Slide 7
DTX Control
Parameter | Location | Definition
dtx-off | Definition | Indicates that discontinuous transmission (DTX) is not used in the session. If not present, DTX is used.
 | Handling | If offered, dtx-off shall not be removed.
TS 26.114 Status | 
UE Support | Use
Mandatory | Optional

## Slide 8
SDP Offer/Answer Example
  This example shows the SDP offer when the session is initiated from MTSI client in terminal using fixed access, which supports AMR with the {12.2, 7.4, 5.9 and 4.75} codec mode set and AMR-WB with the {12.65, 8.85 and 6.60} mode set. In addition, EVS, G.722, and PCM codecs are supported.
  For EVS, RTP Payload Types 97 and 98 are defined, for example, to initiate a speech session with another MTSI client in terminal using fixed access supporting a bit-rate of 64 kbps or radio access supporting all bit-rates from 5.9 to 24.4 kbps.
SDP offer (IPv4)
m=audio 49152 RTP/AVP 97 98 99 9 100 0 8 a=tcap:1 RTP/AVPF a=pcfg:1 t=1 b=AS:80 b=RS:0 b=RR:2000 a=rtpmap:97 EVS/16000/1 a=fmtp:97 br-send=64; br-recv=64; bw-send=wb; bw-recv=wb; dtx-off; max-red=220 a=rtpmap:98 EVS/16000/1 a=fmtp:98 br-send=5.9-24.4; br-recv=5.9-24.4; bw-send=nb-swb; bw-recv=nb-swb; max-red=220 a=rtpmap:99 AMR-WB/16000/1 a=fmtp:99 mode-set=0,1,2; max-red=0 a=rtpmap:100 AMR/8000/1 a=fmtp:100 mode-set=0,2,4,7; max-red=0 a=rtpmap:9 G722/8000/1 a=rtpmap:0 PCMU/8000/1 a=rtpmap:8 PCMA/8000/1 a=ptime:20 a=maxptime:80
(1) SDP answer (IPv4)
m=audio 49152 RTP/AVP 98 b=AS:41 b=RS:0 b=RR:2000 a=rtpmap:98 EVS/16000/1 a=fmtp:98 br-send=13.2-24.4; br-recv=13.2-24.4; bw-send=nb-swb; bw-recv=nb-swb; max-red=220 a=ptime:20 a=maxptime:240
(2) SDP answer (IPv4)
m=audio 49152 RTP/AVP 97 b=AS:80 b=RS:0 b=RR:2000 a=rtpmap:97 EVS/16000/1 a=fmtp:97 br-send=64; br-recv=64; bw-send=wb; bw-recv=wb; dtx-off; max-red=220 a=ptime:20 a=maxptime:240