## Slide 1: Applying the EVS Onion Principle
3GPP TSG SA4 Meeting #85 S4-151009
Kobe, Japan, 24-28 August 2015
Source: Ericsson LM
Title: Call Setup and Handover Scenarios for EVS
Document for: Discussion
Agenda Item: 10.6.1

## Slide 2: The EVS Onion Principle (see also S4-150858)
The table at the left shows all bandwidths and bit rates for EVS-Primary mode of operation. Each table entry has a "speaking name", defining audio bandwidth (bw) and the bit rate index (0...11). Each bit rate index corresponds to a certain bit rate. Empty table entries are not defined. In this paper the term "mode" refers to the combination of bandwidth plus rate.
Each "EVS (primary) Onion" is fully specified and named by its "upper right corner" in this table. The biggest EVS Onion is called EVS-FB-11 and comprises all defined EVS (primary) modes.
The EVS Onion principle mandates that all modes (bandwidths and rates) in that table "left and below" the upper right corner are included in the EVS Onion with that name. All possible EVS Onions (in total 35) are TrFO-compatible to each other.
The table on the right shows all bit rates of the EVS-IO mode of operation, corresponding one-by-one with the AMR-WB modes. All 9 EVS-IO Onions are TrFO-compatible to each other. The biggest is EVS-IO-8. The EVS-IO Onions are not TrFO-compatible to the EVS-Primary Onions. Therefore the EVS-IO is always included in the EVS Codec.
The complete EVS (Primary) Onion
The complete EVS-IO Onion

## Slide 3: Three important EVS Onions
These three EVS Onions A, B, C represent the current Working Assumption (WA) for EVSoCS for three different Spreading Factors.
EVS Onion C has about the same radio resource requirement as AMR-WB(all modes) and EVS Onion B has about the same radio resource requirements as AMR(0,2,4,7).
EVS Onion A is a high capacity, decent quality Onion for overload situations.
The actual network conditions define (by rate- and band-control) the highest rate and bandwidth to be used at a certain moment.
Of course these three EVS-Onions are also suitable for VoLTE calls.
EVS Onion C for Spreading Factor SF=64 (WA) (including EVS-IO-2)
EVS Onion B for Spreading Factor SF=128 (WA) (including EVS-IO-2)
EVS Onion A for Spreading Factor SF=256 (WA) (including EVS-IO-0)

## Slide 4: One example for an EVS NON-Onions
If, however, marginal radio resources or another "hard" link limitation in the path would require even lower rates, then the EVS-SWB-8 Onion provides the best possible conditions to maintain the call.
The EVS-SWBOnly-8 NON-Onion would either go muting, if the bottleneck is really hard, or increase the frame error rate, if the lowest rate is not sufficiently robust on the marginal radio channel.
In case one side enters audio conditions with smaller output-bandwidth, e.g. after handover to a NB-only access, then EVS-SWB-8 can follow optimally and tailor the available bit rate to the needed bandwidth at the remote receiver.
The NON-Onion would continue to send in SWB, which must then be bandlimited, wasting resources on irrelevant signals.
EVS-SWBOnly-8 NON-Onion for SuperWideband up to 48 kbps without fall-back options to lower bandwidths (at least the EVS-IO-2 is included, not shown)
EVS-SWB-8 Onion for SuperWideband up to 48 kbps, with fall-back option to all lower rates and bandwidths (at least EVS-IO-2 is included, not shown)
Both EVS Configurations require the same radio resources for the best possible quality.
Both EVS Configurations can be rate controlled down to 9.6 kbps, while still maintaining SWB quality.

## Slide 5: Exotic EVS Onions
This "exotic" EVS-WB-9 Onion is TrFO-compatible to all other EVS-Onions.
If it is used end-to-end, e.g. in a VoLTE<==>VoLTE call, then it provides HD voice quality on high level on "ISDN-like channels" with 64 kbps and decent HD Voice quality down to low rate channels, without the need to switch to narrowband.
But at Call setup it is typically impossible to know, which route the call may take and were it may terminate.
It may well be that this EVS-WB-9 Onion is sent in SIP Invite from a network node, but the answer is EVS-NB-4, e.g. if the call terminates at a legacy wireline PSTN phone. This call setup would be reasonable and cost efficient, knowing that the wireline side won't change.
Sending the EVS-WBOnly-9 NON-Onion in the Invite would not allow this answer.
On the other hand even a VoLTE<=>VoLTE call may need SRVCC to a 2G radio access with - let's assume - AMR support. In that case it seems most reasonable falling back to EVS-NB-6, let's say for best possible NB quality.
The EVS-WBOnly-9 NON-Onion would not provide better quality, maybe even worse, at maybe higher cost.
EVS-WB-9 Onion (including at least EVS-IO-2)

## Slide 6: Simple VoLTE<=>VoLTE Call
ATGW A
ATCF A
eNB A
UE A
ATGW B
ATCF B
eNB B
UE B
In this simple EVS call scenarios the originating UE A starts with the EVS Open Offer, in terms of the EVS Onion principle this is EVS-FB-11. The originating side of the IMS Network (represented by ATCF A) may allow this EVS-FB-11 to be forwarded. The terminating side (represented by ATCF B) may, however, reduce the EVS Onion to EVS-FB-6, either always or under certain load conditions. The call would be setup end to end with this EVS-FB-6 Onion as the "Framework Onion", see above in the corner. In good conditions (and only then) this would be equivalent to the EVS-FBOnly-6 NON-Onion.
If later, during the call the load conditions on one or the other LTE access would change - or somewhere in a transit network a bottleneck would occur - the EVS CMR would be exchanged in one or both directions and the actual EVS Onion would shrink,
e.g. to EVS-SWB-4 in one direction and EVS-SWB-3 in the other direction. This is in general better than terminating the call. The EVS-FBOnly-6 NON-Onion would not allow this. With a severe bottleneck in the path the call would have to be terminated.
In most cases a call is not terminated even if the rate would be further restricted (temporarily) to EVS-WB-2 or even lower: it is always preferable to let the Users decide, if they want to continue or terminate. Often it is quite helpful that the user experiences graceful quality degradation, when moving out of coverage: it gives guidance how to find good coverage again: a win-win situation, as the user gets back to better quality without call drop and the operator may operate a lower cost again.
IMS Network

## Slide 7: Simple VoLTE<=>CS Call (1)
ATGW A
ATCF A
IMS Network
eNB A
UE A
MGW B
MSC B
NB B
UE B
In this EVS call scenarios the originating UE A starts again with the EVS Open Offer, EVS-FB-11. The originating side of the IMS Network (represented by ATCF A) may allow this EVS-FB-11 to be forwarded to a CS network. It may of course also limit the EVS-Onion to another, smaller one.
The terminating side (represented by MSC B) must reduce the EVS Onion to EVS-FB-6, as no bigger EVS Onion is supported in CS.
In some networks, or under some circumstances, the MSC-allowed EVS-Onion may even be smaller. MSC B sends RAB Assignment to RNC B with EVS-FB-6, but - unfortunately - the 3G network is highly loaded and only EVS-SWB-4 is currently available. RNC B nevertheless accepts the RAB Assignment and sends an acknowledgement to MSC B. Note: THIS is current RNC behavior. It could be discussed to return EVS-SWB-4 to MSC B and all the way back to UE A. The call is setup end to end with this EVS-FB-6 Onion as the "Framework Onion", see above in the corner.
In the background - not known to the MSC - RNC B selects a radio bearer with SF=128, allowing only EVS-SWB-4. RNC B sends the Iu_Init to MGW B corresponding to EVS-FB-6, but with EVS-SWB-4 as first maximum rate- and band-control command.
MGW B sends a CMR-SWB-4 towards UE A in order to not use a mode outside this EVS-SWB-4 Onion. All that would not be possible, if ATCF A would have sent the EVS-FBOnly-6 NON-Onion in its SIP Invite.
RNC B
CS Network

## Slide 8: Simple VoLTE<=>CS Call (2)
ATGW A
ATCF A
eNB A
UE A
MGW B
MSC B
NB B
UE B
The call VoLTE <=> CS is ongoing as described in the previous slide. The resulted framework EVS Onions are shown.
Basically all major nodes in the call assume EVS-FB-6 is setup, but in fact the bottleneck is hidden in the 3G access: EVS-SWB-4. CMR-SWB-4 has been sent, so the actual EVS Onions are EVS-SWB-4 in both directions.
MSC B has also send a "NAS Sync ID" == UMTS_EVS to UE B, without details about the EVS Configuration (current signaling).
RNC B has setup the radio bearers with all necessary TFCs (Traffic Format Combinations) for EVS-SWB-4. Only from these TFCs UE B must assume (per definition) that it may use all modes of EVS-SWB-4 in uplink. Without further information UE B will use the upper right corner of this EVS Onion for Encoding in Uplink direction. In downlink direction UE B will accept and decode everything that fits to the EVS-SWB-4 Onion.
As long as the radio and other resources are sufficiently well provided by the network operator(s) the call will use in both direction the upper right corner of the EVS-SWB-4 Onion.
The lower bandwidths and rates are not used. They are provided without additional cost and used only, if necessary.
RNC B
EVS-FB-6
EVS-FB-6
EVS-FB-6
EVS-FB-6
EVS-SWB-4
IMS Network
CS Network

## Slide 9: Simple VoLTE<=>CS Call (3)
ATGW A
ATCF A
eNB A
UE A
MGW B
MSC B
NB B
UE B
The call VoLTE <=> CS is ongoing as described in the previous slide. The resulted framework EVS Onions are shown.
Several commands or events during the call may influence the actually used EVS rate and bandwidth in Uplink:
a) RNC B may send a RRC (Radio Resource Control) message to the UE to limit the maximum uplink rate (not the bandwidth). RNC B has no knowledge about audio bandwidths; it may happen that this rate control forces UE B to use a smaller bandwidth.
b) UE B may receive at its audio input speech signals with varying audio bandwidth. The EVS Codec may decide to apply a encoding algorithm for a lower audio bandwidth than maximally allowed.
c) UE B may detect TX power limitations that forces it to use a lower rate (and maybe lower bandwidth) in uplink.
d) UE B receives an endless stream of CMR (≤ CMR-SWB-4), together with each Speech, SID or No_Data frame in downlink. These CMR may limit the uplink rate and/or bandwidth. UE B must follow these CMR commands as soon as possible.
e) Received CMR may also command a change from the EVS-Primary Onion into the EVS-IO Onion or vice versa. The transition from the EVS-Primary Onion into the EVS-IO Onion is less critical than the reverse transition. UE B should wait for [2 or more] consecutive EVS-IO-CMRs before switching to the EVS-IO mode of operation.
In all cases CMR transmission errors, which are rare, but not excluded, are quickly healed by the endless CMR repetition.
RNC B
EVS-FB-6
EVS-FB-6
EVS-FB-6
EVS-FB-6
EVS-SWB-4
IMS Network
CS Network

## Slide 10: Simple VoLTE<=>CS Call (4)
ATGW A
ATCF A
eNB A
UE A
MGW B
MSC B
NB B
UE B
The call VoLTE <=> CS is ongoing as described in the previous slide. The resulted EVS Onions are shown.
Several commands or events during the call may influence the actually used EVS rate and bandwidth in Downlink:
a) RNC B may send an RC-Req (Rate Control Request) message to MGW B, limiting the maximum downlink rate. RNC B has no knowledge about audio bandwidths; it may happen that this rate control forces a smaller bandwidth. MGW B sends corresponding CMRs towards UE A within all RTP packets.
b) UE A may receive at its audio input speech signals with varying audio bandwidth. The EVS Codec may decide to apply a encoding algorithm for a lower audio bandwidth than allowed. UE B detects this inside the Speech parameters
c) UE B sends an endless stream of CMR (≤ CMR-SWB-4), together with each Speech or SID (or No_Data) frame in uplink. These CMR may limit the downlink rate and/or bandwidth. MGW B combines these CMR from UE B with RC-Req from RNC B into the CMR sent to UE A. UE A must follow these CMR commands as soon as possible.
RNC B
EVS-FB-6
EVS-FB-6
EVS-FB-6
EVS-FB-6
EVS-SWB-4
IMS Network
CS Network

## Slide 11: SRVCC with EVS to EVSoCS Onions (1)
The call was setup as VoLTE<=>VoLTE call with EVS-FB-6 as framework, see slide 6. Now SRVCC handover has to be performed into a loaded 3G cell, allowing at maximum EVS-SWB-4 as Target RAN Codec.
Due to the EVS Onion principle all Codecs involved are TrFO-compatible. As soon as ATGW A is informed about the SRVCC and the Target RAN Codec, it sends CMR-SWB-4 towards the remote end, i.e. towards UE B.
It takes a while, until UE B gets this CMR and sends back with mode EVS-SWB-4. It takes also a while, until SRVCC is executed on the air interface.
If well done, the Target RAN will receive only EVS-SWB-4 and the speech break is minimal. See the ongoing SETA TR work.
EVS-FB-6
EVS-FB-6
EVS-FB-6
Reference Architecture for SRVCC See TR 26.916, figure 4-1.
Note: reducing from EVS-FB-6 to EVS-SWB-4 may well be done shortly before SRVCC is executed; the LTE leg transports it as well to UE A.

## Slide 12: SRVCC with EVS to EVSoCS Onions (2)
The call was setup as VoLTE<=>VoLTE call with EVS-FB-6 as framework. slide 6. Now SRVCC handover has to be performed into a overloaded 3G cell, allowing at maximum EVS-WB-2 as Target RAN Codec.
As soon as ATGW A is informed about the SRVCC and the Target RAN Codec, it sends CMR-WB-2, see slide before.
EVS-FB-6
EVS-FB-6
EVS-FB-6
Reference Architecture for SRVCC See TR 26.916, figure 4-1.
Note: all this would not be possible with an EVS-NON-Onion, see next slide.

## Slide 13: SRVCC with EVS NON-Onion
Call setup was VoLTE<=>VoLTE with the EVS-SWBOnly-6 Non-Onion. Quality is high ("Super HD-Voice"). Now SRVCC handover has to be performed into a loaded 3G cell, allowing at maximum EVS-WB-2 Onion as Target RAN Codec.
ATCF and ATGW are informed about the Target RAN Codec and select EVS-FB-6 as CS PS Codec and CMR-WB-2 is exchanged, too.
ATGW A inserts transcoding between EVS-FB-6 and EVS-SWBOnly-6. CMR-SWB-6 is sent towards UE B. After SRVCC is finished the ATCF A may send a SIP Re-Invite towards UE B to change the IMS Selected Codec to the EVS-FB-6. This causes, however, in general a second voice path interruption.
EVS-SWBOnly-6
Reference Architecture for SRVCC See TR 26.916, figure 4-1.
EVS-SWBOnly-6
EVS-SWBOnly-6
Due to the short transcoding period the voice quality is degraded below EVS-WB-2 and ATGW A is loaded with transcoding. Without Re-Invite the transcoding must remain.

## Slide 14: Conclusion and Proposal
The EVS Onion principle provides simplest means for interworking at setup and any mid-call modifications, like Interworking with CS, SRVCC and handover-after-handover.
Transcoding Free Operation can always be maintained as long as EVS is supported, even with very different EVS onions in different segments of the voice path.
EVS Onions provide no drawback compared to EVS NON-Onions with same bit rate requirements; EVS Onions provide no quality degradation compared to EVS NON-Onions.
The network operator has the means and duty to provide the wanted/needed network performance to keep the actually used EVS modes (bit rates and audio bandwidths) at the desired level. If e.g. SWB performance up to 24.4 kbps is desired, then EVS-SWB-6 provides the best possible conditions.
Proposal: introduce the EVS Onion Principle for all EVS telephony services in 3GPP.