## Slide 1: Concept clarification for Network Slice SA5#128 18-22 November Zhuhai (China)
Nokia

## Slide 2: Concept clarification for Network Slice SA2
Network Slice: A logical network that provides specific network capabilities and network characteristics.
Network Slice instance: A set of Network Function instances and the required resources (e.g. compute, storage and networking resources) which form a deployed Network Slice.
NSI ID: an identifier for identifying the Core Network part of a Network Slice instance when multiple Network Slice instances of the same Network Slice are deployed, and there is a need to differentiate between them in the 5GC.
Network slices may differ for supported features and network functions optimisations, in which case such Network Slices may have e.g. different S-NSSAIs with different Slice/Service Types (see clause 5.15.2.1). The operator can deploy multiple Network Slices delivering exactly the same features but for different groups of UEs, e.g. as they deliver a different committed service and/or because they are dedicated to a customer, in which case such Network Slices may have e.g. different S-NSSAIs with the same Slice/Service Type but different Slice Differentiators (see clause 5.15.2.1).

## Slide 3: Concept clarification for Network Slice SA2
An S-NSSAI identifies a Network Slice.
  An S-NSSAI is comprised of:
  A Slice/Service type (SST), which refers to the expected Network Slice behaviour in terms of features and services;
  A Slice Differentiator (SD), which is optional information that complements the Slice/Service type(s) to differentiate amongst multiple Network Slices of the same Slice/Service type.
      Note: SD can be used to distinguish differentiated services or tenants?
Based on the operator's operational or deployment needs, a Network Slice instance can be associated with one or more S-NSSAIs, and an S-NSSAI can be associated with one or more Network Slice instances.

## Slide 4: Concept clarification for Network Slice SA5
network slice: Defined in 3gpp TS 23.501
network slice instance: Defined in 3GPP TS 23.501
network slice subnet: a representation of the management aspects of a set of Managed Functions and the required resources (e.g. compute, storage and networking resources).
network slice subnet instance: an instance of Network Slice Subnet representing the management aspects of a set of Managed Function instances and the used resources (e.g. compute, storage and networking resources).
communication services: subset of 3GPP defined services. Examples of 3GPP services (e.g. 5G LAN) can be found in TS 22.261.
communication service instance: run-time construct of a communication service for a defined group of users
service level specification: specification of the minimum acceptable standard of service
SLA requirements: service and network requirements derived from SLAs.

## Slide 5: Concept clarification for Network Slice SA5
From a management point of view a network slice instance is complete in the sense that it includes all the managed function instances, with their supporting resources, to provide a certain set of communication services to serve a certain business purpose. In other words, the network slice instance is complete because it completely satisfies the associated SLS.
The following concepts are related to network slicing management:
  Services which are supported by network slice instances (services who's service level requirements are satisfied by the SLS associated with the network slice instances)
  Network Slice Subnet instances and networks composed of PNF, VNF or both and exposed as Network Slice instances
  Network function (PNFs, VNFs) grouped into Network Slice Subnet instances
  Resources which support the network (e.g. virtualized resource, non-virtualized resource)

## Slide 6: Concept clarification for Network Slice SA5
General information for service profile
Depending on industry requirements and operator’s design requirements, different service profiles may be used to represent SLS associated with instances of Network Slice IOC.
The following are examples for service profiles:
A service profile is used to capture a set of requirements for the new network slice instance such as (eMBB, MIoT, URLLC).
A service profile is used to capture a set of specific industry requirements for creation of network slice instance such as V2X, smart grid, Remote Healthcare.

## Slide 7: Concept clarification for Network Slice Interpretation
A signaling network slice is a committed service provides specific network capabilities and network characteristics to a specific customer (tenant) or a group of UEs of the same customer. A signalling network slice is identified by a sNSSAI. The signaling network slice may represent a network connectivity part of communication service and is committed by the NOP.
A management network slice is a group of resources deployed to support one or multiple signalling network slices/committed services. A management network slice is identified by Network Slice Instance Id (NSI Id).
A Service Profile is used to capture a set of requirements of a (signalling) network slice instance, and the SLS is converted and combined from Service Profiles of committed services/signaling network slices, and represented the Service Level Specification of a (management) network slice instance serving the committed services/signaling network slices. SLS can be represented by Service Profile(s).
Given all said above, a specific service, or a specific service of a specific tenant is called as committed service or signaling network slice, it’s identified with an S-NSSAI (or sNSSAI), and its requirements are represented in a Service Profile. Multiple committed services or signaling network slices can be supported by a single management network slice instance identified with NSI Id which requirements are represented in SLS/Combination of Service Profile(s).

## Slide 8: Concept clarification for Network Slice Relationship in one deployment scenario

## Slide 9: Concept clarification for Network Slice Instance relationship
Management Network Slice reflects network slice in management plane, it’s identified by NSI Id defined as DN.
Committed Service/Signaling Network Slice reflects network slice in signaling plane, it’s same to Network Slice defined in SA2 and it’s identified by sNSSAI. It can represent network part of a communication service (CS is E2E which including device and application). One Communication Service can be supported by multiple Committed Services/Signaling Network Slices (provided by multiple operators)
SLS reflects requirements on the Management Network Slice Instance, and Service Profile reflects requirements on the Signaling Network Slice and can be used to derive/represent SLS