## Slide 1: Discussion paper on Exposure NRM
S5-214101r2

## Slide 2: Exposure Architecture and Interface
External customer
(e.g. SA6 Enablement layer)
BSS
External interface
Service manager
Internal interface
Service manager
External interface
Network manager
Internal interface
- In NSaaS mode, A vertical (i.e. CSP) may provide its service to external customer. The vertical (NSC) orders a network slices from NOSP in order to better serve its external customer. Both external customer and vertical may have the requirement to enable the exposure of certain MnSs that are related to the QoS performance of the network slices.
- Since external customer/vertical may not have good knowledges on the NRM defined in SA5. Exposing existing IoC to externals may not be use-friendly；
- SA5 can consider to encapsulate regroup certain IoC for different type of application in order to make the exposed IoC more customer friendly；
S5-214101r2
Company X
Company Y

## Slide 3
Exposure NRM
- Encapsulate Regroup the IOC regarding Network slice management exposure and exposes the encapsulated exposure IOC to eMnS consumer in order to make the exposure more customer friendly；
NetworkSlice
operationalState
administrativeState
serviceProfileList
Attribute related to role
networkSliceSubnetRef
eNetworkSlice
ServiceType (live video streaming, V2X, etc)
eServiceProfile
PermissionInfo
Exposed IOC for video streaming
NetworkSlice
eServiceProfile(live video streaming)
Latency
reliability
DelayTolerance
Jitter
- The encapsulated exposure IOCs are based on different verticals (e.g. live video streaming) ；
Exposure NRM
- Encapsulated Exposure IOC can be easily used by CSP to serve its external customer；
eServiceProfile(V2X)
Latency
UEMobilityLevel
V2XCommModels
- The encapsulated Exposure IOCs are based on the current concept of NRM；
S5-214101r2