## Slide 1: Discussion paper on 5G exposure
Orange, Ericsson, Huawei, AT&T, Telefonica

## Slide 2: Rationale
SA5 is having lengthy discussions on 5G network / network slice / service / management service (MnS) exposure
There is a lack of common understanding of some concepts and vocabulary
In next slides, it’s proposed to use TM Forum FrameworX, in addition to 3GPP TS 28.53x, to (try to) clarify some concepts

## Slide 3: TMF GB 922: SID: Shared Information/Data model
Customers buy and use Product(s)
Products are supported by Service(s)
Services use Resource(s)

## Slide 4: Preamble
Any CSP needs a BSS (to manage customers, product offerings, tariffs, subscriptions, contracts, etc.). Customers can usually access CSP’s BSS via a Portal
Any CSP needs a Service Management Layer (for service supervision, service performance management, service topology, etc.)
OSS is layered as follows:
  Service Management Layer (SML)
  Network Management Layer
  Network Element Management Layer
Therefore, any CSP needs:
  BSS, and
  Service Management Layer (as part of OSS )

## Slide 5: Organizational scenario No. 1 (CSP and NOP played by the same organization) - Example
ex.: Orange Business
Services (OBS)
ex: United Nations (UN)
CSP
BSS
OSS/SML
NOP
OSS/NML
CSC
Network
2. ‘I want to order Product ‘X’
(TMF API 622 Product Ordering)
1. United Nations chooses a product from OBS Product offerings
Customer Management
Product Management
Service Management
Network Management

## Slide 6: Organizational scenario No. 2 (NSC/NSP in place of CSC/CSP) - Example
ex.: Orange Business
Services (OBS)
NSP
BSS
OSS/SML
NOP
OSS/NML
NSC
2. ‘I want to order the product:
Network Slice eMBB Platinum’
(TMF API 622 Product Ordering)
1. UN chooses a product from OBS Product offerings
Network Slice eMBB (Silver, Gold, Platinum)
Network Slice URLLC (Silver, Gold, Platinum)
Network Slice MIoT (Silver, Gold, Platinum)
OBS product offerings
3. UN gets a ‘Network Slice eMBB Platinum’ product from OBS
Network
TMF API 641 (Service Ordering)
3GPP TS 28.531, TS 28.532
ex: United Nations (UN)
3GPP TS 28.531, TS 28.532

## Slide 7: Organizational scenario No. 3 (Multiple organizations) - Example
3GPP TS 28.531,
TS 28.532
TMF API 641
(Service Ordering)
ex.: Orange Business
Services (OBS)
NSP
BSS
OSS/SML
NSC
ex.: Telefonica Spain (TEF)
CSC
6. ‘I want to order the product ‘X’
(e.g. Wholesale)
(TMF API 622 Product Ordering)
5. OBS chooses a product from TEF Product offerings
2. ‘I want to order the product:
Network Slice eMBB Platinum’
(TMF API 622 Product Ordering)
1. UN chooses a product from OBS Product offerings
3. UN gets a ‘Network Slice eMBB Platinum’ product from OBS
CSP
BSS
OSS/SML
NOP
OSS/NML
Network
NOP
OSS/NML
OBS 5G Core Network
CSC
ex.: AT&T
CSP
BSS
OSS/SML
NOP
OSS/NML
Network
4. OBS needs RAN coverage in Spain
9. ‘I want to order the product ‘Y’
(e.g. Network Slice)
(TMF API 622 Product Ordering)
8. OBS chooses a product from AT&T Product offerings
7. OBS needs RAN coverage in USA
*: OBS owns its 5G CN
TMF API 641
TMF API 641
ex: United Nations (UN)
3GPP TS 28.531,
TS 28.532
3GPP TS 28.531,
TS 28.532
3GPP TS 28.531,
TS 28.532
3GPP TS 28.531,
TS 28.532

## Slide 8: ‘Network Slice eMBB Platinum’ Product Specification Example
  Network Slice type eMBB
    Guaranteed throughput / data rate = 0 (i.e. Best effort)
  Silver + Additional functions
    Guaranteed throughput / data rate = 10 Mbps
    Capabilility to receive Product-level Critical Alarms
    Capability to receive 2 Product-level KPIs:
      Session establishment success rate for the network slice
      Upstream and downstream throughput for the network slice
  Gold + Advanced functions
    Guaranteed throughput / data rate = 100 Mbps
    Capabilility to receive Product-level Critical+Major+Minor Alarms
    Capability to receive all following Product-level KPIs:
      Accessibility KPIs for the Network Slice eMBB Platinum
      Integrity KPIs for the Network Slice eMBB Platinum
      Utilization KPIs for the Network Slice eMBB Platinum
      Retainability KPIs for the Network Slice eMBB Platinum
      Mobility KPIs for the Network Slice eMBB Platinum
      Energy Efficiency KPIs for the Network Slice eMBB Platinum
  Tariff(s)
  Validity (in space and time)
  Allowed usages
  Use consent(s)
  Etc.
Silver
Gold
Plati
num
TECHNICAL
NON-TECHNICAL
  Silver: No ‘Guaranteed Time To Repair’ (GTR)
  Gold: GTR < 8 hours
  Platinum: GTR < 4 hours
OPERATIONAL

## Slide 9: Key Findings
NSP (as any CSP) has a ‘Product Catalogue’ with ‘Product Offerings’
NSC (as any CSC) orders product(s) (NOT service(s)) from NSP (resp. CSP) Product Offerings
A Product represents the subscription of a Product Offering by a Customer (e.g. NSC)
There is NOT necessarily a 1-to-1 correspondence between Product and Service
  A Product may be realized via different Services (e.g. in case NSP deploys multiple ways to support a Product)
NSC (as any CSC) has Product-level visibility ONLY on his Product
  NOT on underlying Service(s)
  NOT on underlying Resource(s) such as e.g. Network Functions, Network Slice Subnet(s), Network Slice(s)
Only Product-level features are exposed by NSP to NSC
NSC can be offered control of key features (such as e.g. capacity increase, policy change)
  If, and within limits, specified in the Product Specification
  Via BSS only
NSC shall not get exposure of management capability by MnS Producer(s)

## Slide 10: Operation phase: from Resource-level alarms to Product-level alarms
Resource-level alarms
Correlation, filtering, enrichment, etc.
Service-level alarms
Correlation, filtering, enrichment, etc.
Product-level alarms
Possibly exposed to NSC (depending on Product Specification)
Not exposed to NSC
Not exposed to NSC
BSS
OSS

## Slide 11: Thank you!