## Slide 1: Discussion paper on architecture options for local breakout roaming
Ericsson
S5-22abcd

## Slide 2: Possible solutions
There are three main alternatives for the local breakout roaming scenario with CHF and SMF interaction
  Two logical CTFs and two logical SMFs
  One logical CTF and one logical SMF
  Two logical CTFs and one logical SMF
  Combined solution
In all cases there will be two CHFs

## Slide 3: Two logical CTFs and two logical SMFs (A)
V-SMF
UPF
V-CTF
V-CHF
H-CHF
N47
N4
N40
An extra UPF and SMF is added for the local breakout roaming
Works like the home routed roaming with the difference the SMF corresponding to the H-SMF is placed in VPLMN
Both SMFs would interact with PCF independently
Limited impact on the specifications e.g., a new deployment option
The VPLMN would have limited knowledge of when and what is sent between A-SMF and H-CHF
A-SMF
A-CTF
UPF
N4
VPLMN
HPLMN

## Slide 4: One logical CTF and one logical SMF (B)
V-SMF
UPF
V-CTF
V-CHF
H-CHF
N47
N4
N40
There is one CTF and one SMF interacting with two CHFs
The CTF have one set of quota, triggers etc. i.e., the H-CHF overwrites all settings by V-CHF
The same information is sent to both CHFs at the sametime, except that some information may be filtered out
There would be one set of information from PCF
VPLMN
HPLMN

## Slide 5: Two logical CTFs and one logical SMF (C)
V-SMF
UPF
V-CTF
V-CHF
H-CHF
N47
N4
N40
An extra UPF and SMF is added for the local breakout roaming
The SMF would combine the settings from the CHFs towards the UPF
The SMF would sort information from the UPF to the right CTF
The SMF would interact with PCF for the settings of the V-CTF and A-CTF
The VPLMN would have limited knowledge of when and what is sent between A-CTF and H-CHF
A-CTF
VPLMN
HPLMN

## Slide 6: Combined solution
V-SMF
UPF
CTF
V-CHF
H-CHF
N47 - FBC (optionally QBC)
N4
N40 - QBC only
There is one CTF and one SMF interacting with two CHFs
The CTF have one set of quota, triggers etc. i.e.
The V-CHF can only set QBC triggers V-CHF
H-CHF can set session, FBC, and QBC triggers
QBC triggers can only be set using roaming charging profile
The same information is sent to both CHFs at the same time for QBC
Retry, failure, and error handling will be operator specific
There would be one set of information from PCF
VPLMN
HPLMN