## Slide 1: Cloud Native Data Streaming
xxxxx xx, 24
Source: Rakuten Mobile Inc [RMI]

## Slide 2: Background
Management service
Management service
NF workload
NF workload
NF
Large scale cloud native deployment requires moving of massive amount of data from multiple sources to multiple consumers in real-time.
Conventional data streaming pattern and architecture for PM/FM/trace/analytics are not suitable anymore
Efficient, high throughput, highly scalable, and fault-tolerant data streaming framework is needed for sharing data between cloud native network functions and management system.
3GPP Management System
MnF
WebSocket
Node
NF workload
Node
Node
Node cluster
Management workload
NF
…
…
Cloud site
Cloud site
Cloud site
Convention streaming architecture
Cloud-native streaming architecture
storage
storage
…
Point-to-point connection based
No data sharing
Simple and static connection topology
No dynamic scaling
No distributed computing
Limited connection resiliency
Application layer manage all connection aspects.
Multipoints-to-multipoints streaming with data sharing.
Complicated topology and dynamic
Dynamic scaling
Highly distributed
High connection resiliency is required.
Integration with cloud storage is required.

## Slide 3: Cloud-Native Streaming Requirement
Parallel streaming at scale and scalable
Data sharing and isolation
Resiliency and failure tolerance
Easy and dynamic connection management
And see below
Partitions
parallel contribution of data pieces
of the same topic
Data bus handling data distribution, routing, subscription management etc
Data bus workload can scale horizontally also
parallel consuming of data pieces of the same topic with data isolation
Producers , consumers and data bus workloads are distributed across multiple nodes and cloud site
Redundant backup connection and data source for failure protection
Data Bus
Producer
Producer
Producer
Producer
Consumer
Producer
publish
Producer
publish
Producer
publish
Consumer
subscribe
Consumer
subscribe
Data Bus
Node cluster
Horizontal scaling of producers
Publish-Subscription based streaming mode designed for cloud-native applications – micro-service, sharing, distributed, scaling
Stream/top A
Stream/top B
Stream/top C

## Slide 4
Feature | Conventional Streaming (3GPP 28.532 ) through Web-sockets | Cloud-Native Streaming through Kafka
Infrastructure | Dedicated Resources: WebSocket demand maintaining connection all the time even no data to stream for certain time, which requires dedicated resources at Netwok function side . | Cloud-Based Resources: Kafka does not required to maintain connection, so it requires minimum resources when there is no data to stream.
Architecture | Monolithic Application or Point-to-Point Integrations: A single, large application might handle data ingestion, processing, and reporting. Modifying functionalities within this application can be complex and require changes to the entire system. Alternatively, point-to-point integrations might be used, where each data source has a custom connection to the processing application. This creates a tightly coupled system that's difficult to modify or scale. | Microservices Architecture with Streaming Platform: The system is broken down into smaller, independent services that handle specific tasks (e.g., data ingestion, processing, reporting). This allows for easier development, deployment, and updates. A dedicated streaming platform, like Apache Kafka, acts as a central hub for data flow. Data sources publish data to the platform, and processing services subscribe to relevant data streams. This decoupled architecture promotes flexibility and independent scaling of services.
Integration | Proprietary Protocols or Custom Integrations: Data exchange between network elements and the processing system might rely on proprietary protocols specific to the network vendor. Alternatively, custom integrations might be developed to connect different elements. This approach can be complex to manage and maintain, especially when integrating new network equipment. | Open-Source or well-known APIs and Event-Driven Architecture: APIs (Application Programming Interfaces) act as standardized communication channels between network elements and the streaming platform. This approach simplifies integration and ensures compatibility with a wider range of equipment. Event-driven architecture allows for loosely coupled communication – network elements publish events (data updates) to the platform, and processing services subscribe to receive relevant events when they occur. This improves scalability and simplifies adding new data sources.
Scalability | Manual Scaling: Adding or removing dedicated servers to handle fluctuations in data volume is a manual process that requires planning and downtime. This can lead to inefficiencies, as underutilized servers during low traffic periods increase costs, while insufficient resources during peak times can lead to performance issues. | Automatic Scaling: Cloud platforms offer automatic scaling based on real-time data flow. Additional virtual servers are automatically provisioned when needed and de-provisioned when traffic subsides. This ensures optimal resource utilization and avoids performance bottlenecks during peak loads.
Real-time Processing | Limited Capabilities: Traditional systems might have limited real-time processing capabilities due to the architecture and the overhead of data processing within a monolithic application or point-to-point integrations. Delays in data processing can lead to outdated insights and slower response times to network issues. | Enabled through Streaming Platform: Streaming platforms like Kafka are specifically designed for handling large volumes of data in real-time. Data is processed as it arrives, enabling faster analysis and quicker identification of network performance problems. This allows for proactive troubleshooting and minimizes potential disruptions.

## Slide 5: Kafka for 3GPP
Current 3GPP streaming architecture
3GPP has defined solution set for streaming data based on WebSocket.
Point-to-point connection based rather than publishing/subscription for cloud native
Single thread connection, no parallel streaming, not scalable.
No resiliency and failure protection.
Application side handles all complexity of the connection management.
Proposals
Kafka based solution set for streaming data reporting service in addition to WebSocket based for PM, FM, trace and analytic data streaming.
Keep data interchange as generic “Serialization format “ so we can define any format such as ASN.1, XML, JSON etc.
The streaming is publish-and-subscribe based instead of point-to-point connection based.
Connection and data distribution/routing complexity is handled by the data bus (hided from applications)
Parallel and distributed writing and reading
Dynamic scaling of producers and consumers.
Serialization Formats

## Slide 6: Related WID /SID in SA5
ID | Unique_ID | Name | Acronym | OutlineLevel | Release | ResourceNames | Start | Finish | %Complete | Hyperlink | Status Report | WI rapporteur name | WI rapporteur e-mail
15 | 1020021 | Study on energy efficiency and energy saving aspects of 5G networks and services | FS_Energy_OAM_Ph3 | 2 | Rel-19 | S5 | 12/8/2023 | 9/9/2024 | 10% | SP-231723 |  | Jean-Michel Cornily (Huawei) | jean.michel.cornily@huawei.com
30 | 1020007 | Study on AI/ML management - phase 2 | FS_AIML_MGT_Ph2 | 1 | Rel-19 | S5 | 1/3/2024 | 9/6/2024 | 0% | SP-231780 |  | Yizhi Yao (Intel) | yizhi.yao@intel.com
187 | 1020019 | Study on Management Data Analytics (MDA) Phase 3 | FS_eMDAS_Ph3 | 1 | Rel-19 | S5 | 1/3/2024 | 9/6/2024 | 0% | SP-231726 |  | Brendan T Hassett (Huawei) | brendan.t.hassett@huawei.com
188 | 1020008 | Study on intent driven management services for mobile network phase 3 | FS_IDMS_MN_Ph3 | 1 | Rel-19 | S5 | 1/3/2024 | 9/6/2024 | 5% | SP-231737 |  | Ruiyue Xu (Huawei) | xuruiyue@huawei.com
189 | 1020009 | Study on closed control loop management | FS_CCLM | 1 | Rel-19 | S5 | 1/3/2024 | 9/6/2024 | 5% | SP-231735 |  | Deepanshu Gautam (Samsung) | deepanshu.g@samsung.com
190 | 1020018 | Study on management aspects of Network Digital Twin | FS_NDT | 1 | Rel-19 | S5 | 1/3/2024 | 9/6/2024 | 5% | SP-231428 |  | Yushuang Hu (China Mobile) | huyushuang@chinamobile.com
191 | 1020010 | Study on Cloud Aspects of Management and Orchestration | FS_Cloud_OAM | 1 | Rel-19 | S5 | 1/3/2024 | 9/6/2024 | 2% | SP-231781 |  | Bahar Sadeghi (Microsoft) | bahar.sadeghi@microsoft.com
192 | 1020016 | Study on Enablers for Security Monitoring | FS_SECM | 1 | Rel-19 | S5 | 1/3/2024 | 9/6/2024 | 0% | SP-231736 |  | Clifton Fernandes (Nokia) | clifton.fernandes@nokia.com
193 | 1020011 | Study on Service Based Management Architecture enhancement phase 3 | FS_SBMA_Ph3 | 1 | Rel-19 | S5 | 1/3/2024 | 9/6/2024 | 0% | SP-231725 |  | Kai Zhang (Huawei) | kai.zhangkai@huawei.com
194 | 1020033 | Study on Management of planned configurations | FS_PlanM | 1 | Rel-19 | S5 | 1/4/2024 | 9/9/2024 | 0% | SP-231721 |  | Olaf Pollakowski (Nokia) | olaf.pollakowski@nokia.com
195 | 1020025 | Data management phase 2 | MADCOL_Ph2 | 1 | Rel-19 | S5 | 1/3/2024 | 6/5/2025 | 0% | SP-231746 |  | Sivaramakrishnan Swaminathan (Nokia) | sivaramakrishnan.swaminathan@nokia.com
196 | 1020012 | Study on data management regarding subscriptions and reporting | FS_Data_SREP | 1 | Rel-19 | S5 | 1/3/2024 | 9/6/2024 | 0% | SP-231732 |  | Robert Petersen (Ericsson) | robert.petersen@ericsson.com
197 | 1020026 | 5G performance measurements and KPIs phase 4 | PM_KPI_5G_Ph4 | 1 | Rel-19 | S5 | 1/3/2024 | 6/5/2025 | 0% | SP-231747 |  | Primary Rapporteur: XiuMin Chen (China Telecom) | chenxiumin@chinatelecom.cn
198 | 1020027 | 5G Advanced NRM features phase 3 | AdNRM_Ph3 | 1 | Rel-19 | S5 | 1/3/2024 | 6/5/2025 | 0% | SP-231745 |  | Sean Sun (Nokia) | sean.sun@nokia-sbell.com
199 | 1020028 | Subscriber and Equipment Trace and QoE collection management | TraceQoE_OAM | 1 | Rel-19 | S5 | 1/3/2024 | 6/5/2025 | 0% | SP-231748 |  | Zu Qiang (Ericsson) | zu.qiang@ericsson.com
200 | 1020013 | Study on Management Aspects of NTN Phase 2 | FS_NTN_OAM_Ph2 | 1 | Rel-19 | S5 | 1/3/2024 | 9/6/2024 | 0% | SP-231733 |  | MingRui Sun (China Unicom) | sunmr19@chinaunicom.cn
201 | 1020014 | Study on management of IAB nodes | FS_NR_mobile_IAB_OAM | 1 | Rel-19 | S5 | 1/3/2024 | 9/6/2024 | 0% | SP-231729 |  | JunFeng Wang (Ericsson) | junfeng.a.wang@ericsson.com
202 | 1020017 | Study on management aspects of RedCap feature | FS_NR_RedCap_OAM | 1 | Rel-19 | S5 | 1/3/2024 | 9/6/2024 | 0% | SP-231734 |  | Zhen Xing (China Unicom) | xingz12@chinaunicom.cn
203 | 1020020 | Study on Enhancement of Management Aspects related to NWDAF Phase 2 | FS_NWDAF_OAM_Ph2 | 1 | Rel-19 | S5 | 1/3/2024 | 9/6/2024 | 0% | SP-231724 |  | Primary Rapporteur: Song Zhao (China Telecom) | zhaosong1@chinatelecom.cn
204 | 1020015 | Study on Management of Network Sharing Phase3 | FS_NetShare_OAM_Ph3 | 1 | Rel-19 | S5 | 1/3/2024 | 9/6/2024 | 0% | SP-231731 |  | ZhaoNing Wang (China Unicom) | wangzn18@chinaunicom.cn
205 | 1020022 | Study on Enhanced OAM for management exposure to external consumers | FS_MExpo | 1 | Rel-19 | S5 | 1/3/2024 | 9/6/2024 | 5% | SP-231728 |  | Primary Rapporteur: Scott Probasco (Nokia) | scott.probasco@nokia.com

## Slide 7: Data management - Phase 2 SA5 WID
TR 28.842 highlighted Key issue of “Define capabilities for Management Data Reporting “ in 4.6
An MnS Consumer can query the attributes of this IOC to determine which methods and options are available for management data reporting
Efforts on defining “SupportedDataReporting <<IOC>> to allow producer supporting capabilities .
An MnS Consumer can query the attributes of this IOC to determine which methods and options are available for management data reporting
SupportedDataReporting
This WID will work on discovering capabilities for Management Data Reporting , to avoid signaling load and consistency at both consumer and producer ends.

## Slide 8
What is to be studied is whether there can be an entity outside the traffic node that can combine the two requests into on towards the traffic node, in order to minimize the administration and reporting in the traffic node. The new entity should be able to change trace jobs without ending and starting a new job (i.e. keep the same Trace Reference when new measurements are added or removed).
Objective
To study:
WT-1 Study how the load on the NFs and/or 3GPP mgmt. system can be decreased by extracting some of the required functionality to be deployed outside the NFs implementing management capabilities defined in SA5.
WT-2 Study how to solve to get unique job identifiers for performance measurement, Trace/MDT and QoE subscriptions/requests within a PLMN from different consumers. Propose potential requirements, use cases and solutions for this issue.
SID: Study on data management regarding subscriptions and reporting Rel19 SA5 WID
This SID talks about defining entity outside which identifies common request and minimize efforts on NF for reporting multiple times.
Which could be like Kafka solution ,where multiple consumers and producers are exchanging common data

## Slide 9
What is to be studied is whether there can be an entity outside the traffic node that can combine the two requests into on towards the traffic node, in order to minimize the administration and reporting in the traffic node. The new entity should be able to change trace jobs without ending and starting a new job (i.e. keep the same Trace Reference when new measurements are added or removed).
Objective
To study:
WT-1: Analysethe use cases which utilize the VNF generic OAM functions (specified in ETSI) and their potential impacts when applied to the 3GPP management system and study whether and how to incorporate the VNF generic OAM functions into the 3GPP management system, i.e., the requirements and the potential solutions.
WT-2: Study the use cases that utilize the newly developed industry solutions for management of cloud native network functions which leverage industry standards not limited to ETSI NFV MANO; study the potential impact of supporting such use cases on the 3GPP management system, i.e., the potential requirements and solutions.
WT-3: Study the use cases, potential requirements and possible solutions for 3GPP management system to support different cloud deployment scenarios, such as public-cloud, private-cloud, hybrid-cloud and multi-cloud deployment scenarios.
SID: Study on cloud aspect of orchestration and management Rel19 SA5 WID
This SID talks about the overall management solution for cloud native NF including the data streaming.
This could be the main host of the work for studying fundamental architectures enhancement and impacts for cloud native streaming collaborated with other SI work.