## Slide 1: Discussion on LCM of Cloud Native NF using Standardized K8S CRD Models
08 July, 24

## Slide 2: Background
In large scale cloud deployment, the management system conveys declarative description of the NF deployment requirements to the orchestrator for creation, modification and termination of cloud-native NFs.
The descriptor includes the requirements (e.g. artifacts, metadata, interface endpoints, performance requirement etc) for the orchestrator to select, configure or modify the appropriate cloud resources to host the workload of the cloud-native NF.
Declarative systems continuously evaluate the current state, determine the steps to realize the intended state as described in the descriptor, and then reconcile those states by modifying the current state.
K8S Custom Resource Definition (CRD) implements the above principle. It is a schema-driven mechanism which allows for creation of customized objects on the K8S API server. The customized object is associated with an operator which handles the imperative NF orchestration procedures to fulfill the declarative requirements defined in the custom resource model.
to match
Future state
represent
Update status
State change events
Custom resource
Operator
Current state
adjust
modifications

## Slide 3: Problems Today with K8S CRD in Multi-Vendor Cloud Environment
Today, vendors are implementing proprietary customer resource models (CRD schemas) to manage their own NFs in the cloud.
Without a standardized CRD schema, there is no interoperable way for 3GPP management system to understand the vendor specific CRD contents and retrieve or construct the deployment requirements for each vendor’s NF.
In use cases where resources allocated for multi-vendor NFs need to be modified, coordinated, or jointly optimized by the 3GPP management system, there is no interoperable multi-vendor solutions today using K8S CRD approach.
Even within the same vendor, without a standard CRD schema, collaboration among different teams (e.g. NF developing team, network service designers, NF deployment team, and infra deployment team) to express the NF resource requirements on the infrastructure is problematic.
There is a strong need to standardize the CRD schema for different types of 3GPP NFs in RAN and core, to enhance interoperability in multi-vendor NFs cloud environment.
Orchestration system (K8S based)
NF workload
(vendor A)
3GPP management system
Orchestration system (K8S based)
Operator
(vendor A)
Cluster A
NF workload
(vendor A)
Operator
(vendor B)
NF workload
(vendor B)
Cluster B
NF workload
(vendor B)
Each vendor manage its own NFs independently in isolated cloud resources, i.e. separate clusters or namespaces
Management system cannot modify the deployment requirements in the CRDs.
There is no centralized management, runtime resource coordination and joint optimisation
Vendor-specific CRDs
CRD based on schema A
Operator
(vendor A)
Operator
(vendor B)
Isolated resource
CRD based on schema B
3GPP management system has no way to understand the content in the CRDs, and to retrieve or construct the deployment requirement information to modify, coordinate or jointly optimize the resource.
The declarative control loop breaks, limited LCM capability.
Cloud site

## Slide 4: Benefits of Standardized CRD for Multi-Vendor Cloud (Single-Tenant Dedicated Resource)
Orchestration system (K8S based)
NF workload
(vendor A)
3GPP management system
Orchestration system (K8S based)
Operator
(vendor A)
Cluster/namespace A
NF workload
(vendor A)
Operator
(vendor B)
NF workload
(vendor B)
Cluster/namespace B
NF workload
(vendor B)
Single-tenant dedicated resource
Each vendor’s operator still manage its own NFs in isolated cloud resources.
Common standardized CRDs
CRD based on schema C
Operator
(vendor A)
Operator
(vendor B)
Isolated resource
CRD based on schema C
3GPP management system can understand the CRD content for each vendor NF’s deployment and manage the resource allocation through retrieving and constructing requirement information from/to the CRDs
The management system can
modify the NF deployment (part of LCM requirements ) to coordinate or jointly optimize the resource in runtime.
modify the infrastructure configuration to adjust the resource allocation to different clusters, namespaces,
Cloud site
multi-vendor cloud
e.g. isolated cluster or namespace

## Slide 5: Benefits of Standardized CRD for Multi-Vendor Cloud (Multi-Tenant Shared Resource)
Example 1: DU, CU-CP and UPF are collocated at the edge and are jointly optimized
Orchestration system (K8S based)
CRD common
Operator
(common)
Edge cloud cluster
DU
(vendor A)
CU-UP
(vendor B)
Operator
(common)
UPF
(vendor C)
3GPP management system
Orchestration system (K8S based)
CRD common
Operator
(common)
Edge cloud cluster
DU
(vendor A)
Operator
(common)
3GPP management system
DU
(vendor B)
UPF, CU-UP
(vendor B)
Best effort slice
Latency and bit rate guaranteed slice
NF workload
(vendor A)
3GPP management system
Orchestration system (K8S based)
CRD common
Operator
(common)
Cluster/namespace common
NF workload
(vendor A)
NF workload
(vendor B)
NF workload
(vendor B)
Operator
(common)
e.g. multi-vendors’ NF share the same cluster and are jointly managed by the common operators
The system integrator manages both NFs from vendor A and B based on standardized CRD schema.
Multi-tenant shared resource
Example 2: Multi-vendor slice with dynamic slice SLA assurance
frequency
time
resource allocated for slice A
resource allocated for slice B
3GPP management system can understand the CRD content for each vendor NF’s deployment and manage the resource allocation through retrieving and constructing requirement information from/to the CRDs
When the traffic demand of Slice B increases, re-allocate resource to slice B to guarantee the bit rate and latency
Cloud site
e.g. Multi-vendor NFs shares single cluster or namespace

## Slide 6: Conclusion
The solution enhances interoperability, cost efficiency, and performance in multi-vendor cloud in both single-tenant as well as in multi-tenant cluster environments.
Through understanding the CRD contents based on the standardized CRD schemas, the 3GPP management system can
  Retrieve vendor specific deployment requirements from the CRDs and configure cloud infrastructure and make NF deployment placement decisions accordingly.
  Construct new deployment requirements to modify the current deployments (part of LCM requirements), coordinate and jointly optimize the resource among different vendors’ NFs in runtime.
The standardized CRD solution only focuses on taking the common, non-differentiating aspects of vendors’ solutions, and standardizing common CRD parameters for those common capabilities while still enables cloud, network function, and orchestration vendors to develop unique and critical value they can bring.
The standardized CRDs only provide a high-level declaration on what to be achieved by the orchestration system (the deployment requirements) rather than how to achieve it, leaving the most value critical functions completely to vendor implementations.
Examples of the standardized CRD parameters can be seen in page 7-9

## Slide 7: Example standardized CRD for UPF
CRD_UPF
Interface
>n3 >n4 >n6
Capacity requirements
>maxUplinkThroughput >maxDownlinkThroughput
Dependency
>smfRef
Network endpoints
>vpcN3 >vpcN4 >vpcN6
Resource requirements (optional)
->resourceConstraint
More capacity requirements e.g.
NF logical interface definitions, mapping with network interfaces
Network interface definitions, IP/FQDN configurations, mapping with NFlogical interfaces
Resource requirement or constraint for the NF deployment, e.g. CPU/RAM/storage capacity, NUMA awareness, node binding etc.
UPF workload
(vendor A)
Cluster
Node
Node
UPF workload
(vendor A)
3GPP management system
Orchestration system (K8S based)
CRD_UPF
Operator
UPF workload
(vendor A)
Node
Operator
The CRD express the high-level requirements of the NF deployment
The orchestration system (operators) automatically allocate resources to the NF workloads to achieve requirements
Ref: Nephio – Linux Foundation Project

## Slide 8: Example standardized CRD for CUUP
CRD_CUUP
Interface
>e1 >f1u >n3
Capacity requirements
>maxUplinkThroughput >maxDownlinkThroughput
Dependency
>cuupRef
Network endpoints
>vpcE1 >vpcF1u >vpcN3
Resource (optional)
->resourceReq ->resourceConstraint
More capacity parameters e.g.
NF logical interface definitions, mapping with network interfaces
Network interface definitions, IP/FQDN configurations, mapping with NFlogical interfaces
Resource requirement and constraint for the NF deployment, e.g. CPU/RAM/storage capacity, NUMA awareness, node binding etc.

## Slide 9: Example Information Model
CRD_CUUP
Interface
>e1 >f1u >n3
Capacity
>maxUplinkThroughput >maxDownlinkThroughput
Dependency
>cuupRef
Network
>vpcE1 >vpcF1u >vpcN3
Resource (optional)
->resourceReq ->resourceConstraint
Notes: @startuml
CRD_TOP "1"*--"*" InterfaceDef
CRD_TOP "1"*--"*" NetworkDef
CRD_TOP "1"*--"*" DependencyDef
CRD_TOP "1"*--"1" CapacityDef
CRD_TOP "1"*--"1" ResourceDef
@enduml