## Slide 1: Discussion on the proposal to extend Energy Efficiency to the OAM domain
Simone Bizzarri
Delegate, Telecom Italia (TIM)

## Slide 2: Outline
EE related past and current activities
Towards 6G for a whole EE system
Energy Efficiency in OAM Processes
Interworking with infrastructure domain
Summary
Proposal

## Slide 3: EE related past activities
Starting from Rel. 10, many SIDs and WIDs have been activated to define measurements and procedures to measure, evaluate and manage the energy consumed by networks (from 3G to 5G).
The scope of all these standardisation activities mainly concerns:
Radio Access Network (mainly GERAN, UTRAN, E-UTRAN and NR, but also including non-3GPP access networks): in terms of radio coverage and traffic load, where cells could be placed in an energy-saving (dormant) state, but also including network interfaces (i.e. Iu for UTRAN, X2 and S1 for E-UTRAN).
Core Network: from 4G to 5GC (from Release 15)
UE
Edge Computing
For all these domains, the role of OAM is central in all steps: monitoring and evaluation, configuration and optimisation, etc., and a number of management functionalities and attributes have been defined.

## Slide 4: EE related current activities (rel. 19)
In the current standardisation release, there are the following issues related to EE:
Energy Efficiency as a Service Criteria in SA1
EE and energy saving aspects in SA2 and SA5 (EnergySys)
Charging aspects related to EE in SA5
Security aspects of ES in SA3
For SA5 we have to consider documents SP-241003 for charging and SP-231723 for OAM
In addition, other activities regarding RAN aspects related to "Enhancements of Network Energy Savings for NR" are followed by working groups RAN1, RAN4, RAN5 and SA4.
Also for the AI/ML topic, the energy consumption evaluation and management aspects is considered for all steps in the lifecycle of an ML algorithm. RAN is also active on this context, e.g., RAN3 is working on use cases related to Energy Efficiency as a specific use case of AI/ML optimisations

## Slide 5: Towards 6G to a whole EE system
OAM/Charging
RANs
CNs
Edge
UEs
Infrastructure (NFV MANO/Cloud)
AI/ML
AI/ML
AI/ML
AI/ML
AI/ML
OAM processes
With EE functionalities
Without EE functionalities

## Slide 6: Energy Efficiency in OAM Processes
Use case #1: Performance Measurement Job Optimization
  Gather performance information from the network and network slices. Each of the enabled PerfMetricJobs has an energy consumption that can depend on several factors (number and type of activated measurements, granularityPeriods, reportingMethods and reportingPeriods). Each combination of these values has an impact on the energy consumed by the PerfMetricJob process. The requirement is to have an energy consumption indication associated with each measurement job in order to manage such processes accordingly.
Use case #2: SON (non-AI/ML based) operation and CCL:
  As for AI/ML algorithm, also all optimisation functionalities such as SON and/or CCL consume energy during their operational state. It could be useful to introduce some indication of energy consumption to manage such algorithms (i.e. through policy management).

## Slide 7: Interworking with infrastructure domain
Every software function (NF or management function) running in a virtualised infrastructure domain uses processing, storage and communication resources. Each of these has an associated energy consumption.
For this reason, it is very important to define a correlation between energy consumption related information for each domain (network, infrastructure and OAM domains), in order to manage the inter-domain interaction in an efficient way
  Example: in case of high energy consumption for a network performance monitoring process, an OAM orchestrator will be able to modify the configuration process and/or reduce the associated virtualised resource energy consumption by interacting with MANO in case of NFV environment.

## Slide 8: Summary
The trend of making a green mobile system must also consider the network and service management domain as a part of the whole system, to meet overall energy-efficiency targets.
In addition, we must also consider the relationship with the infrastructure domain, to ensure that virtualization is managed taking into account energy efficiency target.
Energy Efficiency is a crucial aspect when addressing economic and environmental sustainability impacts of solutions. The identification and definition of indicators that quantitatively and qualitatively describe these aspects are important

## Slide 9: Proposal
Our proposal is to extend the Energy Efficiency management aspects to OAM processes in order to optimise the entire energy consumption defining an overall energy efficient system.