## Slide 1: Cloud Native NF Data Streaming Solution Analysis WebSocket VS HTTP2.0 VS Kafka
15 Jan 2025
Source: Rakuten Mobile Inc [RMI]

## Slide 2: Overview
Introduction of solutions for cloud-native NF data streaming based on different technologies
Pros and cons analysis and comparison among technologies
Conclusions on the technical analysis and key discussions
Commercial benefit highlight for operators with Kafka technology
3GPP standard Impact
Addressing Kafka scalability concern from some company
Addressing Kafka performance concern from some company

## Slide 3: Overview
Introduction of solutions for cloud-native NF data streaming based on different technologies
Pros and cons analysis and comparison among technologies
Conclusions on the technical analysis and key discussions
Commercial benefit highlight for operators with Kafka technology
3GPP standard Impact
Addressing Kafka scalability concern from some company
Addressing Kafka performance concern from some company

## Slide 4
PM
Application
instances
PM
Application
instances
NF
MnS Producer
NF
MnS Producer
Solution 1 – WebSocket based
WebSocket
Server node
(high availability)
WebSocket
Server node
(high availability)
WebSocket
server node
(high availability)
WebSocket
server node
WebSocket
server node
WebSocket
server node
(high availability)
Message broker
PM
Application
NF
MnS Producer
NF
MnS Producer
NF
MnS Producer
NF
MnS Producer
WebSocket load balancer
3. The message broker acts as a middleware layer that decouples the front-end WebSocket servers from the backend services so that
The backend service can see data from all independent server nodes.
Routing of data to backend services is independent of data routing at the front-end.
Decoupling the front-end and back-end data transport protocols
Backend service and front-end can be scaled independently.
MnS consumer
4. High node and connection availability is needed for
              Scaling up the server pool to match the increasing traffic demand from an old NF (the NF connect to more servers, e.g. blue+green servers)
              Scaling up the server pool to match the new traffic demand from a new NF (more servers to server new NFs)
              Resilient to single server node failure (connections on failed node move to backup server node)
              Resilient to single transport path failure and avoids transport down time (by having backup connections, e.g. blue + green)
1. Each NF MnS producer sets up a persistent WebSocket connection with the consumer
2. A load balancer distributes the connections from the NFs to multiple server nodes to balance the load on each server. Once a connection is established with a particular server node, it remains persistent with the server node.
These are vital for cloud-native NF deployment especially for centralized cloud because
Single point of failure causes significant service impact (e.g. impacts the service in an entire city).
PM traffic load from NFs increases/decreases dynamically and can go beyond a single WebSocket server capability.
New NF instances can be added dynamically.
Micro-service workload instances

## Slide 5: Solution 2 – HTTP based (1.0/2.0/3.0)
1. Each NF or its component instance directly sends data to the management system through HTTP POST. No persistent connection between NF and front-end HTTP server nodes
2. A load balancer distributes the HTTP POST requests from the NFs to multiple server nodes to balance the load. Unlike WebSocket based solution where a connection persistently stays with a particular server node, the HTTP POST requests can be forwarded to any of the server node without persistent attachment with a particular server node.
3. The message broker acts as a middleware layer that decouples the front-end HTTP servers from the backend services so that
The backend service see data from all independent server nodes.
Routing of data to backend services is independent to data routing at the front-end.
Decoupling the front-end and back-end data transport protocols
Backend and frontend services can be scaled independently.
4. High server node availability is needed for scalability, load-balancing and fault-tolerance
5. High load balancer availability is needed to enable fault-tolerance during server crashes, network issues, or data center outages. Balancing the load between load balancers is also needed.
A DNS failover and load balancing mechanism is normally needed for the purpose
PM
Application
instances
PM
Application
instances
NF
MnS Producer
NF
MnS Producer
HTTP
server node
(high availability
HTTP
server node
HTTP
server node
HTTP
server node
(high availability)
Message broker
PM
Application
NF
MnS Producer
NF
MnS Producer
NF
MnS Producer
NF
MnS Producer
HTTP Load balancer
MnS consumer
HTTP Load balancer
DNS failover and LB
4,5 are vital for cloud-native NF deployment especially for centralized cloud
Same reasons as page 3
Micro-service workload instances
Notes: 4 -7 vital for cloud-native NF deployment especially for centralized cloud because

## Slide 6: Solution 3 – Message bus based
Kafka Message broker
Kafka message broker
Server node
Kafka message broker
server node
PM
Application
instances
PM
Application
instances
NF
MnS Producer
NF
MnS Producer
PM
Application
NF
MnS Producer
NF
MnS Producer
NF
MnS Producer
NF
MnS Producer
MnS consumer
Kafka push
Micro-service workload instances
1. Each NF or its component instance simply sends data to the management system through Kafka protocol.
2. Kafka framework automatically route the data to right applications at the backend and handles
Successful data delivery
Load balancing
Data replications for fault-tolerance
Auto scaling
Kafka cluster
3. Complexity with HTTP or WebSocket for handling scaling, load balancing and fault-tolerance, data integrity and delivery performance are mostly eliminated.

## Slide 7: Overview
Introduction of solutions for cloud-native NF data streaming based on different technologies
Pros and cons analysis and comparison among technologies
Conclusions on the technical analysis and key discussions
Commercial benefit highlight for operators with Kafka technology
3GPP standard Impact
Addressing Kafka scalability concern from some company
Addressing Kafka performance concern from some company

## Slide 8: Solution 1 – WebSocket based Pros and Cons
Cons
WebSocket connections consume server resources (e.g., memory, file descriptors, and CPU).
WebSocket keep-alive messages consume network bandwidth.
Client reconnection during failure cause service interruption.
WebSocket connections are long-lived, which makes load balancing and scaling less effective. Once a connection is established, it remains tied to a specific server, which can lead to uneven distribution of connections across servers.
WebSocket connections are stateful. Maintaining state across servers for reconnecting clients due to failures can be difficult.
WebSockets introduce additional complexity compared to state-less protocol communication (e.g. HTTP, Kafka), which requires additional architectural and engineering complexity to manage load balancing, connection states, handling of dropped connections, reconnections at scale.
To enable handling reconnections, failovers, scaling, packet loss and duplication, NF (WebSocket client ) and management system (WebSocket server) sides are not completely decoupled leading to interoperability challenges for operators.
Data produced from each microservice instance of the NF are collected and aggregated by the NF management function first who own and manage the persistent connections. This leads to additional overhead and scaling challenges for the MnS producer.
Pros
WebSocket is a IETF standardized protocol (RFC 6455), ensuring compatibility across different platforms and technologies.
Websocket is already supported by most of the conventional (non-cloud-native) NFs.
PM
Application
instances
PM
Application
instances
NF
MnS Producer
NF
MnS Producer
WebSocket
Server node
(high availability)
WebSocket
Server node
(high availability)
WebSocket
server node
(high availability)
WebSocket
server node
WebSocket
server node
WebSocket
server node
(high availability)
Message broker
PM
Application
NF
MnS Producer
NF
MnS Producer
NF
MnS Producer
NF
MnS Producer
WebSocket load balancer
MnS consumer
Micro-service workload instances

## Slide 9: Solution 2 – HTTP based Pros and Cons
Cons:
No guarantee of in sequence delivery of the HTTP POST requests, thus the PM data payloads
Additional HTTP protocol overhead (HTTP header, Request + Response)
Producer and consumer jointly handles reconnections, lost and duplicated packets with additional proprietary engineering complexity leading to interoperability challenges for operators.
Pros:
HTTP is also a standardized protocol ensuring compatibility across different platforms and technologies.
No persistent connections that consume server resources (e.g., memory, file descriptors, and CPU).
No keep-alive messages consume network bandwidth.
Effective load balancing and scaling compared against WebSocket.
Maintaining connection state across servers for reconnecting clients due to failures is not needed.
Handling scaling, load balancing, and failure requires less complexity compared against WebSocket when done at scale.
For handling reconnections, failovers, data integrity, scaling, NF and management system are more decoupled.
Data produced from each microservice instance of the NF can be sent directly to the management system without going through the centralized connection point. This avoids additional the overhead and scaling challenges compared against WebSocket.
PM
Application
instances
PM
Application
instances
NF
MnS Producer
NF
MnS Producer
HTTP
server node
(high availability
HTTP
server node
HTTP
server node
HTTP
server node
(high availability)
Message broker
PM
Application
NF
MnS Producer
NF
MnS Producer
NF
MnS Producer
HTTP Load balancer
MnS consumer
HTTP Load balancer
DNS failover and LB
NF
MnS Producer
Micro-service workload instances

## Slide 10: Solution 3 – Message bus based Pros and Cons
Kafka is a not a standardized protocol. But compatibility across different platforms and technologies are ensured by opensource community.
Not supported by conventional (non-cloud-native) NFs. New implementation is needed for cloud-native NFs.
Cons
Pros:
Similar to HTTP due to benefit of stateless comparing against WebSocket
Less protocol overhead than HTTP.
Additional front-end data transport layer (HTTP, WebSocket) and protocol conversions (WebSocket->Kafka, HTTP->Kafka) are avoided for better efficiency.
Guaranteed successful data delivery.
Guaranteed in-sequence delivery within single broker instance (partition) where management system and NF can leverage it for sequential delivery when needed.
Complexity with HTTP for handling scaling, load balancing and fault-tolerance, data integrity and delivery performance are mostly eliminated.
NF and management system sides are completely decoupled which provide better interoperability.
Direct integration with operator backend enterprise applications/ services, for e.g. analytic, telemetries monitoring, service assurance for less complexity, better efficiency, better data exposure and integrity.
Kafka Message broker
Kafka message broker
Server node
Kafka message broker
server node
PM
Application
instances
PM
Application
instances
NF
MnS Producer
NF
MnS Producer
PM
Application
NF
MnS Producer
NF
MnS Producer
NF
MnS Producer
NF
MnS Producer
MnS consumer
Kafka push
Micro-service workload instances
Kafka cluster

## Slide 11: Summary and comparison of pros and cons
 | WebSocket | HTTP (1.0/2.0/3.0) | Kafka
Protocol overhead and efficiency | M Overhead from keep alive messages and resource maintaining connections and storing the state Overhead from centralized data collection and delivery via the managed connections Overhead from front-end to backend conversion (WebSocket->Kafka) TCP head-of-line blocking | HTTP 1.0: L, 2.0: M, 3.0: M Higher overhead from HTTP headers, TCP multiplexing, and Request-Response based protocol. Each NF microservice instance can data send directly to the management system Overhead from front-end to backend conversion (WebSocket->Kafka) HTTP1.0: large overhead due to TCP reconnection in every request HTTP2.0: TCP head-of-line blocking HTTP3.0: TCP head-of-line blocking is solved with QUIC | H Extra implementation overhead is not needed, designed for efficient data streaming Same as HTTP Single data transport layer, no separation and conversion between front-end and back-end (Kafka to Kafka direct) TCP head-of-line blocking is solved with multiple partitions
Scaling and load balancing performance | L Persistent connection with a particular server node, no flexibility to move traffic across servers for load balancing and scaling | H Data packets are dynamically loaded to any available servers | H Same as HTTP
Fault-tolerance, data integrity and in-sequence-delivery performance | L down time during reconnection whenever there is a server or connection failures | M PM data is automatically forwarded to healthy servers. Some packet loss and interruption are still encountered when a server node fails packets already arrived in the failed HTTP server load balancer will get lost; load balancer takes time to detect the failed HTTP server node; DNS server takes time to detect failed load balancer. | H Automatic data delivery repetition for strong resiliency: if lead path fails, follower path still guarantees data is delivered
Ease of implementing for large scale cloud | L WebSocket introduces additional complexity compared to state less protocol communication which requires significant additional architectural and engineering complexity to manage load balancing, connection states, handle dropped connection, reconnections specially when done at scale | M Still requires some architectural complexity and engineering efforts: Load balancer DNS load balancing mechanism HTTP failure handling Packet reordering handling dropped and delayed packet handling | H Complexity handling scaling, load balancing and fault-tolerance, data integrity and delivery performance are mostly offloaded to Kafka layer.
Standard support and Interoperability | L Although it is a standardized protocol, scalability, failures, packet errors and sequence delivery requires proprietary implementation because of the tight coupling. | M Although it is a standardized protocol, scalability, failures, packet errors and sequence delivery requires proprietary implementation because of the tight coupling. | H Although not a standard defined by a SDO, it is already an industry standard solution providing better decoupling and interoperability.
Support in conventional NFs | H Supported since Rel17 | M HTTP2.0 for file transfer since Rel15 but not for streaming reporting service yet. | L Not supported by 3GPP standard before for NF, but already
Performance score is given to each technology for each cloud requirement.
H: Best performance
M: Medium performance
L: Lower performance

## Slide 12: Overview
Introduction of solutions for cloud-native NF data streaming based on different technologies
Pros and cons analysis and comparison among technologies
Conclusions on the technical analysis and key discussions
Commercial benefit highlight for operators with Kafka technology
3GPP standard Impact
Addressing Kafka scalability concern from some company
Addressing Kafka performance concern from some company

## Slide 13: Conclusions and Key Discussions
Kafka stands out as the best method for cloud-native NF data streaming in terms of performance/efficiency, scalability, fault-tolerance, data integrity, interoperability etc.
Although it is not a standard protocol defined by a SDO, it is already widely used as industry standard solution, providing better decoupling and the interoperability than WebSocket and HTTP when being in the cloud at scale.
It was not supported in conventional NFs (non-cloud native), so some implementation effort is needed for the emerging cloud-native NF solutions. But the overall complexity for implementing a scalable and fault-tolerant system suitable for cloud deployment at scale is much lower than other methods (WebSocket and HTTP).
The 3GPP standard and NF industry should evolve to capture up with the speed of cloud industry and be open to leverage those advanced cloud technologies (e.g. K8S, Kafka).
In the cloud industry, supporting multiple communication mechanisms for cloud applications is very normal - primary communication mechanism for better performance and fallback mechanism to ensure largest compatibility.
Similarly, for cloud native NFs, propose to add Kafka as an additional data streaming method for better performance in large scale cloud environment and keep WebSocket as fallback mechanism for backward compatibility.

## Slide 14: Overview
Introduction of solutions for cloud-native NF data streaming based on different technologies
Pros and cons analysis and comparison among technologies
Conclusions on the technical analysis and key discussions
Commercial benefit highlight for operators with Kafka technology
3GPP standard Impact
Addressing Kafka scalability concern from some company
Addressing Kafka performance concern from some company

## Slide 15: Commercial benefit highlight for operators using Kafka
Kafka provide significant commercial benefits for operators’ businesses, especially when dealing with large-scale, real-time data processing and event-driven architectures.
Better user experience: Kafka enables businesses to process and analyze data in real time, allowing for faster decision-making and improved responsiveness to network changes. Real-time insights lead to better user experiences. Faster response to operational issues reduces downtime and improves efficiency.
Scalability and cost efficiency: Kafka is designed to handle massive amounts of data with high throughput and low latency. It can scale horizontally by adding more brokers to the cluster. Reduces the need for expensive, monolithic systems to handle large-scale data. Cost-effective scaling ensures businesses can grow without incurring exponential infrastructure costs.
Decoupling of system and interoperability: Kafka acts as a central event streaming platform, decoupling producers (data sources) and consumers (data processors). This simplifies system architecture and reduces dependencies. Faster development cycles and improved interoperability between NF and OAM suppliers reduces integration costs and complexity, saving time and money in the long run.
Improved resiliency and data integrity: Kafka is fault-tolerant and ensures data durability through replication. It can handle failures without losing data or disrupting operations. Minimizes downtime and data loss, which can be costly for businesses. Ensures consistent and reliable user experiences, improving brand reputation.
Unified data platform: Kafka can act as a single platform for collecting, storing, and distributing data across multiple systems (e.g., databases, analytics tools, NWDAF, MDT, AI/ML microservices). Reduces the need for multiple data integration tools and adaptations (e.g. WebSocket to Kafka), lowering operational costs. Simplifies data pipelines, making it easier to manage and maintain.
Private 5G and enterprise cloud: Kafka is already widely used in enterprise cloud in new industry verticals making it easier to integrate private 5G network with existing industry cloud with the unified data platform.
Integration with Existing Tools: Kafka integrates seamlessly with a wide range of tools and systems in the cloud, including databases, analytics platforms, and cloud services, reducing the cost and effort of building custom integrations. Leverages existing investments in tools and infrastructure in the cloud.
Future-Proofing the Business: Kafka's ability to handle diverse use cases (e.g., PM metrics, messaging, log aggregation, stream processing) makes it a versatile platform for evolving business needs. Protects investments by providing a platform that can adapt to future requirements.

## Slide 16: Overview
Introduction of solutions for cloud-native NF data streaming based on different technologies
Pros and cons analysis and comparison among technologies
Conclusions on the technical analysis and key discussions
Commercial benefit highlight for operators with Kafka technology
3GPP standard Impact
Addressing Kafka scalability concern from some company
Addressing Kafka performance concern from some company

## Slide 17: 3GPP standard impact
WebSocket based solution
Message bus-based solution
For Kafka, the logical streaming session is equivalent to Kafka topic, and the streaming session establishment request contains a topic ID, consumer’s broker endpoint information and optionally a partition information.
After the streaming session is established, the MnS producer start reporting the management data using Kafka protocol, referring to the ID and endpoint information provided by the MnS consumer.
there is no change to the existing Streaming Data Reporting Service APIs which establish a WebSocket streaming connection between MnS producer and MnS consumer.
A new Streaming Data Reporting Service API will be added for the MnS consumer send request to the MnS producer to establish a logical streaming session instead of a connection.
Solution today (WebSocket only)
Additional solution proposed
There is minor impact to the TS28.532 streaming data reporting service APIs to support the additional Kafka based streaming protocol.
There is no impact to other MnS and architecture since this is purely transport layer change.
There is no backward compatibility impact, no change to existing network and investment.

## Slide 18: Overview
Introduction of solutions for cloud-native NF data streaming based on different technologies
Pros and cons analysis and comparison among technologies
Conclusions on the technical analysis and key discussions
Commercial benefit highlight for operators with Kafka technology
3GPP standard Impact
Addressing Kafka scalability concern from some company
Addressing Kafka performance concern from some company

## Slide 19: Addressing Kafka scalability concern from some company
Kafka is designed natively to handle massive amounts of data with high throughput and low latency.
It is already widely used in the cloud industry already handling much higher data volume than telecom industry today.
  Confluent has reported that some of their customers process petabytes of data per day using Kafka.
  Netflix has shared that they process trillions of messages per day using Kafka.
  LinkedIn, where Kafka originated, has reported processing over 7 trillion messages per day (as of recent updates).
Mobile operators already use Kafka in 5G network
  Rakuten Mobile, Dish Network, DoCoMo, AT&T, Verizon, Vodafone, T-Mobile, Telefonica, Orange, Resilience Jio, BT
Kafka can scale horizontally by adding more independent brokers or adding more Kafka clusters. Scalability in cost effective and interoperable manner is at the heart of the Kafka design.
If one broker works for e.g. 100 cells , there is no reason it cannot work for 100K+ cells through horizontal scaling. The scalability of Kafka is well known and demonstrated in many real-world cloud applications.
Message broker server node 1
…
X cells
X cells
X cells
Kafka cluster 1
…
Kafka cluster 2
Kafka cluster M
Message broker server node 2
Message broker server node N
Kafka load balancing and data replication handling
…

## Slide 20: Overview
Introduction of solutions for cloud-native NF data streaming based on different technologies
Pros and cons analysis and comparison among technologies
Conclusions on the technical analysis and key discussions
Commercial benefit highlight for operators with Kafka technology
3GPP standard Impact
Addressing Kafka scalability concern from some company
Addressing Kafka performance concern from some company

## Slide 21: Addressing performance concern in unstable transport condition
Automatically handling resiliency and data loss and duplication protection for the cloud operators to tackle the most challenging large-scale distributed cloud environment is at the heart of Kafka design.
It is already widely used in the cloud industry already handling much higher data volume than telecom industry today and deployed in most challenging cloud environment.
Kafka maintains a list of in-sync replicas of the data processed by multiple high-availability brokers. Even if a broker fails, the replicated data ensures no data loss and uninterrupted service.
Kafka allows consumer offsets to be stored in a special internal topic which is also replicated. This mechanism ensures fault tolerance for consumers and prevents data duplication or loss.
Many other mechanisms are implemented to protect against failures: Acknowledgment Mechanism, Leader Election, Durable Writes, failure node detect, ZooKeeper high availability, Monitoring and Alerts, Rebalancing and Partition Reassignment etc.
All above are handled automatically in Kafka middleware layer, minimize development complexities and cost, maximize reliability. More importantly Kafka decouples the producers and consumers implementations for a better interoperable system in the cloud at scale.

## Slide 22: Addressing performance concern in unstable transport condition
Comparing performance between WebSocket, HTTP and Kafka.
WebSocekt | HTTP (1.0/2.0/3.0) | Kafka
If WebSocket connection or WebSocket server node fails, client reconnect with the server side -> service interrupted during reconnection. Producer and consumer jointly handles reconnection, lost and duplicated packets with additional application layer complexity -proprietary implementation of the fault-tolerant features provided by Kafka above. The tight coupling leads to interoperability challenges. | If connection between producer and consumer (the HTTP load balancer endpoint) fails, it takes time for DNS service to detect failed load balancer node and resolve to a new LB endpoint IP -> service interrupted . If one HTTP server node fails, PM data is automatically forwarded to healthy servers by load balancer. It takes time for load balancer to detect a failure node->service interrupted Producer and consumer jointly handles reconnection, lost and duplicated packets, with additional proprietary application layer complexity. The tight coupling leads to interoperability challenges. | If connection between producer and one broker fails, or one broker fails, other brokers automatically take over. The replicated data ensures no data loss and uninterrupted service. Failed node or transport link are automatically removed from Kafka cluster and can be automatically recommitted and reloaded after recovery. Kafka ensure exactly-once semantics for stream processing, ensuring that messages are processed exactly once, even in the event of failures. All fault-tolerant mechanisms are offloaded to Kafka middleware layer, producer and consumer are completely decoupled.