## Slide 1: K8S CRD based Orchestration
January 22, 2025

## Slide 2: Background for Declarative systems
to match
Future state
represents
Update status
State
change
Declarative state + Current status
Managing software
Current state
adjust
Modifications
Declarative systems incorporate
  Requirements
    In declarative state
  Managing Software
    Watches the declarative state for changes
    Adjusts resources to represent the latest declarative state
  Current status
    Represents latest state of resources
Resources

## Slide 3: Custom Resource Definitions in K8S
to match
Future state
represents
Update status
State
change
K8S CR
(Declarative state + Current status)
K8S Operator
(Managing software)
Current state
adjust
Modifications
K8S operator pattern
  Schema
    Represented by CRD
  Requirements
    Represented by CR
  Managing Software
    Watches the declarative state for changes
    Adjusts K8S resources to represent the latest declarative state
  Current status
    Represented in CR
K8S Cluster for workloads

## Slide 4: Problems Today with K8S CRD in Multi-Vendor Cloud Environment
Communication service providers work with vendor-specific helm charts or CRs to manage NFs
There is no interoperable way for 3GPP management system to define the deployment requirements for each vendor’s NF.
A user employed by the service provider creates separate artifacts for each vendor
There is a strong need to standardize the CRD schema for different types of 3GPP NFs in RAN and core, to enhance interoperability in multi-vendor NFs cloud environment.
Orchestration system (K8S based)
3GPP management system
Orchestration system (K8S based)
Operator
(vendor A)
Cluster A
3GPP NF workload
(vendor A)
Operator
(vendor B)
Cluster B
3GPP NF workload
(vendor B)
Each vendor manage its own NFs independently in isolated cloud resources, i.e. separate clusters or namespaces
Management system cannot modify the deployment requirements in the CRs.
There is no centralized management, runtime resource coordination and joint optimisation
Vendor-specific CRDs
CR based on CRD schema A
Operator
(vendor A)
Operator
(vendor B)
CR based on CRD schema B
3GPP management system has no way to understand the content in the CRs, and to retrieve or construct the deployment requirement information to modify, coordinate or jointly optimize the resource.
Cloud Infrastructure
3GPP NF workload
(vendor A)
3GPP NF workload
(vendor B)

## Slide 5: Benefits of Standardized CRD for Multi-Vendor Cloud (Single-Tenant Dedicated Resource)
Orchestration system (K8S based)
3GPP management system
Orchestration system (K8S based)
Operator
(vendor A)
Cluster/namespace-A
3GPP NF workload
(vendor A)
Operator
(vendor B)
Cluster/namespace-B
3GPP NF workload
(vendor B)
Single-tenant dedicated resource
Each vendor’s operator still manage its own NFs in isolated cloud resources.
Uses standardized CRDs
CR based on standardized schema
Operator
(vendor A)
Operator
(vendor B)
CR based on standardized schema
3GPP management system can understand the CR content for each vendor NF’s deployment and manage the resource allocation through retrieving and constructing requirement information from/to the CRs
The management system can
modify the NF deployment (part of LCM requirements ) to coordinate or jointly optimize the resource in runtime.
Cloud infrastructure
multi-vendor cloud
e.g. isolated cluster or namespace
3GPP NF workload
(vendor A)
3GPP NF workload
(vendor B)

## Slide 6: Benefits of Standardized CRD for Multi-Vendor Cloud (Multi-Tenant Shared Resource)
Example 1: DU, CU-CP and UPF are collocated at the edge and are jointly optimized
Orchestration system (K8S based)
CRD common
Operator
(common)
Edge cloud cluster
DU
(vendor A)
CU-UP
(vendor B)
Operator
(common)
UPF
(vendor C)
3GPP management system
Orchestration system (K8S based)
CRD common
Operator
(common)
Edge cloud cluster
DU
(vendor A)
Operator
(common)
3GPP management system
DU
(vendor B)
UPF, CU-UP
(vendor B)
Best effort slice
Latency and bit rate guaranteed slice
3GPP management system
Orchestration system (K8S based)
CR based on standardized schema
Operator
(common)
Cluster/namespace common
3GPP NF workload
(vendor A)
3GPP NF workload
(vendor B)
Operator
(common)
3GPP NF workload
(vendor A)
3GPP NF workload
(vendor B)
e.g. multi-vendors’ NF share the same cluster and are jointly managed by the common operators
The system integrator manages both NFs from vendor A and B based on standardized CRD schema.
Multi-tenant shared resource
Example 2: Multi-vendor slice with dynamic slice SLA assurance
frequency
time
resource allocated for slice A
resource allocated for slice B
3GPP management system can understand the CR content for each vendor NF’s deployment and manage the resource allocation through retrieving and constructing requirement information from/to the CRs
When the traffic demand of Slice B increases, re-allocate resource to slice B to guarantee the bit rate and latency
Cloud site
e.g. Multi-vendor NFs shares single cluster or namespace

## Slide 7: Example based on standardized CRD for UPF
CRD_UPF
Interface
>n3 >n4 >n6
Capacity requirements
>maxUplinkThroughput >maxDownlinkThroughput
Dependency
>smfRef
Network endpoints
>vpcN3 >vpcN4 >vpcN6
Resource requirements (optional)
->resourceConstraint
More capacity requirements e.g.
NF logical interface definitions, mapping with network interfaces
Network interface definitions, IP/FQDN configurations, mapping with NF logical interfaces
Resource requirement or constraint for the 3GPP NF deployment, e.g. CPU/RAM/storage capacity, NUMA awareness, node binding etc.
UPF workload
(vendor A)
Cluster
Node
Node
UPF workload
(vendor A)
3GPP management system
Orchestration system (K8S based)
CR_UPF
Operator
UPF workload
(vendor A)
Node
Operator
The CR express the high-level requirements of the 3GPP NF deployment
The orchestration system (operators) automatically allocate resources to the NF workloads to achieve requirements
Ref: Nephio – Linux Foundation Project

## Slide 8: Creation of NF instance using 3GPP-defined CRD
CRD_UPF
Interface
>n3 >n4 >n6
Capacity requirements
>maxUplinkThroughput >maxDownlinkThroughput
Dependency
>smfRef
Network endpoints
>vpcN3 >vpcN4 >vpcN6
Resource requirements (optional)
->resourceConstraint
Example
CRD

## Slide 9: Conclusion
The solution enhances interoperability, cost efficiency in multi-vendor cloud in both single-tenant as well as in multi-tenant cluster environments.
The standardized CRDs shall
  Provide a high-level declaration on what to be achieved by the orchestration system (the deployment requirements)
  The how is achieved by vendor-specific operator implementations.
  Focuses only on taking the common, non-differentiating aspects of 3GPP NFs
  Vendor extensions will enable cloud, NF and orchestration vendors to develop unique and critical value they can bring.
Using the standardized CRD schemas, the 3GPP management system can
  Retrieve vendor specific deployment requirements from the CRs, configure cloud infrastructure and make NF deployment placement decisions accordingly.
  Construct new deployment requirements to modify the current deployments (part of LCM requirements)

## Slide 10: Example Information Model for CRD
CRD_CUUP
Interface
>e1 >f1u >n3
Capacity
>maxUplinkThroughput >maxDownlinkThroughput
Dependency
>cuupRef
Network
>vpcE1 >vpcF1u >vpcN3
Resource (optional)
->resourceReq ->resourceConstraint
Notes: @startuml
CRD_TOP "1"*--"*" InterfaceDef
CRD_TOP "1"*--"*" NetworkDef
CRD_TOP "1"*--"*" DependencyDef
CRD_TOP "1"*--"1" CapacityDef
CRD_TOP "1"*--"1" ResourceDef
@enduml