## Slide 1: ECS configuration information
Nishant Gupta
Delegate, Qualcomm

## Slide 2: Current status
Requirements
6.3.4 Edge Configuration Server (ECS)
NOTE: The ECS can be deployed in the MNO domain or can be deployed in 3rd party domain by service provider.
8.3 ECS Discovery and Service provisioning
If the ECS deployed by MNO is contracted with one or more ECSP(s), the ECS provides EES configuration information of MNO owned and ECSP owned EESs via MNO ECS as described in clause 8.3.3.3.3.
Observations
Description of the ECS provider identifier needs to be updated as it can be provided by non-ECSP MNOs also.
Additional IEs are needed to list ECSPs which are supported by the ECS.
Additional IE is needed to include ECS’s Spatial Validity Conditions.
Current specification
Information element | Status | Description
ECS address | M | One or more endpoint information (e.g. URI(s), FQDN(s), IP address(es)) of ECS(s)
ECS Provider Identifier | O | The identifier of the ECSP that provides the ECS.
Table 8.3.2.1-1: ECS configuration information

## Slide 3: Proposed changes
Proposed Update
Information element | Status | Description
ECS address | M | One or more endpoint information (e.g. URI(s), FQDN(s), IP address(es)) of ECS(s)
ECS Provider Identifier | O | The identifier of the ECSP that providers the ECS.
Spatial Validity Conditions | O | Spatial validity conditions associated with the ECS.
List of supported ECSPs | O | List of ECSPs whose information is available via this ECS.
> ECSP ID | M | Identifier of the ECSP
> Spatial Validity Conditions | O | Spatial validity conditions associated with the ECSP.
Requirements
6.3.4 Edge Configuration Server (ECS)
NOTE: The ECS can be deployed in the MNO domain or can be deployed in 3rd party domain by service provider.
8.3 ECS Discovery and Service provisioning
If the ECS deployed by MNO is contracted with one or more ECSP(s), the ECS provides EES configuration information of MNO owned and ECSP owned EESs via MNO ECS as described in clause 8.3.3.3.3.
Change summary
Description of ‘ECS provider identifier’ IE is updated to clarify that the IE denotes the ID of the Edge Configuration Server’s provider,
Additional IEs are added to list ECSPs which are supported by the ECS.
Additional IE is added to include ECS’s Spatial Validity Conditions.
Table 8.3.2.1-1: ECS configuration information