## Slide 1: EWBI Interface for Federation
3GPP
Samar Shailendra (Intel)

## Slide 2: E/WBI – GSMA OP (1/3)
In its PRD v3, GSMA OPG defines the EWBI functionalities for federation as:
  Federation Interconnect Management (Sec 3.3.1): secure transport, plus capabilities such as integrity protection for the E/WBI messaging between OP instances.
  Resource Catalogue Synchronisation and Discovery (Sec 3.3.2): Type of resource, maintenance etc.
  Application and Resources Management (Sec 3.3.4): the Application Provider criteria provided to the Leading OP are transferred via the E/WBI to the Partner OP and used to deploy the application.
  Service Availability (Sec 3.3.4): the E/WBI shall allow the Home OP to provide the Visited OP with the necessary information to perform authorisation and grant the service access (e.g. a token).
  Edge Node Sharing (Sec 3.3.5): The connectivity between two OPs is over the E/WBI interface.

## Slide 3: E/WBI – GSMA OP (2/3)
GSMA PRD v3, also describes the list of services for E/WBI interface (Sec 3.5.4)
  East/West Bound Interface Management Service
  Availability Zone Information Synchronisation Service
  Application and Resources Management
  Edge Node Sharing Service
  Application Deployment Management Service
  Events and Notifications Service
  Service Availability in Visited Network Management Service

## Slide 4: E/WBI – GSMA OP (3/3)
GSMA PRD v3, also describes Requirements for E/WBI interface (Sec 5.1.2)
  The E/WBI is universal, meaning that all Operators and Operator Platforms provide Edge Cloud to each other through the same E/WBI.
  Security Requirements
  Application Management
  Sharing Usage statistics for the service requested by federated connection (Sec 5.2.3.2)

## Slide 5: GSMA OP – Separation of Concern
GSMA OPG PRD describes Separation of Concern of
  OP and Application Providers (Sec 2.1.2)
    the Application Providers and OP do not require knowledge of each other's internal workings and implementation details
      the OP does not expose its internal topology and configuration etc.
      the OP does not know how the application works (for instance, it does not know about the application's identifiers and credentials)
  Between Two OPs (Sec 2.1.4)
    "separation of concerns" of the operators between each other and between OPs. Where the Operator Platform is not part of the operator's security domain, there is also a "separation of concerns" of the operators from the OP.
"Separation of concerns" again means that they do not require knowledge of each other's internal workings and implementation details. For instance, the operators do not expose their internal topology and configuration, Cloudlets' (exact) physical locations, internal IP addressing, and real-time knowledge about detailed resource availability from one operator to other.

## Slide 6: Interconnect between ECS-ERs
ECS-Edge Repository (ECS-ER) is a specialized/elevated ECS with added functionalities for roaming and federation
ECS-ER maps to
  Federation Manager Role as defined by GSMA OPG
  MEC Federator as defined by ETSI ISG MEC
  Receiving and storing information about edge computing resources from other ECS(s) of the ECSP;
  Receiving and storing information about edge computing resources from other ECS-ER(s) of the federation;
  Providing information about Edge computing resources to other ECS-ER(s) of the federation.

## Slide 7: Architecture option for Edge Node Sharing
Option#10 in TR 23.700-98
  Provides interface between ECS-ERs for Edge Node Sharing (E/WBI functionalities)
    EDGE-18 is used for sharing of shared node information (EAS information and associated EES information) among the two OPs

## Slide 8: IE/WBI interface between two OPs
EDGE-18 is required between two ECS-ER or ECS-ER and MEC Federator (MEF) belonging to two OPs
Based upon the previous discussion, EDGE-18
  Should not expose any internal details about OP
  Should have clear separation from other interfaces within OP.
  Should be aligned with interface provided by ETSI MEC (Mff).
OP-A
OP-B
  Need to provide security and management capabilities (in the scope of SA3 and SA5 respectively.)
MEF
ECS-ER
EDGE-18

## Slide 9: Conclusion
EDGE-18 aligns with GSMA E/WBI requirements and mandate of “Separation of Concern”
EDGE-18 can be used to provide list of services as defined by GSMA.
EDGE-18 can align with/reuse Mff as defined by ETSI ISG MEC.