3GPP TSG-SA WG6 Meeting #28	S6-190239

Kochi, India, 21th – 25th January 2019	(revision of S6-190066)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.280 | CR | 0176 | rev | 1 | Current version: | 15.4.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | x | Radio Access Network |  | Core Network | x |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Correction of emergency location triggering criteria |
| --- | --- |
| Source to WG: | BDBOS |
| Source to TSG: | SA6 |
| Work item code: | enhMCPTT |  | Date: | 2019-01-23 |
| Category: | F |  | Release: | Rel-15 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | Correction of missing information element in the location reporting configuration and location reporting trigger as described in clauses 10.9.2.1 and 10.9.2.4. Related requirement in 3GPP TS 22.280 [R-5.11-013] The MCX Service shall provide a means for an MCX UE to send a Location information update whenever a trigger condition is satisfied while the MCX User is in MCX Service Emergency State (e.g., initial registration, distance travelled, elapsed time, cell change, tracking area change, PLMN change, MCX Service communication initiation). NOTE 1: The Location information update triggers for an MCX User in an MCX Service Emergency State might be different than the Location information update triggers used when the MCX User is not in an MCX Service Emergency State. |
| Summary of change: | Additionally to the already existing information element "triggering criteria in non-emergency cases", the corresponding information element "triggering criteria in emergency cases" is added to the location reporting configuration and location reporting trigger. |
| Consequences if not approved: | Location triggering criteria in emergency cases cannot be configured. |
| Clauses affected: | 10.9.2.1, 10.9.2.4 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

******* First Change *******

#### 10.9.2.1	Location reporting configuration

Table 10.9.2.1-1 describes the information flow from the location management server to the location management client for the location reporting configuration.

Table 10.9.2.1-1: Location reporting configuration

| Information element | Status | Description |
| --- | --- | --- |
| MC service ID | M | Identity of the MC service user to which the location reporting configuration is targeted. |
| Requested non-emergency location information | O (NOTE) | Identifies what location information is requested, except for emergency or imminent peril calls or emergency alerts |
| Requested emergency location information | O (NOTE) | Identifies what location information is requested, for emergency or imminent peril calls or emergency alerts |
| Triggering criteria in non- emergency cases | O (NOTE) | Identifies when the location management client will send the location report in non-emergency cases |
| Triggering criteria in emergency cases | O (NOTE) | Identifies when the location management client will send the location report in emergency cases |
| Minimum time between consecutive reports | O (NOTE) | Defaults to 0 if absent and 0 for emergency calls, imminent peril calls and emergency alerts |
| NOTE: If none of the information element is present, this represents a cancellation for location reporting. |

******* Second Change *******

#### 10.9.2.4	Location reporting trigger

Table 10.9.2.4-1 describes the information flow from the location management client to the location management server for triggering a location reporting procedure.

Table 10.9.2.4-1: Location reporting trigger

| Information element | Status | Description |
| --- | --- | --- |
| MC service ID | M (NOTE 1) | Identity of the requesting authorized MC service user (e.g. MCPTT ID, MCVideo ID, MCData ID) |
| MC service ID | M (NOTE 1) | Identity of the requested MC service user (e.g. MCPTT ID, MCVideo ID, MCData ID) |
| Immediate Report Indicator | O (NOTE 2) | Indicates whether an immediate location report is required |
| Requested non-emergency location information | O (NOTE 2) | Identifies what location information is requested, except for emergency or imminent peril calls or emergency alerts |
| Requested emergency location information | O (NOTE 2) | Identifies what location information is requested, for emergency or imminent peril calls or emergency alerts |
| Triggering criteria in non- emergency cases | O (NOTE 2) | Identifies when the client will send the location report in non-emergency cases |
| Triggering criteria in emergency cases | O (NOTE 2) | Identifies when the client will send the location report in emergency cases |
| Minimum time between consecutive reports | O (NOTE 2) | Defaults to 0 if absent and 0 for emergency calls, imminent peril calls and emergency alerts |
| NOTE 1: The identity of the requesting MC service user and the requested MC service user should belong to the same MC service. E.g. if requesting MC service user is using a MCPTT ID, then the requested MC service user identity should be an MCPTT ID. NOTE 2: At least one of these rows shall be present. |

******* End of Change *******