3GPP TSG-SA WG6 Meeting #38-e meeting	S6-200994r1

20th – 31st July 2020	(revision of S6-200994)

Source:	one2many

Title:	Pseudo-CR on FS 5GMARCH Correction for broadcast scenarios

Spec:	3GPP TR 23.700-24 v0.6.2

Agenda item:	8.6

Document for:	Approval

Contact:	Peter Sanders (peter.sanders@one2many.eu)

# 1. Introduction

SA1 has clarified in its LS in S6-200969 that "broadcast to all UEs in the service area" means all UEs that support receiving the broadcast message and not all UEs regardless if they support the broadcast message. This implies that distributing the broadcast message via SMS or any non-3GPP transport is removed from the broadcast message scenarios.

As defined in section 4.1 broadcast is supported only by Legacy 3GPP type UEs, derived from UE type C in TS 22.262. This implies that broadcast to non-3GPP type UEs is not supported and scenarios 4.3 and 4.4 are removed and that UE B type devices are removed from the scenarios.

In scenario 4.5 (4.3 after the modification) the Application Server connects to the 5GMSG Server via a 5GMSG Gateway. Such a broadcast scenario is not required in TS 22.262 and is removed.

# 2. Reason for Change

This pCR implements the information received from SA1 in S6-200969 and applies corrections based on SA6 agreements after the scenarios were written, such as those listed in section 4.1.

# 3. Conclusions

<Conclusion part (optional)>

# 4. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-24 v0.6.2.

* * * First Change * * * *

## 4.5	Scenario 4: Broadcast message

### 4.5.1	Scenario 4.1: Message Broadcast from MSGin5G Server

This scenario describes the case where an APP Server in the network communicates with Controlled UE C by using MSGin5G service via broadcast.

The message will be routed via the 5G system from the APP Server to UE C. The scenario is illustrated in figure 4.5.1-1.

UE C is connected to the 5G system and supports broadcast.

Figure 4.5.1-1: Message Broadcast from APP Server to UEs

Editor's Note: The Figure 4.4.1-1 merges the changes from S6-200612 and S6-200614. The UEs name need to be updated according to S6-200614.

The scenario consists of the following aspects:

-	The message is originated by authorized APP Server and the APP Server also provides the service area information.

-	The MSGin5G Server forwards the 5GMSGS message to the 5G System, which takes care of broadcasting the message in the designated service area.

-	UEs  that support the MSGin5G Service and are located in the service area and configured to receive the message will receive it via broadcast.

### 4.5.2	Scenario 4.2: Message Broadcast initiated from 5GMSGS UE

This scenario describes the case where Controller UE1 (e.g. a mobile handset Terminal 1, or an application client APP 1 in a mobile handset Terminal 1) communicates with Controlled UE C via broadcast.

The message will be routed via the 5G system from the APP in UE1 to UE C. The scenario is illustrated in figure 4.5.2-1.

Figure 4.5.2-1: Message Broadcast from APP in UE1 to UEs2

Editor's Note: The Figure 4.4.1-1 merges the changes from S6-200612 and S6-200614. The UEs name need to be updated according to S6-200614.

The scenario consists of the following aspects:

-	The message is originated by authorized APP in UE1 and the APP also provides the service area information.

-	The MSGin5G Server forwards the 5GMSGS message to the 5G System, which takes care of broadcasting the message in the designated service area.

-	UEs2 that support the MSGin5G Service and are located in the service area and configured to receive the message will receive it via broadcast.

### 4.5.3	Scenario 4.3: Message broadcast from non-3GPP Message Service to 5GMSGS UEs

This scenario describes the scenario where Non-3GPP UE1  (e.g. OMA LWM2M specified in OMA OMA-ERELD-LightweightM2M [5]) delivers a broadcast message by using non-3GPP Message service to 5GMSGS UEs2 (e.g. a mobile handset terminal 1 or an application client APP 1 in a mobile handset Terminal 1) which is configured according to application policy.

5GMSGS UEs2 connected to 5G system and served by MSGin5G server. The 5GMSGS message and non-3GPP message will be translated by the MSGin5G gateway. The scenario is illustrated in figure 4.5.3-1.

Figure 4.5.3-1: Message broadcast from non-3GPP message service to 5GMSGS UE

The scenario consists of the following aspects:

-	If broadcast message is originated by authorized Non-3GPP UE1, the 5GMSG Server broadcasts the message to all the UEs. 5GMSGS UEs may send the delivery status back to Non-3GPP UE1 or APP Server.