3GPP TSG-SA WG6 Meeting #40-e	S6-202061_rev2

e-meeting, 16th – 24th November 2020	(revision of S6-20xxxx)

Source:	Huawei, Hisilicon

Title:	Corrections on solution of MOAT messaging

Spec:	3GPP TR 23.700-24 v1.1.0

Agenda item:	8.5

Document for:	Approval

Contact:	Hongxia Hao, haohongxia@huawei.com

1. Introduction

Just for small corrections.

2. Reason for Change

3 "application client" should be "application server".

3. Conclusions

4. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-24 v1.1.0.

* * * First Change * * * *

#### 6.22.1.1	MSGin5G UE sending/replying a message to Application Server

Figure 6.22.1.1-1 shows the solution of a MSGin5G UE sending/replying a message to an APP Server.

Pre-conditions:

1)	The APP Server and MSGin5G Client in MSGin5G UE has registered with the MSGin5G server.

Figure 6.22.1.1-1: MSGin5G UE sending/replying a message to App Server

1)	The MSGin5G UE sends an MSGin5G message request to MSGin5G Server through 5GC. The delivery report is requested in the message.

Table 6.22.1.1-1: MSGin5G message request

| Information element | Status | Description |
| --- | --- | --- |
| Originator MSGin5G service ID | M | The service identity of the sender sending the message. |
| AS service ID | M | The service identity of the recipient (i.e. application server) receiving the message. |
| Message ID | M | Unique identifier of this message |
| Delivery report | O | Indicates if delivery acknowledgement is requested |
| Application Client ID | O | Identifies the application for which the payload is intended. |
| Payload | M | Payload of the message |

NOTE 1:	If the delivery report is not requested this procedure will stop after step 3 and step 4 will not be needed.

2)	The MSGin5G Server sends the application request to the target App Server for delivering message payload.

NOTE 2:	The application request can be any request (e.g. API request) supported by the App Server.

3)	The App Server sends a response corresponding to the application request in step 2.

4)	Based on the response in step 3, the MSGin5G Server sends the MSGin5G message delivery report to the MSGin5G UE based on the received delivery status in step 3.

#### 6.22.1.2	Legacy 3GPP UE replying a message to Application Server

Figure 6.22.1.2-1 shows the solution of a SMS UE (i.e. a Legacy 3GPP UE with SMS Client) replying a message to an APP Server.

Pre-conditions:

1)	APP Server and SMS Client in SMS UE has registered with the MSGin5G server.

2)	The SMS UE received a message from the App Server.

3)	The Legacy 3GPP message gateway is aware of the SMS client and provides the mapping to MSGin5G service ID.

4)	The SMS UE replies to the MSGin5G UE upon receiving the message from the APP Server.

Figure 6.22.1.2-1: SMS UE replies to App Server

1)	The SMS UE sends an SMS message request to the Legacy 3GPP Message Gateway through SMSC according the procedure in 3GPP TS 23.204 [15] or the procedure in clause 4.13.3 of TS 23.502 [10]. The delivery report is requested in the message.

NOTE 1:	If the delivery report is not requested this procedure will stop after step 4 and step 5 to 6 will not be needed.

2)	The Legacy 3GPP Message Gateway translates the SMS message to MSGin5G message with delivery report requested and sends a MSGin5G message request to the MSGin5G Server, including the IEs of MSGin5G message according to the table 6.22.1.2-1.

Table 6.22.1.2-1 MSGin5G message request

| Information element | Status | Description |
| --- | --- | --- |
| Originator MSGin5G service ID | M | The service identity of the sender sending the message. |
| AS service ID | M | The service identity of the recipient (i.e. application server) receiving the message. |
| Message ID | M | Unique identifier of this message |
| Delivery report | O | Indicates if delivery acknowledgement is requested |
| Application Client ID | O | Identifies the application for which the payload is intended. |
| Payload | M | Payload of the message |

3)	The MSGin5G Server sends the application request to the target App Server for delivering message payload.

NOTE 2:	The application request can be any request (e.g. API request) supported by the App Server.

4)	The App Server sends a response corresponding to the application request in step 3.

5)	Based on the response in step 4, the MSGin5G Server sends the MSGin5G message delivery report to the Legacy 3GPP Message Gateway based on the received delivery status from App Server.

6)	The Legacy 3GPP Message Gateway translates the MSGin5G message delivery report to a SMS message delivery report and sends it to the SMS Client through SMSC.

#### 6.22.1.3	Non-3GPP UE replying a message to Application Server

Figure 6.22.1.3-1 shows the solution of a Non-3GPP UE (e.g. RCS, LwM2M) replying a message to a MSGin5G UE.

Pre-conditions:

1)	APP Server and Non-3GPP UE has registered with the MSGin5G server.

2)	The Non-3GPP UE received a message from the App Server.

3)	The Non-3GPP Message Gateway is aware of the Non-3GPP message client on the Non-3GPP UE and provides the mapping to MSGin5G service ID.

4)	The Non-3GPP UE replies to the App Server upon receiving the message from the App Server.

Figure 6.22.1.3-1: Non-3GPP UE replies to MSGin5G UE

1)	The Non-3GPP message client in Non-3GPP UE sends a Non-3GPP message request to the Non-3GPP Message Gateway. The delivery report is requested in the message.

NOTE 1:	If the delivery report is not requested this procedure will stop after step 4 and step 5 to 6 will not be needed.

2)	The Non-3GPP Message Gateway translates the Non-3GPP message to MSGin5G message with delivery report requested and sends a MSGin5G message request to the MSGin5G Server, including the IEs of MSGin5G message according to the table 6.22.1.3-1

Table 6.22.1.3-1: MSGin5G message request

| Information element | Status | Description |
| --- | --- | --- |
| Originator MSGin5G service ID | M | The service identity of the sender sending the message. |
| AS service ID | M | The service identity of the recipient (i.e. application server) receiving the message. |
| Message ID | M | Unique identifier of this message |
| Delivery report | O | Indicates if delivery acknowledgement is requested |
| Application Client ID | O | Identifies the application for which the payload is intended. |
| Payload | M | Payload of the message |

3)	The MSGin5G Server sends the application request to the target App Server for delivering message payload.

NOTE 2:	The application request can be any request (e.g. API request) supported by the App Server.

4)	The App Server sends a response corresponding to the application request in step 3.

5)	Based on the response in step 4, the MSGin5G Server sends the MSGin5G message delivery report to the Legacy 3GPP Message Gateway based on the received delivery status from App Server.

6)	The Non-3GPP Message Gateway translates the MSGin5G message delivery report to a SMS message delivery report and sends it to the Non-3GPP message client.

* * * Next Change * * * *

<Proposed change in revision marks>

* * * Next Change * * * *

<Proposed change in revision marks>