3GPP TSG-SA WG6 Meeting #40-e	S6-202220_Rev1

e-meeting, 16th – 24th November 2020	(revision of S6-202220)

Source:	Samsung

Title:	Pseudo-CR on EN gateway translation

Spec:	3GPP TR 23.700-24 V1.1.0

Agenda item:	8.5

Document for:	Approval

Contact:	Basavaraj (Basu) Pattan (basavarajjp@samsung.com)

1. Introduction

This pCR proposes resolving some of the editor's notes as per the discussion during [Pre-SA6#40-e conference call] 5GMARCH call #2 held on 5th Nov, 2020.

2. Reason for Change

Following editor's notes is resolved in this pCR:

| EN # | Clause # | EN | Reasoning |
| --- | --- | --- | --- |
| 19 | 6.5.1.5 | Legacy 3GPP message client receives message from group | Editor's Note: Step 1 needs to be aligned with SA1 requirement related to translation of MSGin5G message to legacy 3GPP message is revised. | Translation is Gateway functionality as discussed in other solutions. |

3. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-24 v1.1.0.

* * * First Change * * * *

#### 6.5.1.5	Legacy 3GPP message client receives message from group

Figure 6.5.1.5-1 shows the procedure for Legacy 3GPP message client to receive message from group.

Pre-conditions:

1)	Based on service ID, an application server has received the group message from the originator.

2)	The MSGin5G server is aware of the UE type (determined by service ID) which is Legacy 3GPP message client.

3)	The MSGin5G server has received the message to send to target UE.

# Figure 6.5.1.5-1: Legacy 3GPP message client receives a message from the group

1)	The MSGin5G server sends the Group Message Request to the MSGin5G Gateway. The information elements defined in Table 6.5.1.4-1 are included in the request.

2)	The Legacy 3GPP message gateway translates the MSGin5G Group message to legacy 3GPP message (e.g. SMS).

3) The Legacy 3GPP message gateway sends legacy 3GPP message (e.g. SMS) to 3GPP Message Client.

4) The 3GPP Message Client delivers the contents of the legacy 3GPP message (e.g. SMS) to the targeted Application Client.

* * * Next Change * * * *