## Slide 1: Linked EAS with good QoS
Wenliang Xu (Ericsson)

## Slide 2
Linked EAS requirements (from KI#18)
However, to provide services to the end user a typical AC communicates with multiple endpoints i.e., multiple EASs. This creates a linkage between these EASs, which impacts the support provided by the Edge Enabler Layer. Taking an example of an online game where to support large number of users, different game functions are split across multiple servers; like, a game engine for game state and user input management, in-game chat server for communication between players and a capture server for capturing rendered images, encoding, and transporting them to the player's device.
If each of these EASs are discovered, controlled, and relocated individually, it may impact the overall quality of service. e.g. ACR failing for the game engine should cancel the ACR of the capture server to maintain their proximity.

## Slide 3
The Key Point is that the AC can still enjoy good QoS during mobility and in this case, the linked EAS doesn’t need to be relocated together when UE moves to non-overlapping area in EDN2.
For the example used in KI:
e.g. ACR failing for the game engine should cancel the ACR of the capture server to maintain their proximity.
It has conditions not revealed clearly. E.g. when EAS chat is selected in EDN1 and successful ACR is performed to EDN2, but no suitable EAS game is available in EDN2, why to fallback to EAS chat in EDN1? Noting that the EAS game & chat in EDN1 cannot serve the AC anymore due to service area limitation.