## Slide 1: Why base stations need to recognise MCPTT group calls as half duplex?
Nathan Jeyaratnarajah
Delegate, Home Office UK

## Slide 2: Outline
Problem statement
Gaps in the existing ideas
Potential solution
The benefits
Summary

## Slide 3: Problem statement
MCPTT duplex mode is transparently signalled between MCPTT client and MC application server (MC AS)
So, eNodeB/gNodeB cannot determine between half duplex and full duplex call legs
eNodeB/gNodeB cell radio resource management functions consider MC voice communication call legs as full duplex
As a result, MCPTT group call cell capacity is lower than possible
Example at cell edge for a 5MHz carrier, group call leg cell capacity is min(50DL/12UL)= 12 call legs
  3x4-member group calls as opposed to 12x4-member group calls

## Slide 4: Gaps in the existing ideas 1/2
One idea is the use of multicast GBR for DL and unicast GBR for UL
UL unicast radio bear (GBR) is established for a group call, it stays allocated to the UE for the entire duration of the group call
A few suggestions to solve the UL capacity issue
  Only talker UE is dynamically setup and released UL GBR by MC AS
    Practically adds delays in the start of every talk spurts due to UL GBR bearer setup time
    Increased signalling (quick allocation, release and reuse of resources) in RAN and Core
  Keep UEs near cell centre in RRC idle mode and multicast receive only mode.
    For UL communication, transition to RRC idle to RRC connected mode and UL GBR bearer setup can take a long transition time. ESN keeps all UEs in RRC connected mode and prefers persistent UL GBR bearer
  Higher admission control (overbooking) threshold for both UL & DL or for UL only
    Overbooking applies to both full duplex and half duplex calls
    QoS issues can arise to admitted calls due to blind approach

## Slide 5: Gaps in the existing ideas 2/2
Another idea is a monitoring solution for handling events and conditions
This solution is predicated on the RAN/Core Network identifying and reporting the relevant conditions and events
Events and conditions impacting MC AS
  pre-emption of radio bearers or UEs
  congestion
  traffic shaping resulting in dropping of packets by the core network or RAN
  mobility events
  reports of bad RF from certain UEs
MC AS may effect some of the UEs in the cells reported to have high congestion to transition to receive data in idle mode in order to avoid the chance of the UEs being pre-empted.
Reactive approach after QoS has been degraded and allows further degradation of QoS in different ways

## Slide 6: Potential solution
A potential solution
  MC AS notifies a pseudo MCPTT group ID (not actual) for each call leg/group to the base station through RAN and Core interfaces
eNodeB/gNodeB cells can derive the following information from the pseudo MCPTT group ID
  Whether an incoming call is a half duplex call leg or a full duplex call leg
  Any incoming calls belonging to the same call group or different call groups
  The number of call legs per call group per eNodeB/gNodeB cell
Half duplex group calls are setup for DL/UL but resources are allocated for one UL resource/group/cell in admission control and other RRM function decisions

## Slide 7: The benefits
The base stations are accurately informed whether a call leg is full duplex and half duplex
Increases MCPTT group call capacity for both multicast and unicast scenarios without compromising mission critical QoS
A proactive approach and no need to wait to see QoS degradation
No early degradation of QoS measures like sending UE to RRC idle
Reduction in end-to-end signalling
A streamlined RRM functionality across different RAN vendors leading to better interoperability

## Slide 8: Summary
Since e/gNodeB cells treat each half duplex (MC)PTT group call legs as full duplex 1-2-1 calls, the base station capacity of (MC)PTT group calls is a lot less
The suggestions in the standards and elsewhere allow QoS degradation to increase capacity
If an e/gNodeB cell has pseudo group ID information, it can reliably work out half duplex mode, the number of call legs from the respective groups to improve RRM functions and base station cell MCPTT group call capacity.
The standardisation work is required in MC AS, Core and RAN sides