## Slide 1: SA6 Rel-19: Discussion on Network enabler for XR service
May, 2023
Shaowen Zheng (CMCC)

## Slide 2: Outline
FS_AEXRS Rel-19 SID/WID Template
Annex A: Background and motivation
Annex B: Potential use case

## Slide 3: FS_AEXRS-1/3
Continuation or New Item: New Item
Study Item/Work Item/Both: Both
Source of requirements: requirements and use cases from SA1, and XRM solution has been developed by SA2,
Expected Output: new TR+TS, and also some existing TS
Anticipated start date/meeting: Aug. 2023 SA6#56
Target Completion: Jun. 2024 SA#104
Estimated TUs: 5TUs(SID)+5TUs(WID)
Rapporteurship: Zheng, Shaowen, China Mobile, zhengshaowen@chinamobile.com
Supporting IMs: AsiaInfo, CATT, ZTE
Rel-19 SID/WID Proposal Slide Template

## Slide 4: FS_AEXRS-2/3
Description:
  The XR (Extended Reality) Services refer to a general service catalog, including High Data Rate Low Latency (HDRLL) services, AR/VR/XR services, and tactile/multi-modality communication services. SA1 defines the requirement for XR relevant Services, including tactile and multi-modal communication service in the TS 22.261 clause 6.43, FS_Metaverse in TR 22.856. Based on these requirements, to support the XR Services , both SA2 and SA4 have related directions. XRM in SA2 studies the key issues, solutions on how to support XR and advanced media services from 3gpp architecture perspective. SA4 focus more on the application layer interaction between the UE and media/audio service server. However, it is not yet clear how the XR service, which are not limited to media/audio services, can be supported by network enabler layer based on the 3GPP system.
  Goals:
    To study how SA6 enablement layer can support the XR service to enhance the QoS of XR service, with the following objectives:
      a.Identify architecture requirements and solution for generic/specific architecture based on SEAL to support the XR;
      b.Identify key issues,and solution recommendations to enable capabilities for XR and Metaverse/Media including:
        Support seamless XR streaming over 3GPP or none-3GPP devices (Wi-Fi-enabled device for instance) ,
        Split computing, principle of computing task/content splitting to enable split rendering, split modeling etc.
        Potential CAPIF/SEAL enhancement to support the XR service register, discovery and association(based on service, and/or presence reporting area)
        Service associated information provisioning with the help of enabler, e.g. XR service ID provisioning,
        PDU/flows coordination, including PDUs information/flow ID provisioning, delay difference handling;
        Information measurement and extraction, e.g. traffic periodicity etc,
        What and how to convey the information extracted from the application layer to 3GPP to enhance the QoS and support the features of SA2
        NOTE: potential enhancement to transport layer may need to coordinate with CT groups.
Rel-19 SID/WID Proposal Slide Template

## Slide 5: FS_AEXRS-3/3
Dependency on other working groups:
  None
Impacts to 3GPP/Industry work if this is not accepted into Rel-19:
  If not accepted, the gap between the 5GC XRM features and the Vertical application layer remains, which may leads to the XR service not satisfying as expected

## Slide 6: Background and motivation
SA1
R17: tactile and multi-modal communication service
R18: FS_Metaverse
R18: XRM
R18: FS_SmarTAR
R18: MeCAR
R18: SR_MSE
R16: FS_5GXR
R17: FS_ 5GSTAR
provide policy(ies) for flows associated with an application
apply 3rd party provided policy(ies).
precise location triggered information provisioning,
management of the spatial anchor
management of the digital assets
...
AF information provisioning: common ID, PDU Set related assistance information including PDU Set QoS parameters, Burst periodicity, Description of Service Protocol.
Network information exposure: congestion level information, Data rate, delay difference and round trip delay of QoS flow, Estimated bandwidth.
  Based on the requirement from SA1, XRM in SA2 studies the key issues, solutions on how to support XR and advanced media services from 3gpp architecture perspective. SA4 focus more on the application layer interaction between the UE and media/audio service server. However, it is not yet clear how the XR service, which are not limited to media/audio services, can be supported by network enabler layer based on the 3GPP system.
SA4
SA2

## Slide 7: The tactile and multi-modal communication service
The tactile and multi-modal communication service may include multiple types of flows from multiple type of dervices, e.g. video/audio stream, and haptic or sensor data for more immersive experience
Requirement from 22.261 for tactile and multi-modal communication service:
  The 5G system shall enable an authorized 3rd party to provide policy(ies) for flows associated with an application. The policy may contain e.g. the set of UEs and data flows, the expected QoS handling and associated triggering events, other coordination information.
  The 5G system shall support a means to apply 3rd party provided policy(ies) for flows associated with an application.
Possible objective:
  How to help 3rd party to provide policy(ies) for flows associated with an application, e.g. information (e.g., I、B、P frame, time stamp) extraction and provisioning to 5GC,
  What and how to apply 3rd party provided policy(ies) for flows associated with an application, e.g. PDU/flows coordination, delay difference handling

## Slide 8: Supporting multi-service coordination in one mobile metaverse
As John is painting and enjoying the live show at the same time, the coordination between video flow, audio flow in live music mobile metaverse service and the video flow and tactile flow in painting mobile metaverse service need to be coordinated. This coordination information need to be share with the network for policy modification.
[PR 5.8.6-1] The 5G system shall provide the capability of coordination between different mobile metaverse services to prevent poor user experience due to conflicting XR media.
Requirement from SA1:
Requirement for SA6:
  Whether and how the enabler helps to discover and associsate the multiple services?
  Whether and how the enabler could help the interaction between AF and 5GC to do the QoS coordination between multiple QoS flows from multiple services?
Possible objective:
  Potential CAPIF/SEAL enhancement to support the XR service register, discovery and association(based on service, and/or presence reporting area)
  Service associated information provisioning with the help of enabler, e.g. XR service ID provisioning,

## Slide 9: Immersive Live concert
Large amount of computing resouces is needed to perform real-time processing for audio, video, and interactive data, etc. Considering different customers will use terminals e.g. XR glasess with different brands and different processing capabilities, some of the glasses will not have enough computing resources to perform the real-time rendering. Through split rendering, most of the computing work task can offload to the network, the high speed and low latency transmission provided by 5G system can cooperate with the edge cloud side for real-time rendering, and combine with the local optimized rendering of the XR terminal side to provide the immersive and unbounded XR experience.
Table 7.6.1-1 KPI Table for additional high data rate and low latency service
Use Cases | Characteristic parameter (KPI) |  |  | Influence quantity | 
 | Max allowed end-to-end latency | Service bit rate: user-experienced data rate | Reliability | UE Speed | Service Area(note2)
Cloud/Edge/Split Rendering(note 1) | 5ms(i.e. UL+DLbetween UE and the interface to data network) (note 4) | 0,1 to [1] Gbit/s supportingvisualcontent(e.g. VR based or high definition video)with 4K, 8K resolution and up to120 frames per second content. | 99,99 % in uplink and 99,9 % in downlink (note 4) | Stationary or Pedestrian | Countrywide
Requirement from SA1:
Requirement for SA6:
  Whether and how the enabler could help to meet the high data rate and low latency requirement of XR service via spliting the computing and/or rendering task based on the collected location and network status
Possible objective:
  Split computing, principle of computing task/content splitting to enable split rendering, split modeling etc.

## Slide 10: SA 2 solutions and exiting gaps
SA 2 solution: The AF may allocate the same Multi-modal Service ID to all UE PDU sessions that compose a multi-modal service. The PCF may take this information into account (e.g. to allocate a specific QoS profile) when processing each PDU session independently. The data flows that contribute to the service experience, but may still be valid stand-alone, may be transmitted over separate PDU sessions from multiple UEs.
Gap: how the Multi-modal Service ID is allocated is not clear.
Possible objective: Multi-modal Service ID provisioning.
SA 2 solution: AF may provision one or more of the following PDU Set related assistance information to NEF/PCF during AF QoS request procedure: Burst periodicity etc. NOTE 2: How the UPF derives periodicity when not provided by the AF is implementation dependent.
Gap: How the periodicity is provided when not provided by the AFis not clear.
Possible objective: Traffic periodicity calculating.

## Slide 11: Potential objectives
  a.Identify architecture requirements and solution for generic/specific architecture based on SEAL to support the XR;
  b.Identify key issues,and solution recommendations to enable capabilities for XR and Metaverse/Media including:
  Support seamless XR streaming over 3GPP or none-3GPP devices (Wi-Fi-enabled device for instance) , e.g., data pre-processing, or a virtual driver to enable seamless XR streaming, etc,
  Split computing, principle of computing task/content splitting to enable split rendering, split modeling etc.
  Potential CAPIF/SEAL enhancement to support the XR service register, discovery and association(based on service, and/or presence reporting area)
  Service associated information provisioning with the help of enabler, e.g. XR service ID provisioning,
  Information measurement, and exposure to the VAL, e.g. traffic periodicity etc,
  How to help 3rd party to provide policy(ies) for flows associated with an application, e.g. information extraction and provisioning to 5GC,
  What and how to apply 3rd party provided policy(ies) for flows associated with an application, e.g. PDU/flows coordination, delay difference handling
  NOTE: potential enhancement to transport layer may need to coordinate with CT groups.
enabler for XR service
5GC
PCF/NEF
UE
VAL 2
UPF
CAPIF
data flow
signaling
Notes: XR service 打卡看看
分一分哪些是XR specific
动态的分离渲染可行性；实现上

## Slide 12: Thanks