## Slide 1: Discussion on bundle EAS and composite EAS
Yajie
Huawei, Hisilicon

## Slide 2
Issue: The EES/ECS cannot distinguish composite EAS and bundle EAS
EES’s operation on EAS discovery:
Bundle EAS: The EES need to send the all the EAS including the EAS#1 and EAS#2 to the EEC
  Composite EAS: The EES only need to send the main EAS (i.e. EAS#1) to the EEC
  Issue: The EES cannot determine whether to return all the EASs or only return main EAS to the EEC
ECS’s operation on EES discovery:
Bundle EAS: The ECS need to send the all the EESs supporting EAS#1 and EAS#2 to the EEC
  Composite EAS: The ECS only need to send one EES which supporting main EAS (i.e. EAS#1) to the EEC
  Issue: The ECS cannot determine whether to return all the associated EESs or only return main EES to the EEC
EAS#1
EAS#2
AC
Association ID
(EASID#1EASID#2
or ID#1)
EAS#1
EAS#2
AC
AC profile | EAS profile
ACID | EASID
Association ID (EASID#1EASID#2 or ID#1) | Association ID (EASID#1EASID#2 or ID#1)
EAS ID list | Association ID (EASID#1EASID#2 or ID#1)
Bundle requirement | List of EAS ID
Bundle EAS and composite EAS
Bundle EAS
Composite EAS
Association ID
(EASID#1EASID#2
or ID#1)

## Slide 3
Way forward
OPTION#1: Using different ID (i.e. bundle ID or composite ID) to indicate different EAS combination case (bundle EAS or composite EAS)
OPTION#2: using same association ID but add different type (bundle EAS, composite EAS) to distinguish the different EAS combination (bundle EAS or composite EAS)

## Slide 4
Thanks