## Slide 1: Discussion on support multiple service API invocation requests for CAPIF and RNAA
Junpei Uoshima
NTT DOCOMO, INC.

## Slide 2: Issues on support multiple service API invocation requests for CAPIF and RNAA
Currently, It seems that the specification of CAPIF and RNAA do not take into account the case where multiple API invocation requests are received.
For example, the current specification of CAPIF and RNAA cannot support the following cases.
  Different applications on same UE
    Game application A and video transmission application B on same UE
  Different application on different UE with same network(one API Invoker)
    Game application A and video transmission application B on different UE under mobile Wi-Fi.
  Different application on different UE with same network(multiple invokers)
    Game application A and video transmission application B on different UE under mobile Wi-Fi.

## Slide 3: Case1 : Different applications on same UE
Game application A and video transmission application B on same UE
  1.First game application sends service API invocation.
  2.After that, second video transmission application B also sends service API invocation but the specification is not clear.
UE
API
Invoker
Resource Owner
Function
CCF
AEF
APF
AMF
Game app A
Video transmission app B
1. service API invocation
2. service API invocation
This specification is not clear
(rewrite? or reject?)

## Slide 4: Case2 : Different application on different UE with same network(one API Invoker)
Game application A and video transmission application B on different UE under mobile Wi-Fi.
  1.First game application sends service API invocation.
  2.After that, second video transmission application B sends service API invocation but the specification is not clear.
UE A
API
Invoker
Resource Owner
Function
CCF
AEF
APF
AMF
Game app A
Video transmission app B
This specification is not clear
(rewrite? or reject?)
UE B
Same
network
1. service API invocation
2. service API invocation

## Slide 5: Case3 : Different application on different UE with same network(multiple invokers)
Game application A and video transmission application B on different UE under mobile Wi-Fi.
  1.First game application sends service API invocation.
  2.After that, second video transmission application B also sends service API invocation but the specification is not clear.
UE A
API
Invoker
Resource Owner
Function
CCF
AEF
APF
AMF
Game app A
Video transmission app B
This specification is not clear
(rewrite? or reject?)
UE B
API
Invoker
Same
network
1. service API invocation
2. service API invocation

## Slide 6: Summary
It is proposed to support multiple API invocation requests for CAPIF and RNAA.
This enhancement increases the value of CAPIF by addressing the needs of various developers.