## Slide 1: R19 MC GWUE fixup
Cuili Ge
Huawei, Hisilicon

## Slide 2: Content
Issues in R19 current form
How to resolve ?

## Slide 3: Issues in R19 current form
Issues
  A peer application layer functional entity is required in the MC gateway UE to handle the signallings from the MC client hosted by the non-3GPP device.
  The identity of the MC service user is not aligned with existing identity management mechanism
Observation#1 – No peer application functional entity in MC gateway UE and reference point to the MC service client and CSC client @non-3GPP device
Observation#2 – There are signaling exchanged between the MC gateway UE and the MC service client and CSC client @non-3GPP device
Observation#3 – Identity of the MC service user is not correct
Information element | Status | Description
GW MC service ID | M | The GW MC service ID of the requesting MC service user

## Slide 4: How to resolve ?
New application functional entity in MC gateway UE
New reference points
3. The MC service client has already obtains its identity during the identity authentication interactions with IDM server where the MC gateway UE transparently forwarding those messages b/w MC client and the IDM server.
so the identity of the MC service user should be the MC service ID.
Information element | Status | Description
GW MC service ID | M | The GW MC service ID of the requesting MC service user
GW-local-1
GW-local-2
MC client proxy
Location management messages
MBMS related messages
Handle the signallings from MC client

## Slide 5: Proposals
The corresponding S6-243294/CR0574 should be agreed.