## Slide 1: Discussion on how to link location information subscription and location reporting trigger procedures
Mythri Hunukumbure, Sivasubramaniam Ramanan
UK Home Office

## Slide 2: Current status
In the current TS 23.280 v19.4.0, there is no linkage between the location information subscription and location reporting trigger procedures.
  It was discussed in the pre-meeting (on 5th Sept.) that linking or determining the order of precedence for these two procedures would be useful.
  Samsung proposed a cancel procedure for the client triggered location reporting procedure in SA6 #62 (S6-243307).
  Samsung also proposed (S6-243308) to remove the on-demand (immediate) location reporting feature from the client triggered location reporting.
ESN proposes to link the two procedures while enabling some aspects of the above Samsung CR’s.

## Slide 3: ESN proposal
ESN proposal is noted below for discussion:
  The location information subscription (either for an individual target UE or target UE list or group ID list) by an authorized client (A) should happen before the trigger for reporting is issued.
  A reporting trigger issued by client A should start the reporting procedure.
    Reporting can happen as per a default configuration (stored in the user profile) or the trigger itself can contain a temporary reporting configuration.
    The reporting triggers can be cancelled and re-initiated (may be with different configurations) multiple times, but the location subscription should remain.
  If the location information subscription is cancelled by client A, any current reporting trigger to the same targets will be cancelled along with this.