## Slide 1: Discussion paper on location user profile configuration data
Ericsson
Rana.alhalaseh@ericsson.com

## Slide 2: List of topics for discussion
1. Current configurations related to the requesting MC user and target (requested) MC user
  The related CRs are
    S6-244084 (TS 23.280)
    S6-244085 (TS 23.379)
    S6-244087 (TS 23. 281)
    S6-244088 (TS 23.282)
2. Restrict location info dissemination
  Understand the purpose and use case behind it

## Slide 3: 1. Current configurations
There is an authorization check (and configuration) at LMS for the requesting MC user, when requesting location information of
  A target MC user from the same primary MC system
  A target MC user from a partner MC system
There is no authorization check (and configuration) at LMS if the target MC user is allowed to share its location information
  The LMS always allows the target MC user to share its location information irrespective of the identity of the requesting MC user, e.g., different MC organizations or different MC systems
TS 23.379 v. 19.4.0
TS 23.281 v. 19.4.0
TS 23.282 v. 19.4.0
TS 23.280 v. 19.4.0

## Slide 4: Current Location Information authorization
LMS
Use case: As a police officer Alice, I need to know the location information of Firefighter Bob
Alice
Bob
MC Organization: City Police Org
MC Organization: Fire Brigade
From 23.280 v19.4.0
This list includes MC service ID for Bob
1. Location Request
2. Authorization: Check that Alice is authorized to query Bob’s location
3. Location Request
Limitation:
The Fire Brigade organization must trust that the MC organization; City police correct MC service IDs in the Location user profiles. This becomes even more problematic in a multi system scenario.
From 23.379 -> to 23.280 as it is

## Slide 5: Current Location Information authorization
LMS
Use case: As a police officer Alice, I need to know the location information of Firefighter Bob
Alice
Bob
MC Organization: City Police Org
MC Organization: Fire Brigade
From 23.280 v19.4.0
This list includes MC service ID for Bob
1. Location Request
2. Authorization: Check that Alice is authorized to query Bob’s location
3. Location Request
Limitation:
The Fire Brigade organization must trust that the MC organization; City police correct MC service IDs in the Location user profiles. This becomes even more problematic in a multi system scenario.
From 23.379 -> to 23.280 as it is
Newly added MC user
Caesar
No authorization check is happening at the fire brigade side
The fire brigade organization does not have the mandate to block (or accept) users outsides the fire brigade organization, to send location information requests to its own users.
This has the consequence, that any new vicious MC organization, could easily configure all its users to be able request the location of any other users in the system, even for users under cover.

## Slide 6: Proposed Location Information authorization
LMS
Alice
Bob
MC Organization: City Police Org
MC Organization: Fire Brigade
location user profile data
From 23.379 -> to 23.280 as it is
1. Location Request
2. Authorization
3. Location Request
This list includes MC service ID for Alice
a) Check that Alice is authorized to send location information requests
b) Check that Bob is willing to share his location
Each MC organization controls the authorization to share location information with other MC org’s MC users.
Provides better support for multi system scenarios.
From 23.280 v19.4.0
This list includes MC service ID for Bob

## Slide 7: 2. Restrict location info dissemination
Figure 10.9.3.11-1: Restrict the location information dissemination procedure
We need to understand the use case behind the procedure
The MC user itself creates and manages a “block list”?

## Slide 8: Thank You!