## Slide 1: Discussion on work plan of MMTelAPP
Yue Liu
China Mobile

## Slide 2: Outline
The two LSs received from SA2 clarify the objective and scope of the MMTelAPP WID.
  S6-244008 Reply LS on data channel application related capability exposure
  S6-244009 Reply LS on SA WG6 new work item proposal for MMTel
This Discussion will review the objectives of MMTelAPP WID and related KIs in the study based on the LSs, and suggests the way forward.

## Slide 3: Objective b) Call session related
Objective b) the service enabler layer capability exposure procedures and related APIs, based on architecture and procedures specified in Annex AC.2 of 3GPP TS 23.228 [3] and SA WG2 Rel-18 NG_RTC WID, used in:
I. the call between application without IMS and DCMTSI client; (related to KI#1, KI#3)
II. the Third-Party Call (related to KI#1)
  SA2 concluded not to define any new APIs for IMS session management, e.g., OMA APIs provides such functionality
  Based on the gap analysis of OMA OneAPI framework in clause 4.2 in the TR, IMS data channel is not supported by OMA API
Proposal:
  The related solutions (#2, #6) with necessary modification, i.e. modified based on OMA APIs, and combined with the new SA2 specified IMS DC capability APIs will be considered as the baseline for technical specification.
  The Application may invoke the integrated APIs provided by MMTel Enabler. The MMTel Enabler invokes the OMA API to establish the IMS session and invokes the new API to add DC respectively and gives the final response to the Application

## Slide 4: Objective b) Call session related
III. the multi-party call; (related to KI#8)
  SA2 will not define APIs for application to handle a multiparty call with data channel media
  One solution (Solution#9) is agreed for the KI#08. Based on the EN in Solution#9:
    Editor's note: If SA2 exposes the multi-party call interface that supports DC media in the future, this solution can be directly invoked. Otherwise, this solution may be used as a substitute for the multi-party call solution that supports DC.
  The normative work of KI#8 and Solution#09 can be continued.
Proposal:
  The related solutions (#9) with necessary modification, i.e. modified based on OMA APIs, and combined with the new SA2 specified IMS DC capability APIs will be considered as the baseline for technical specification.
  The Application may invoke the integrated APIs provided by MMTel Enabler. The MMTel Enabler invokes the OMA API to establish the IMS session and invokes the new API to add DC respectively and gives the final response to the Application

## Slide 5: Objective c) DC APP related
c) the necessary application layer architecture and procedures for enabling MMTel service enhanced with Data Channel usage in IMS network, including:
I. controlling the downloading of data channel applications on UE by providing data channel application profile to UE (related to KI#2); and
  II. configuration for the MMTel service, e.g. configuration of the data channel application profile (related to KI#2 and KI#7);
  SA2 the details of HTTP based interactions for DCSF downloading DC applications is not in the scope of SA2
  SA2 has no intention to define this northbound interface of DCAR, which is separated from DC5.
Proposal:
  Regarding the objective c)I. (KI#2), the related solutions#3, #4, #5 will continue to normative work. The DC APP Profile downloads to the MMTel via DCSF (go over the top). When the normative work is finished, we propose to make SA2 refer this procedure in TS23.228 as an optional implementation.
  Regarding the objective c)II. (KI#2 and KI#7) , the related solutions#13 will continue to normative work. The DC APP will be uploaded to DCAR via northbound interface of DCAR (SA6 specified)
MMTel Enabler Server
DCSF/MF
DCAR
Controlling Application Server
MMTel Enabler Client
DCMTSI Client
Upload the DC APP and configure the DC APP Profile
download the DC APP
get the DC APP Profile

## Slide 6: Objective d) value added services
  d) the necessary value added services provided by eMMTel Enabler, e.g. virtual number etc. (related to KI#4 and KI#5)
  SA2 is specifying the authorization/verification of third-party specific caller ID and information (e.g., RCD) that is transported in SIP signalling.
  SA2 will not specify te virtual number.
Proposal:
  Regarding the KI#4 on "support of providing application layer caller information to callee", if no gap on RCD is found, this KI#4 will not go to normative work.
  Regarding the KI#5 on "Support of virtual number", the architecture and solution for this KI can be discussed in normative phase. The architecture and solution for this KI should based on the capabilities provided by OMA APIs and new SA2 specified IMS DC capability APIs.

## Slide 7: Summary
We can continue most of our work to the normative phase except the KI#4 on "support of providing application layer caller information to callee", if no gap on RCD is found.
Calling related APIs
  The IMS Session management capability is provided by OMA API.
  Application invokes the integrated APIs provided by MMTel Enabler. The MMTel Enabler invokes the OMA API to establish the IMS session and invokes the new API to add DC respectively
  DC Application management
  The DC APP will be uploaded to DCAR via northbound interface of DCAR (SA6 can specify)
  The DC APP Profile downloads to the MMTel via DCSF (go over the top). When the normative work is finished, we propose to make SA2 refer this procedure in TS23.228 as an optional implementation.
  value added services
  "support of providing application layer caller information to callee", if no gap on RCD is found, this KI#4 will not go to normative work.
  "Support of virtual number" can be discussed in normative phase.