## Slide 1
SA6 SID Consolidated consent architecture for Applications (FS_COCOA) for Rel-20
Including alignment with GSMA OPG and CAMARA
Ericsson

## Slide 2: Background: additional info for SA6 SID
S6-251064 [was S6-250561]

## Slide 3: Background Information
Current status of the RO authorization (e.g., user consent) in Rel-19:
Incomplete RO authorization (e.g., user consent) solution in CAPIF Rel-19
Current 3GPP user consent management solution for applications is dependent on CAPIF, but CAPIF is optional
Unclear end-to-end solution for user consent for user data sharing to applications
Misalignment between solution in 3GPP SA6 with GSMA OPG and CAMARA consent approaches
Operators have consent management solutions to address regulation requirements
  no dependency on any specific exposure platform, regardless if they use CAPIF as part of the exposure platform, or not (e.g., CAPIF, GSMA OP, hyperscalers-based, etc.)
This material contains additional background and information for the Rel-20 SA6 SID FS_COCOA (COnsolidated COnsent management architecture for Applications) (S6-251064)

## Slide 4: Problem statement
UE
Different User Consent Management solutions for the application exposure cases
CSP data
CCF
UE
3GPP CAPIF
Without CAPIF
Authorization Function & Consent Management
Apps
Apps
Apps
Browser/ self-care
ROF
1. Gets a redirect URL to CSP consent solution
Consent Management
solution
2. URL
3. Consent management or revocation
Other exposure platforms (e.g., OPG, CAMARA)
Consent Manager
Consent Management
Non-CSP data
CAPIF-8
- 3GPP CAPIF: Consent management is tightly coupled with Authorization Function in CAPIF
Authorization
OP
Apps
Apps
Apps
Some Exposure platform (e.g., hyperscaler, others…)
Authorization

## Slide 5: Proposed approach in FS_COCOA SID
A common User Consent Management solutions for the application exposure cases
CCF
UE
CAPIF
Separate out Consent Management from CAPIF CCF &Authorization Function
One consent architecture, industry reusable
Authorization Function
Apps
Apps
Apps
Browser/ self-care
ROF
Consent Management
Checks consent for apps
Consent management handling (including revocation)
NOTE:
In GSMA OPG the functionality on the client was left to implementations and operators’ choice (browser, client, app, etc)

## Slide 6: Proposed approach
Separate out the Consent management from CAPIF
  consent management solutions existed at operators independent of the Exposure platform used (regardless if e.g., CAPIF-based, GSMA OP, hyperscalers-based, etc)
  no functional dependency for consent management functionality on CAPIF
  user consent and security aspects are different topics (security features can consume Consent management service for e.g., checks, queries as part of authorization procedure)
Handle the user consent architecture aspects holistically
  avoid splitting consent topics between SIDs
Handle narrower, dedicated topics in one SID
  Consent can complete at own pace, independent on the completion level for other topics in CAPIF
Align the User consent solution to the approach and experience defined in GSMA OPG & CAMARA
SA3 can complement with security mechanisms (as previously done in Rel-18, Rel-19) the consent solution architected by SA6

## Slide 7: GSMA OPG.02 Case 1: User opt-in
Notes: OPG.02 Section 4.11.1:
“If there is no associated Consent Record, the OP signals the Consent Manager to start the capture of the Consent from the end user (Step 8). Once the Consent is requested (Step 9), the result of that operation is stored in the Consent Manager (Step 10). If the consent is not granted by the end user (for instance the user does not agree with sharing its information for the signalled Purpose of data processing) the authorization process fails and the access to the personal information resources is denied. If the consent is granted an Authorization Code sent back (Step 11,12) which can be later exchanged for an operator Access Token (Step 13). Upon reception of NBI API call carrying the operator Access Token in Step 14, the OP decrypts the Access Token and forwards the request to receive a response which is sent back.”

## Slide 8: GSMA OPG.02 Case 2: Federated environment

## Slide 9: Overlay SA6 CAPIF Consent architecture on GSMA OPG.02 solution (1)
v
v
Oauth 2.0 Authorization Server
v
RO Authorization Management
Authorization Function
v
No ROF on UE
CAPIF Core Function
In OPG the Consent Mgr is outside the Exposure Platform (OP)
Notes: OPG.02 Section 4.11.1:
“If there is no associated Consent Record, the OP signals the Consent Manager to start the capture of the Consent from the end user (Step 8). Once the Consent is requested (Step 9), the result of that operation is stored in the Consent Manager (Step 10). If the consent is not granted by the end user (for instance the user does not agree with sharing its information for the signalled Purpose of data processing) the authorization process fails and the access to the personal information resources is denied. If the consent is granted an Authorization Code sent back (Step 11,12) which can be later exchanged for an operator Access Token (Step 13). Upon reception of NBI API call carrying the operator Access Token in Step 14, the OP decrypts the Access Token and forwards the request to receive a response which is sent back.”

## Slide 10: Overlay SA6 CAPIF Consent architecture on GSMA OPG.02 solution (2)
v
Oauth 2.0 Authorization Server
v
RO Authorization Management
CCF in CSP domain 1
v
No ROF mandated on UE
Authorization Function
CAPIF Core Function in CSP domain 2
In OPG the Consent Mgr is outside the Exposure Platform (OP)

## Slide 11: CAMARA
https://github.com/camaraproject/IdentityAndConsentManagement/blob/r2.1/documentation/CAMARA-API-access-and-user-consent.md

## Slide 12: CAMARA Scenario 1: Authorization code

## Slide 13: CAPIF Authorization overlay on CAMARA Scenario 1
v
Oauth 2.0 Authorization Server
v
RO Authorization Management
Authorization Function
v
No ROF on UE
CCF in CSP domain
In CAMARA the Consent Master is outside the API Exposure Platform

## Slide 14: CAMARA Scenario 2: CIBA flow (Backend flow)

## Slide 15: CAMARA Scenario 2: CIBA flow (Backend flow)
v
Oauth 2.0 Authorization Server
v
RO Authorization Management
Authorization Function
v
No ROF on UE
CCF in CSP domain
In CAMARA the Consent Master is outside the API Exposure Platform

## Slide 16: CAMARA Scenario 3: Client credentials
https://github.com/camaraproject/IdentityAndConsentManagement/blob/r2.1/documentation/CAMARA-Security-Interoperability.md